## Slide 1: radar flight data Controller Training
Lesson 5: Computer Field Format
Course - 55053
Version 2019-12.1

## Slide 2: Does Everything Look Right to You?
Paris
in the
the Spring
Once
in a
a Lifetime
A
Bird
in the
the Hand

## Slide 3: Objectives
At the completion of this lesson, you will be able to:
Identify computer command structure
Determine the appropriate command field entries

## Slide 4: Computer Commands
Format
Fields
  Elements
    Characters
Aircraft ID Syntax
  La(a)(a)(a)(a)(a)

## Slide 5: Input Command Breakdown
Field
Field
Element
Element
Element
Element
Characters
Characters
Characters
Characters
Characters
Characters
Characters

## Slide 6: Fields, Characters and Elements
H/ /L
B789
UAL866 450
Field 02
Field 03
Field 05
Space
Elements
Space
Characters

## Slide 7: Knowledge Check
For most commands, if the input fields are not in the required order, the command will fail.
  True
  False

## Slide 8: Knowledge Check
Elements are ________.
  smaller units of information within a field
  the sole item in a command
  separated by a space

## Slide 9: Knowledge Check
A field is separated from another field by a ________.
  equal sign
  period
  space

## Slide 10: Command Fields
Field 01
  Message Type
Fields 02 - 11
  Three letter abbreviations
Field Number | Field Abbreviation | Field Content
02 | AID | Aircraft ID
03 | TYP | Type
04 | BCN | Beacon
05 | SPD | Speed
06 | FIX | Fix
07 | TIM | Time
08 | ALT | Altitude
09 | RAL | Requested Altitude
10 | RTE | Route
11 | RMK | Remarks
AM AAL12 05 450
AM AAL12 SPD 450

## Slide 11: Knowledge Check
All commands begin with a ________.
  field abbreviation
  command ID
  space character

## Slide 12: Field 01 Message Type
Element | Format | Example
Command ID | LL | FP
 | Hard-Labeled Function Keys | 
Format Characters | Definition
L | Letter
d | Number
a | Alphanumeric
( ) | Optional

## Slide 13: Field 02 (AID) - Flight Identification (FLID)
Element | Format | Examples
Aircraft ID | La(a)(a)(a)(a)(a) Ld | AF1 SWA1237 VV3C45 N1
Computer Identification (CID) | ddd daa | 128 12A
Beacon Code | dddd | 2014
Slant Character / |  | 
Departure Point (Optional) | aa(a)(a)(a)(/)(a)(a)(a)(a)(a) | AAL112/KSLC A458/4600N/12845W

## Slide 14: Field 03 (TYP) Aircraft Data
 | Element | Format | Examples
Element A | Number of Aircraft | (d) or (d)(d) | 3/F15 or 12/T38
 | Special/Heavy Aircraft Indicator | (L) (d)(L) | H/B747 2H/C17
Element B | Slant Character / |  | 
Element C | Type of Aircraft | La(a)(a) | B2 M20T
Element D | Slant Character / |  | 
Element E | Aircraft Equipment Suffix | (L) | C172/X

## Slide 15: Knowledge Check
Within Field 03, will the system accept ten heavy aircraft (e.g., 10H/C17/L)?
  Yes
  No

## Slide 16: Knowledge Check
The Special Aircraft Indicator (SAI) is found in Field 02.
  True
  False

## Slide 17: Knowledge Check
Select the correct format for a flight of two F15s with aircraft equipment suffix P.
  2-F15/P
  2F15/P
  2/F15/P

## Slide 18: Field 04 (BCN) Beacon Code
Element | Format | Example
Beacon Code | (dddd) | 1426

## Slide 19: Knowledge Check
Which of the following contain all valid Field 02 flight IDs?
  3XGVR, 3214, AF1, AAL3214
  VVAC321, N24TF, 689, 3218
  VVAC321, 3214, CGWRD, 14A
  AAL23114, VM2485, SWA3214

## Slide 20: Field 05 (SPD) Speed
Element | Format | Examples
True Airspeed | (d)(d)dd | 95 095 440
Mach Speed | Lddd | M083
Classified Speed | SC | SC

## Slide 21: Field 06 (FIX) Coordination Fix
Element | Format | Examples
Fix Name | aa(a)(a)(a) | SERVE KSLC
Fix-Radial-Distance | aa(a)(a)(a)dddddd | TINGS310013
Lat/Long | aaaa(a)(a)/aaaa(a)(a) | 3500N/14000W 3405/11824

## Slide 22: Field 07 (TIM) Coordination Time
 | Element | Format | Examples
Element A | Type of Time | L | E = Estimated P = Proposed Departure D = Actual Departure
Element B | Time | dddd XXdd | 1500 XX20

## Slide 23: Knowledge Check
Choose the valid Field 06 format.
  GINGR093089
  IWR18025
  3625N/09875W

## Slide 24: Knowledge Check
Choose the proper Field 07 format for an airborne flight.
  P1548
  E1628
  D2262

## Slide 25: Knowledge Check
What is a key format limitation for Field 04?
  Must be entered in hours + minutes.
  Has a maximum value of 3700.
  Only numbers 0-7 can be used.

## Slide 26: Knowledge Check
What is the proper Field 05 format for MACH .82?
  M82
  M082
  0.82

## Slide 27: Knowledge Check
Which field is the coordination fix?
  03
  05
  06

## Slide 28: Knowledge Check
How is a point indicated in Field 06 for a location that is NOT stored in the computer?
  Screen X/Y coordinates
  Full spelling of town name
  Latitude/longitude coordinates or fix-radial-distance

## Slide 29: Field 08 (ALT) Assigned Altitude
Element | Format | Example
Altitude in Hundreds of Feet | (d)dd | 70
VFR-on-Top | OTP | OTP
VFR-on-Top with Altitude | OTP/(d)dd | OTP/85
Block Altitudes | (d)ddB(d)dd | 190B220
Aircraft Above Specified Altitude | ABV/(d)dd | ABV/600
Assigned Altitude with Different Altitude After Fix | (d)dd/FIX/(d)dd | 140/DSM/160
VFR | VFR | VFR
VFR with Altitude | VFR/(d)dd | VFR/095

## Slide 30: Field 09 (RAL) Requested Altitude
Element | Format | Example
Altitude in Hundreds of Feet | (d)dd | 80
VFR-on-Top | OTP | OTP
VFR-on-Top with Altitude | OTP/(d)dd | OTP/65
Block Altitudes | (d)ddB(d)dd | 100B120
Aircraft Above Specified Altitude | ABV/(d)dd | ABV/600
VFR | VFR | VFR
VFR with Altitude | VFR/(d)dd | VFR/095

## Slide 31: Knowledge Check
What is a correct altitude format for VFR-On-Top at 8,500’?
  OTP/85
  VFR/85
  VOT/085

## Slide 32: Knowledge Check
Any entry made into Field 08 is also valid for Field 09.
  True
  False

## Slide 33: Knowledge Check
How is an assigned altitude of FL290 through FL350 entered in Field 08?
  350B290
  290+350
  290B350

## Slide 34: Knowledge Check
You are entering the altitude into an active flight plan. In which field is this altitude entered?
  Field 05
  Field 08
  Field 09

## Slide 35: Field 10 (RTE) Route
Element | Format | Examples
Fix Name | aa(a)(a)(a) | TUL DANCI KU51E
Fix-Radial-Distance | aa(a)(a)(a)dddddd | AMG180015
Lat/Long | dddd(L)/(d)dddd(L) | 3500S/10200E

## Slide 36: Field 10 (RTE) Route (cont’d)
Element | Format | Examples |  | 
Airway | aa(a)(a)(a)(a)(a)(a) | V16 Q154 |  | J73 T304
Coded Route | aa(a)(a)(a)(a)(a)(a) | IR20 IR143 |  | VR66 AR101
SID/STAR | aa(a)(a)(a)d | BUJ6 VOLLS3 |  | ELVIS1
Element Delimiters | Description |  | Example | 
. | Separates Unlike Elements |  | GRB.J38 | 
.. | Separates Like Elements |  | GRB..EAU | 

## Slide 37: Field 10 (RTE) Route (cont’d)
Element | Meaning
/ | Tailoring/Truncation Indicator
XXX or ??? | Incomplete Route Indicator
> < | Protected Segment Indicator Electronic Readout
) ( | Protected Segment Indicator Flight Strip
✱ | Asterisk or Splat
⨁ | Overcast Symbol

## Slide 38: Field 10 (RTE) Route (cont’d)
Element | Meaning
VFR DVFR | Visual Flight Rules Defense Visual Flight Rules
+ | Plus Sign

## Slide 39: Field 10 (RTE) Route (cont’d)
Element | Format | Examples
Stereo Tag | La(a)(a)(a)(a)(a)(a) | AD2 FOX7
Slant Character / |  | 
Delay Data | /D(d)d+dd | /D10+30
Estimated Time En Route (ETE) | /dddd | /0130
Estimated Time of Arrival (ETA) | /dddd | /1445

## Slide 40: Field 11 (RMK) Remarks and/or ICAO Special Handling (STS)
Element | Format | Example
Interfacility Remarks | 𐰗(Text) | 𐰗FRC
Intrafacility Remarks | ⨁(Text) | ⨁REQ FL210
ICAO Special Handling | ⦶(Text) | ⦶HAZMAT

## Slide 41: Knowledge Check
Which of the following remarks, in its entirety, will NOT be transmitted to another center?
   REQ HIGHER ALT AFTER BNA
  ⨁ REQ FL210 AFTER VHP  ONE VOR INOP
  ⨁ REQ HIGHER ALT AFTER GRR

## Slide 42: Knowledge Check
Format the following route of flight for Field 10:
KSEA V23 V182 ONP T274 CRAAF CVO070040 DSD KBDN
KSEA.V23..V182.ONP.T274.CRAAF..CVO070040.. DSD..KBDN

## Slide 43: Knowledge Check
What is the significance of the “✱” in Field 10?
  Warns of route merge problems
  Indicates additional information in Remarks
  Suppresses ADR, AAR or ADAR

## Slide 44: Knowledge Check
What is the significance of the “/” character in Field 10 when it appears as the second element?
  Expired route is omitted
  Estimated Time En Route follows
  The route contains a SID

## Slide 45: Knowledge Check
When “./.” appears immediately before the destination fix, what does it denote?
  ETA was omitted at departure
  The flight will delay to the destination
  A portion of the route is suppressed on Flight Strips

## Slide 46: Knowledge Check
Which of these fix elements can be filed in Field 10?
  VFR Reporting points, Victor airways, Q Routes
  Adapted fixes, Fix-radial-distance points, Lat./Long. Coordinates
  Jet Routes, Obstructions, Cities

## Slide 47: Knowledge Check
What is the correct order if both the  and  are used in the same command?
   precedes ⨁
  ⨁ precedes 
   + precedes ⨁

## Slide 48: Practice Exercise 1: Computer Field Format
To be completed in this classroom
Your instructor will provide direction

## Slide 49: Practice Exercise 2: Command ID
Completed in the Test and Training Lab (TTL)
You may use notes and references to complete the exercise
Your instructor will provide direction

## Slide 50: Lesson Summary
Fields
  Elements
    Characters