## Slide 1: Radar Flight Data Controller Training
Lesson 6: Computer Command
Composition and Entry
Course 55053
Version 2019-12.1

## Slide 2: Lesson Objectives
At the end of this lesson you will be able to:
Identify Command Composition
Identify Types of System Responses
Determine Eligibility for Command Entry
Determine Flight Data Command Composition
Determine Information Request Command Composition
Determine Miscellaneous Command Composition

## Slide 3: Command Composition Order
03-TYP
C172/G
80
09-RAL
Field
Element
Element
/
P1455
07-TIM
KALB .. GDM . V2 . KBOS
10-RTE
FP
01
N123
02-AID
115
05-SPD
KALB
06-FIX
SPACE
Field
Element
Field
Element
Field
Element
Field
Element
SPACE
SPACE
SPACE
Field
Element
Element
Element
Element
.
.
..
Field
Element
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
Field
Element
Element
Hard-Labeled Key
All commands must begin with a Command ID:
Two (2) letter designator
Hard-labeled function keys

## Slide 4: Message Composition Area (MCA) View
Expanded
View
Accept
Message
Reject
Message
MCA Preview and Feedback Areas

## Slide 5: Command Acceptance Checks
Commands entered by the controller are checked for:
Syntax and Format
Source Legality
Semantics

## Slide 6: Types of System Responses
After entry, the system will respond:
Accept
Reject
Error

## Slide 7: Accept
If input passes all checks, data is displayed on one or more of the following:
MCA Feedback Area
Flight Strip Printer (FSP)
Situation Display

## Slide 8: Reject/Error Message Overview
Display in the MCA Feedback Area.
Error checking stops at the first error.
  Additional errors may be present.
Command is not retained in the Preview Area.
RECALL will display the command in the Preview Area for correction and resubmission.

## Slide 9: Syntax and Format
Command Input Example
FP AAL14238 MD83/L 440 KLEX P0040 320 KL EX..VXV.J43.OTK..KMCO
X REJECT – AAL14238 FLID FORMAT
FLIGHT PLAN
FP AAL14238 MD83/L 440 KLEX P0040 320
KLEX..VXV.J43.OTK..KMCO
Note: Field 02 (AID) must be 2 to 7 characters
Error Message Example

## Slide 10
Syntax and Format Checking
AM TIM 152 P1455
AM 359 SPD 045
AM 204 10 KDFW.ARDIA6.E✱LVR..NNEAL.KIDDZ3
PF N25TK BE55/G 185 KMAF P1005 160 KMAF.BG TOE.BACHR4.KDAL
ILLEGAL CHARACTER
INCORRECT SEQUENCE
PARAMETER OUTSIDE RANGE
INVALID TWO-LETTER COMMAND ID

## Slide 11
GI W30 OD4 NEEDS ASSISTANCE
X REJECT – W30 INCORRECT ROUTING
GEN INFO
GI W30 OD4 NEEDS ASSISTANCE
Syntax and Format Errors
  W30 is an incorrect position
  The letter “O” is incorrect, it should be the clear weather symbol
  The system stops processing at the first error it encounters in the command

## Slide 12: Source Legality Error
The source legality check determines if a position is authorized to enter the command. If not, the system generates a source legality error.
  ILLEGAL SOURCE error message is displayed in the Feedback Area
  Original command is not retained in the Preview Area
CP TMDI 600
X ILLEGAL SOURCE
CP TMDI 600

## Slide 13: Semantic Error
X NO AIRSPACE PENETRATION
FLIGHT PLAN AAL142
FP AAL142 H/B763/L 440 RBL EXX00 330 KSFO./.RBL..FMG.J32.MLD..KMSP
FP AAL142 H/B763/L 440 RBL EXX00 330 KSFO ./.RBL..FMG.J32.MLD..KMSP
Note: Flight does not penetrate sector airspace

## Slide 14: Reject/Error Message Examples
BCN CODE USED BY OTHER AC
NOT YOUR CONTROL
DUPLICATE FIELD REFERENCE
MESSAGE TOO LONG – or – SHORT
(FIX NAME) CANNOT MERGE

## Slide 15: Invalid Field Reference
X RAH INVALID REFERENCE
AMENDMENT
AM N8629N RAH 120
AM N8629N RAH 120
Note: RAH is an invalid field reference.

## Slide 16: Message Too Long
X MESSAGE TOO LONG
DEPARTURE
DM AAL25 0102 270 ○SLOW CLIMBER
DM AAL25 0102 270 ○SLOW CLIMBER
Correct Format: DM FLID (TIM) (ALT)

## Slide 17: Controller Responses to Error Messages
Cancel Entire Command
  CXX cancels the entire command.
Take No Action
  Command will cancel after an adapted number of minutes.
Edit / Correct Command
  Recall the command via the RECALL key.
  Use text-editing capabilities to correct the command.

## Slide 18: Knowledge Check
What will happen if CXX is entered in response to an error?
  Change the time entered to Current Time
  Cancel the command
  Enter .XXX. into Field 10
Notes: ELO-3

## Slide 19: Knowledge Check
A command entry does not have the expected result. You should _______.
  re-enter the command
  have the Radar Controller coordinate
  check the MCA View for ‘Accept’ or ‘Reject’
Notes: ELO-1

## Slide 20: Knowledge Check
When is ILLEGAL SOURCE displayed?
  Flight plan starts from a restricted airport
  Aircraft call sign is on a watch list
  Position is not authorized to enter the command
Notes: ELO-2

## Slide 21: Command Eligibility
Flight Data Commands
  Sector Eligibility Requirements
  Termination of Eligibility
Information Request Commands
  Eligibility not Required

## Slide 22: Knowledge Check
A sector is eligible to enter a command affecting the flight plan database if ________.
  the flight is IFR
  a flight will pass through your facility
  your sector will receive a departure strip
Notes: ELO-2

## Slide 23: Flight Data Command Types
Field | Contents
FP | Flight Plan
SP | Stereo Flight Plan
RS | Remove Strip
DM | Departure Message
HM | Hold Message
AM | Amendment Message

## Slide 24: Flight Plan - FP
FP NKS701 B737/L 1235 450 PBI P1730 370 PBI..ACY ⨁ FRC
09-RAL
370
10-RTE
PBI..ACY
11 – RMK
⨁ FRC
07-TIM
P1730
06-FIX
PBI
03-TYP
B737/L
04–BCN
1235
05-SPD
450
02-AID
NKS701
01-MSG TYP
FP
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
SPACE
(
)
(
)

## Slide 25: Stereo Flight Plan - SP
03–TYP
2/F15/I
05-SPD
dd(d)(d)
02-AID
ROCK1
01-Msg Typ
SP
SP ROCK1 2/F15/I P1730 BASSI
SPACE
SPACE
SPACE
07-TIM
P1730
SPACE
(
)
(
)
08-ALT
or
09-RAL
ddd
SPACE
(
)
11-RMK
⨁ or 𐰗 and text
(
)
SPACE
10-RTE
BASSI
SPACE

## Slide 26: Remove Strip - RS
02-FLID
N1234
01-Msg Typ
RS
SPACE
RS N1234
FLID may be:
AID
CID
BCN

## Slide 27: Remove Strip - RS (cont'd)
√ ACCEPT
REMOVE STRIP
N1234/001
Y
CONFIRM BY ENTERING Y
REMOVE STRIP N1234/001
RS N1234
Example: Accept4

## Slide 28: Remove Strip - RS (cont'd)
YES
X REJECT - NOT CONFIRMED
REMOVE STRIP
RS 001
CONFIRM BY ENTERING Y
REMOVE STRIP N1234/001
RS N1234
Example: Reject4

## Slide 29: Departure Message - DM
07-TIM
2003
08-ALT
VFR
02-FLID
N700PX
01-Msg Typ
DM
(
)
)
(
SPACE
SPACE
SPACE
DM N700PX 2003 VFR

## Slide 30: Hold Message - HM
S P A C E
02-FLID
354
S P A C E
Position(/EFC)
21-Hold Data
HM
01-Msg Typ
S P A C E
N/LT/10NM
310-Holding Instructions
)
(
HM N700PX RDU/1245 N/LT/10NM

## Slide 31: Hold Message Syntax
Action | Syntax | Example
Present Position Hold | HM FLID P | HM AAL236 P
Hold at Fix | HM FLID FIX | HM AAL236 RMG
Hold at Fix with EFC | HM FLID FIX/EFC | HM AAL236 RMG/1234
Present Position Hold with EFC and Hold Instructions | HM FLID P/EFC (Direction/Turns/ Leg Lengths) | HM AAL236 P/1234 NW/LT/20NM
Cancel Hold | HM FLID C | HM AAL236 C

## Slide 32: Amendment Message - AM
SPACE
BCN
Field Ref
SPACE
3442
Amendment Data
S P A C E
02-FLID
112
AM
01-Msg Typ
AM 112 BCN 3442

## Slide 33: Flight Data Field Abbreviations
Field 02 - AID
Field 03 - TYP
Field 04 - BCN
Field 05 - SPD
Field 06 - FIX
Field 07 - TIM
Field 08 - ALT
Field 09 - RAL
Field 10 - RTE
Field 11 - RMK

## Slide 34: Flight Data Fields
---------------------------------------------------------------------------------⨁FRC
KDFW
KDFW.DALL4.OKM.J181.BAYLI.BENKY4.KORD
280
P0435
435
3422
B752/L
FP DAL45
02
AID
03
TYP
04 BCN
05
SPD
06
FIX
07
TIM
09
RAL
10 RTE
11 RMK
01
Message Type
FP

## Slide 35: Field 02 Amendment
SPACE
AID
Field Ref
SPACE
N4TC
Amendment Data
S P A C E
02-FLID
235
AM
01-Msg Typ
AM 235 AID N4TC

## Slide 36: Knowledge Check
Which field(s) are optional in a DM Command?
  07 (TIM) and 09 (RAL)
  08 (ALT)
  07 (TIM) and 08 (ALT)
Notes: ELO-3

## Slide 37: Knowledge Check
Which command requires confirmation?
  Stereo Flight Plan (SP)
  Remove Strips (RS)
  Strip Request (SR)
Notes: ELO-3

## Slide 38: Knowledge Check
AM N404JP 02 N405JP ALT 100
AM N404JP BCN 6624 04
AM N404JP RAL 100
Which of the following AM commands is correct?
Notes: ELO-3

## Slide 39: Route Amendment Special Characters
Special Character(s) | Field 10 Placement | Result
 | After departure fix | Insert or change a departure point
 | Appended to end | New destination
+ + | From the divergent fix until the route converges again or destination | Pending ARTCC adapted preferential route
> < | From the divergent fix until the route converges again or destination | Pending Traffic Flow Management (TFM) protected segment
✱ | Appended to end | Prohibit the system application of adapted routes and new destination
⊕ | Appended to end | Inhibit Equipment Restricted Route (ERR) application and new destination

## Slide 40: Route Amendment
Current Route:
Amendment:
Result:
KATL.KAJIN2.STNGA..MLU..KDFW
AM AAL22 10 MLU..YUYUN.BEREE1.KDFW
KATL.KAJIN2.STNGA..MLU..YUYUN.BEREE1.KDFW
Example 14

## Slide 41: Route Amendment
KORD.JOT.J35.STL..FSM..BRDJE3.KDFW
AM AAL22 10 JOT.J35.KSTL↓
KORD.JOT.J35.KSTL
Example 24
Current Route:
Amendment:
Result:

## Slide 42: Time Element Suffix
Current Route:
Amendment:
Result:
KCEF..VIPER/D1+00..SYR087075..LASER/D0+15..KCEF
AM AAL22 10 VIPER/D1+00..SYR087075..LASER..KCEF/1800
KCEF..VIPER/D1+00..SYR087075..LASER..KCEF/1800
Example 4

## Slide 43: Amend Departure Fix - Active
AM AAL22 10 KBOS↑
KBED..REVSS..BAF..MOBBS..SAGES.V489.COATE..KMMU
KBOS..REVSS..BAF..MOBBS..SAGES.V489.COATE..KMMU
Example 4
Current Route:
Amendment:
Result:

## Slide 44: Amend Departure Fix - Proposal
AM AAL22 06 KHAO 10 KHAO↑
KLUK..JBNCH..GIJ.V526.DEERE..KPWK
KHAO..JBNCH..GIJ.V526.DEERE..KPWK
Example 4
Current Route:
Amendment:
Result:

## Slide 45: Suppressing ADR / AAR / ADAR (Adapted Departure Route / Adapted Arrival Route / Adapted Departure Arrival Route)
Current Route:
Amendment:
Result:
KHOU.STYCK6.DOLEY..FUZ..SPS..HALEN..+HALEN.BOSSS2+.KDEN/0130
AM AAL22 10 KDEN✱/0130
KHOU.STYCK6.DOLEY..FUZ..SPS..HALEN..KDEN✱/0130

## Slide 46: Active Flight Plan - Amend Merged Route Data
Current Route:
Amendment:
Result:
KTLH..SZW..DAWWN..BEORN.HOBTT2.KATL
AM AAL22 06 BEORN 10 BEORN.GNDLF2.KATL
KTLH./.BEORN.GNDLF2.KATL

## Slide 47: 06, 07, 10 Route Amendment
Current Route:
Amendment:
Result:
KSFO./.FMG.J32.CZI..ABR..RWF..KMSP
AM AAL22 06 BAM040023 07 E2345 10 BAM040023..FAR.GEP6.KMSP
KSFO./.BAM040023..FAR.GEP6.KMSP

## Slide 48: Knowledge Check
Given the route above, an amendment that will change the route from over SAV via V37 SSI direct OMN is _______.
AM N45TD 10 SAV.V37.SSI.OMN
AM N45TD 10 SAV.V37.SSI..OMN
AM N45TD 10 SAV..V37..SSI.OMN
KCHS.V437.SAV..KELER..SSI.V3.OMN..KDAB
Notes: ELO-3

## Slide 49: Knowledge Check
Given the route above, an amendment that will change the route from over OCF via V581 DADES V7 KLAL landing KLAL is _______.
KGNV..OCF.V157.LAL..SRQ..KVNC
AM AAL12 10 OCF.V581.DADES.V7..KLAL
AM AAL12 10 OCF.V581.DADES.V7.LAL..KVNC
AM AAL12 10 OCF.V581.DADES.V7.KLAL
Notes: ELO-3

## Slide 50: Route Amendment – “By The Numbers”
Current Route:
Input:
Route Readout:
KMIA./.ORL.J53.CRG..CAE..RDU..CAE..KPOB
1-KMIA.2-/.3-ORL.4-J53.5-CRG..6-CAE..7-RDU..8-CAE..9-KPOB
AM N1234
Result:
KMIA./.ORL.J53.CRG..CAE..KPOB
Field 10 Correction:
5..8

## Slide 51: Field 10 Amendment
1-KISM.2-/.3-GUANO.4-V267.5-CRG.6-V51.7-AMG..8-DBN/D1+30..9-KFTY
KABC.V1.DEF..CDE.V3.LMN..KABC
Data Entry | Results | New Field 10 Data
KISM./.GUANO..AMG..DBN/D1+30..KFTY
Removes elements 4 thru 6
3..7
8
8/D0+30
5.V37.SAV..8
Deletes delay after DBN
Changes delay after DBN from 1+30 to 0+30
Changes route between CRG and DBN
KISM./.GUANO.V267.CRG.V51.AMG..DBN..KFTY
KISM./.GUANO.V267.CRG.V51.AMG..DBN/D0+30..KFTY
KISM..ORL..GUANO.V267.CRG.V37.SAV..DBN..KFTY*/1530
Examples 4

## Slide 52
To be completed in this classroom
Your instructor will provide direction.
Practice Exercise 1:
Route Amendment Correction

## Slide 53: Exercise: Route Amendment Correction
1-KISM..2-ORL..3-GUANO.4-V267.5-CRG.6-V51.7-AMG..8-DBN..9-KFTY
KABC.V1.DEF..CDE.V3.LMN..KABC
Data Entry | Results | New Field 10 Data
KISM..ORL..CRG.V51.AMG.. DBN..KFTY
Deletes elements 3 and 4
2..5
3..9
5.V51.AMG..9
5..AYS..7
5/D1+00
Deletes elements 4 thru 8
Changes route between CRG and KFTY
Changes element 6
Adds delay to element 5
KISM..ORL..GUANO..KFTY
KISM..ORL..GUANO.V267.CRG.V51.AMG..KFTY
KISM..ORL..GUANO.V267.CRG..AYS..AMG..DBN..KFTY
KISM..ORL..GUANO.V267.CRG/D1+00.V51.AMG..DBN..KFTY

## Slide 54: Exercise: Route Amendment Correction
1-KISM..2-ORL..3-GUANO.4-V267.5-CRG.6-V51.7-AMG..8-DBN..9-KFTY
KABC.V1.DEF..CDE.V3.LMN..KABC
Data Entry | Results | New Field 10 Data
KISM..ORL..GUANO.V267.CRG.V51.AMG..DBN..KFTY/1430
Adds ETA to KFTY
9/1430
KMLB
8..KPDK
9*/1530
Revises departure point
Revises destination
Inhibits AAR, revises ETA
KMLB..ORL..GUANO.V267.CRG.V51.AMG..DBN..KFTY
KISM..ORL..GUANO.V267.CRG.V51.AMG..DBN..KPDK
KISM..ORL..GUANO.V267.CRG.V51.AMG..DBN..KFTY*/1530

## Slide 55
To be completed in this classroom
Your instructor will provide direction.
Practice Exercise 2:
Route Amendment Correction

## Slide 56: Field 11 Amendment
SPACE
RMK
Field Ref
SPACE
○TCAS EQUIPPED
Amendment Data
S P A C E
02-FLID
235
AM
01-Msg Typ
AM 235 RMK ○TCAS EQUIPPED

## Slide 57: Information Request Commands
Field | Contents
AR or QD | Altimeter Request
WR | Weather Request
SR | Strip Request
FR | Flight Plan Readout

## Slide 58: Altimeter Request - AR
SPACE
01
AR
LOCID
SDF
…
SPACE
aaa
LOCID
(
)
Additional
SPACE
aaa
LOCID
(
)
AR SDF CRW HTS JKL

## Slide 59: Altimeter Request - QD
SPACE
01
QD
LOCID
PDX
…
SPACE
aaa
LOCID
(
)
Additional
SPACE
aaa
LOCID
(
)
QD PDX HIO UAO SLE CVO EUG

## Slide 60: Weather Request - WR
SPACE
01
WR
LOCID
BOS
SPACE
aaa
LOCID
(
)
Additional
SPACE
aaa
LOCID
(
)
WR BOS

## Slide 61: Knowledge Check
What is the command to print the weather at the following airports: CNM ELP FST?
  WR CNM ELP FST P
  WR CNM ELP FST D
  WR CNM ELP FST
Notes: ELO-5

## Slide 62: Strip Request - SR
SPACE
01
SR
02-FLID
178
SPACE
BNAT
16 - Output Routing
SPACE
BNA
13 - LOCID
SR 178 BNA BNAT

## Slide 63: Strip Request - SR (cont’d)
SPACE
01
SR
02-FLID
178
SPACE
38
16 - Output Routing
SPACE
/T
551 - Scope
SR 178 /T 38

## Slide 64: Strip Request - SR
SR AAL1292 /T 01
SR 234 /A 36
SR AAL1292 /A04 38
Most relevant strip
All strips for another local sector
All strips for requesting sector
Examples 4

## Slide 65: Flight Plan Readout - FR
SPACE
01
FR
02-FLID
UAL72
SPACE
P
Out. Rte.
(
)
SPACE
C
ICAO Flight Data
(
)
Note: Field 16 can only be the letter P (Printer)
Note: Field 42 can be a C,F,I,1,2 or A. Each returns a slightly different version of the ICAO data.
FR UAL72 C P

## Slide 66: ICAO Flight Plan Readout (Printer)
FR HAL11 P
Start of ICAO FP

## Slide 67: ICAO Flight Plan Readout (Response Area)
FR HAL11 I
A 525 HAL11 FLR I FLT S HAK H EQP SDESFGHIJ2J3J4JSH1PZRHXYZ SRV LB2D1 ALA PHOG 0TH ++PBN/ A1B1C1D1L1O1S1 DAT/ 1FANSP2PDC SUR/ 260=RSP180 DOF/ 180726 REG/ N393HA EET/ KZAK0035 PHZH0413 SEL/ ASHM CODE/ A48E9E OPR/ HAWAIIAN AIRLINES PER/ C RALT/ KSFO PHNL RACE/ BAART /M081F400++ RNV D1A1EFR HAL11 I
Start of ICAO FP

## Slide 68: Knowledge Check
Select the correct command to readout ICAO information.
  FR I DAL55
  FR ICAO AAL20
  FR UAL35 I
Notes: ELO-4

## Slide 69: Knowledge Check
Which is the correct command to print a Domestic Flight Plan?
  FR 3501 D
  FR 3507 P
  FR 3509 P

## Slide 70: Miscellaneous Commands
Field | Contents
GI | General Information Command
RF | Request Flight Plan Transfer
WX | Weather Input
AS | Altimeter Setting Input

## Slide 71: General Information - GI
SPACE
01
GI
Output Routing
03
…
SPACE
31
Out. Rte.
(
)
Up to 47 additional
SPACE
General Info
𐰗SECTOR 12 CLOSED
GI 03 31 ○SECTOR 12 CLOSED

## Slide 72: General Information Syntax
Field 01 | Field 16 | Field 11 | Result
GI | aaaT | ○Free Text | Sent to named tower, e.g., ORDT
GI | aaaA | ○Free Text | Sent to named approach control arrival position
GI | C | ○Free Text | Sent to all active sector FSPs and AT Specialist Workstations in the center.
GI | aaaO | ○Free Text | Sent to named approach control overflight position
GI | aaaD | ○Free Text | Sent to named approach control departure position
GI | dd (dd) | ○Free Text | Sent to sector number (up to 48 sectors/positions)

## Slide 73: Request Flight Plan Transfer - RF
SPACE
SPACE
01
RF
02-FLID
322
Facility
PCT
RF 322 PCT
Note: The RF command is used to transfer flight data to a neighboring facility (ARTS/STARS, CAATS, ATOP, etc.)

## Slide 74: Weather Input - WX
SPACE
SPACE
01
WX
WX PKB 1155 ○17007KT 10SM CLR 17/03 A3002
LOCID
PKB
Weather Data
𐰗17007KT 10SM CLR 17/03 A3002
Time
1155
SPACE

## Slide 75: Altimeter Setting Input - AS
AS 1155 PKB 992
SPACE
SPACE
01
AS
LOCID
PKB
Time
1155
SPACE
Additional
SPACE
aaa
LOCID
(
)
Altim.
992
SPACE
Altim.
ddd

## Slide 76: Knowledge Check
Which is not a characteristic of a GI command?
  May begin with clear or overcast weather symbol
  Sends plain language command to specified address
  May be sent to up as many as 48 destinations
Notes: ELO-3

## Slide 77: Knowledge Check
What is the purpose of an RF command?
  Transfers flight data to a neighbor facility
  Specify a Radio Frequency for a sector
  Force a flight plan to another facility’s situation display or view
  Prevent an Unsuccessful Transmission Message (UTM) to a facility
Notes: ELO-3

## Slide 78: Knowledge Check
What is the purpose of a WX command?
  Requests weather observation data for an adapted station
  Enters weather observation data for an adapted reporting station
  Requests weather observation data for a non-adapted reporting station
  Enters weather observation data for a non-adapted reporting station
Notes: ELO-3

## Slide 79: Knowledge Check
Which of the following is a correct AS command format?
  AS PSB 998 1215
  AS 998 PSB 1215
  AS 1215 998 PSB
  AS 1215 PSB 998
Notes: ELO-3

## Slide 80
Completed in the Test and Training Lab (TTL)
Exercise to practice the steps for:
  Command Composition and Entry
You may use notes and references to complete the exercise
Your instructor will provide direction
Practice Exercise 3

## Slide 81
Completed in the Test and Training Lab (TTL)
Exercise to practice the steps for:
  Entering Miscellaneous and Information Request Commands
You may use notes and references to complete the exercise
Your instructor will provide direction
Practice Exercise 4

## Slide 82: Lesson Summary
This lesson covered:
Command Composition
Types of System Responses
Eligibility for Command Entry
Flight Data Command Composition
Information Request Command Composition
Miscellaneous Command Composition

## Slide 83
THE END