## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify:
Phraseology for ATC communications
Communications procedures

## Slide 3: International Civil Aviation Organization (ICAO) Phonetics
ICAO phonetics are used for the pronunciation of numbers and letters
  Clarifies individual letters
  Prevents misunderstanding

## Slide 4: Serial Numbers
Number | Stated
11,295 | "ONE ONE TWO NINER FIFE"
20,069 | "TWO ZERO ZERO SIX NINER"

## Slide 5: Altitudes or Flight Levels
Number | Stated
10,000 | "ONE ZERO THOUSAND“ or, restated for clarity: “TEN THOUSAND”
17,900 | "ONE SEVEN THOUSAND NINER HUNDRED“ or, restated for clarity: “SEVENTEEN THOUSAND NINER HUNDRED”
Flight Level | Stated
180 | "FLIGHT LEVEL ONE EIGHT ZERO"
290 | "FLIGHT LEVEL TWO NINER ZERO"

## Slide 6: MDA/DH Altitudes
Number | Stated
1,320 | "MINIMUM DESCENT ALTITUDE, ONE TREE TWO ZERO"
386 | "DECISION HEIGHT, TREE EIGHT SIX"

## Slide 7: Time
Time (12 Hour) | Time (24 Hour) | Stated
1:15 a.m. | 0115 | “ZERO ONE ONE FIFE”
1:15 p.m. | 1315 | “ONE TREE ONE FIFE”
Time | Stated
2230 UTC | “TWO TWO TREE ZERO ZULU”
4:30 p.m. | “ONE SIX TREE ZERO LOCAL”
6:30 p.m. | “ONE EIGHT TREE ZERO PACIFIC”
11:02:15 | “ONE ONE ZERO TWO AND ONE QUARTER”
22:03:27 | “TWO TWO ZERO TREE AND ONE HALF”

## Slide 8: Knowledge Check
What is the phraseology for stating an altitude?
  “NINE THOUSAND FEET”
  “NINER THOUSAND”
  “NINER THOUSAND FEET”

## Slide 9: Practice Exercise 1: ATC Times
Purpose
  Review appropriate pronounciation of times in ATC communications
Materials
  Practice exercise 1: ATC Times
  Pen or pencil
Directions
  Convert the 12 hour time into 24 hour time. Write the 24 hour time and the pronunciation in the spaces provided.

## Slide 10: Practice Exercise 1
Time
Time
(24 Hour)
Stated: (ZULU or LOCAL as appropriate)
2:30 a.m.
0230
“ZERO TWO TREE ZERO LOCAL”
2058 UTC
2058
“TWO ZERO FIFE EIGHT ZULU”
6:25 a.m.
0625
“ZERO SIX TWO FIFE LOCAL”
11:30 p.m.
2330
“TWO TREE
TREE
ZERO LOCAL”
3:59 UTC
0359
“ZERO TREE FIFE NINER ZULU”
10:11 p.m.
2211
“TWO
TWO
ONE
ONE LOCAL”
7:12 a.m.
0712
“ZERO SEVEN ONE TWO LOCAL”
2136 UTC
2136
“TWO ONE TREE
SIX ZULU”

## Slide 11: Field Elevation
Elevation | Stated
17 feet | "FIELD ELEVATION, ONE SEVEN"
817 feet | "FIELD ELEVATION, EIGHT ONE SEVEN"
2,817 feet | "FIELD ELEVATION, TWO EIGHT ONE SEVEN"

## Slide 12: Altimeter Setting
Setting | Stated
29.92 | "ALTIMETER, TWO NINER NINER TWO"
30.01 | "ALTIMETER, TREE ZERO ZERO ONE"

## Slide 13: Knowledge Check
What is the phraseology for stating an altimeter?
  “ALTIMETER TWENTY NINE NINETY TWO”
  “ALTIMETER TWO NINER POINT NINER TWO”
  “ALTIMETER TWO NINER NINER TWO”

## Slide 14: Practice Exercise 2: Numbers Phraseology, Part 1
Purpose
  Review pronunciation of numbers in ATC communications
Materials
  Practice exercise 2: Numbers Phraseology, Part 1
  Pen or pencil
Directions
  Write the pronunciation for each group of numbers in the spaces provided

## Slide 15: Practice Exercise 2
Number | Pronounced
Altitude, 13,000 feet | 
Altitude, 19,000 feet | 
Altimeter, 29.92 | 
UTC Time, 2235 | 
Field Elevation, 166 | 
“ONE TREE THOUSAND”
“FLIGHT LEVEL ONE NINER ZERO”
“ALTIMETER TWO NINER NINER TWO”
“TWO TWO TREE FIFE ZULU”
“FIELD ELEVATION ONE SIX SIX”

## Slide 16: Surface Wind
Surface Wind | Stated
03025 | "WIND, ZERO TREE ZERO AT TWO FIFE"
27015G35 | "WIND, TWO SEVEN ZERO AT ONE FIFE GUSTS TREE FIFE"

## Slide 17: Heading
5 degrees
30 degrees
360 degrees
“Heading zero zero fiFe”
“Heading zero tree zero”
“Heading tree six zero”
Heading
Stated

## Slide 18: Beacon Code
Beacon Code | Stated
1000 | "ONE ZERO ZERO ZERO"
2100 | "TWO ONE ZERO ZERO"
1622 | "ONE SIX TWO TWO"

## Slide 19: Runways

## Slide 20: Frequencies
126.55
369.0
121.5
253.0
135.275
302 kHz
“One two six point fiFe fiFe”
“Tree six niner point zero”
“One two one point fiFe”
“Two FIFE tree point zero”
“One tree fiFe point two seven”
“Tree zero two kiloHertz”
Frequency
Stated

## Slide 21: Frequencies (Cont’d)
Channel | Stated
12 | “LOCAL CHANNEL ONE TWO”
103 | “TACAN CHANNEL ONE ZERO TREE”

## Slide 22: Speed and Mach Number
Speed | Stated
250 | "TWO FIFE ZERO KNOTS"
190 | "ONE NINER ZERO KNOTS”
Mach | Stated
1.5 | "MACH ONE POINT FIFE"
0.66 | "MACH POINT SIX SIX"
0.7 | "MACH POINT SEVEN"

## Slide 23: Miles
Mileage | Stated
30 | "TREE ZERO MILES"
55 | “FIFE FIFE MILES"
108 | "ONE ZERO EIGHT MILES"

## Slide 24: Knowledge Check
What is the phraseology for stating the frequency 116.225?
  “ONE SIXTEEN POINT TWO TWENTY FIFE”
  “ONE ONE SIX POINT TWO TWO FIFE”
  “ONE ONE SIX POINT TWO TWO”

## Slide 25: Practice Exercise 3: Numbers Phraseology, Part 2
Purpose
  Review pronunciation of numbers in ATC communications
Materials
  Practice exercise 3: Numbers Phraseology, Part 2
  Pen or pencil
Directions
  Write the pronunciation for each group of numbers in the spaces provided

## Slide 26: Practice Exercise 3
Number
Pronounced
Speed, 250
"TWO FIFE ZERO KNOTS"
Frequency, 126.1
"ONE TWO SIX POINT ONE"
Miles, 30
"TREE ZERO MILES"
Runway, 15
"RUNWAY ONE FIFE"
Heading, 30 (degrees)
"HEADING ZERO TREE ZERO"
Wind, 50 (degrees) 20 (knots)
"WIND ZERO FIFE ZERO AT TWO
ZERO"
Code, 1200
"ONE TWO ZERO ZERO"
Mach, 0.9
"MACH POINT NINER"
Frequency, 123.255
"ONE TWO TREE POINT TWO FIFE"
Runway, 31C
"RUNWAY TREE ONE CENTER"
Wind, 200 (degrees) 10 (knots)
"WIND TWO ZERO ZERO AT ONE
ZERO"

## Slide 27: Facility Identification
“Oakland Center”
“Anchorage Radio”
“Boston Tower”
“Tampa Approach”
“CORPUS CHRISTI G-C-A”

## Slide 28: Knowledge Check
How does a pilot identify an airport traffic control tower?
  State the name of the facility followed by the word “AIRPORT”
  State the name of the facility followed by the word “TOWER”
  State the word “TOWER” followed by the facility name

## Slide 29: Knowledge Check
QUESTION
How is Oakland, California ARTCC identified?
  “Oakland Center”
  “OAKLAND RADIO”
  “OAKLAND APPROACH”

## Slide 30: Aircraft Identification - Civil
Civil identification examples
  U.S. Aircraft Registry
    “November One TREE two SIX”
  Aircraft Model
    “Skylane One TREE Two SIX”
  Aircraft Manufacturer
    “cessna one TREE two SIX”

## Slide 31: Aircraft Identification - Air Carrier
Group form examples:
  AAL52 - “AMERICAN FIFTY-TWO”
  DAL100 - “DELTA ONE HUNDRED”
  UAL75 - “UNITED SEVENTY-FIFE”
If confusion exists, pronounce digits one at a time for clarity
  SWA570 - “SOUTHWEST FIFE SEVEN ZERO”

## Slide 32: Aircraft Identification - Air Taxi
Air taxi identification examples:
  TN15Q
    “TANGO MOONEY ONE FIFE QUEBEC”
  TN31H
    “TANGO NOVEMBER TREE ONE HOTEL”

## Slide 33: Aircraft Identification - Air Ambulance
Air Carrier and Air Taxi examples:
  “MEDEVAC” in the flight plan remarks
    DAL51 - “MEDEVAC DELTA FIFTY-ONE”
    TN612 - “MEDEVAC TANGO NOVEMBER SIX ONE TWO”
General Aviation example:
    LN3BH - “MEDEVAC TREE BRAVO HOTEL”

## Slide 34: Restate Call Sign for Clarity
Examples
  AAL52 - “AMERICAN FIFTY-TWO AMERICAN”
  ASA52 - “ALASKA FIFTY-TWO ALASKA”

## Slide 35: U.S. Military Prefixes
Prefix | Service | Example
A | Air Force | A35562
C | Coast Guard | C12577
G | Air/Army National Guard | G56472
R | Army | R33617
VM | Marine | VM56734
VV | Navy | VV32756

## Slide 36: Special Operations Prefixes
Prefix | Mission/Special Operation | Example
E | Air Evac (Air Evacuation) | E50213
RCH | AMC (Air Mobility Command) | RCH276
S | SAM (Special Air Mission) | S29000
L | Logair (USAF Contract) | L65324
Service prefix | Example: “COAST GUARD RESCUE” | C7233

## Slide 37: U.S. Military Tactical and Training
Examples:
  PINON63 - “Pinyon six tree”
  Skyblt11 - “skybolt one one”
  Roper61 - “roper six one”
  VVAB10 - “NAVY ALPHA BRAVO ONE ZERO”

## Slide 38: Presidential Aircraft Identification
Office | Military | Civil
President | "(Military service) ONE" Examples: "AIR FORCE ONE", "MARINE ONE" | "EXECUTIVE ONE"
President's Family | "EXECUTIVE ONE FOXTROT" | "EXECUTIVE ONE FOXTROT"
Vice President | “(Military service) TWO" Examples: "AIR FORCE TWO", "MARINE TWO" | "EXECUTIVE TWO"
Vice President's Family | "EXECUTIVE TWO FOXTROT" | "EXECUTIVE TWO FOXTROT"

## Slide 39: DOT and FAA Flights
Official | Identifier | Call Sign
Secretary of Transportation | DOT-1 | "TRANSPORT ONE"
Deputy Secretary of Transportation | DOT-2 | "TRANSPORT TWO"
Administrator, Federal Aviation Administration | FAA-1 | "SAFEAIR ONE"
Deputy Administrator, Federal Aviation Administration | FAA-2 | "SAFEAIR TWO"

## Slide 40: Other Special Flights
Special Flight | Call Sign
Flight Check | "FLIGHT CHECK"
Air Force Aerial Sampling Mission | "SAMP"

## Slide 41: Foreign Registry
Civil:
  State aircraft type or manufacturers name followed by letters/digits of aircraft registration, or
  Letters/digits of aircraft registration or call sign
Air Carrier:
  State ICAO 3LD telephony of operating company followed by letters/digits of registration or call sign, or
  The flight number in group form
Military:
  Name of the country and military service followed by separate digits/letters of registration or call sign

## Slide 42: Foreign Registry (Cont’d)
Foreign aircraft registry beginning with a number
  Current En Route automation will not process an aircraft identification that begins with a number
    Amend an aircraft ID containing six or fewer characters by inserting the letter “Q” as the first character of the aircraft ID
    An aircraft ID that contains seven characters is amended by replacing the first character with the letter “Q”
This procedure does not apply to Advanced Technologies and Oceanic Procedures (ATOP)

## Slide 43: Knowledge Check
What is the prefix for a domestic general aviation aircraft?
  “TANGO”
  “KILO”
  “NOVEMBER”

## Slide 44: Knowledge Check
What is the phraseology for AAL52?
  “AMERICAN FIFTY-TWO”
  “52 AMERICAN”
  “AMERICAN FIFTY”

## Slide 45: Knowledge Check
What is the prefix for a civilian airborne ambulance flight?
  “LIFEFLIGHT”
  “LIFEGUARD”
  “MEDEVAC”

## Slide 46: Knowledge Check
What are the letter prefixes for the following military services: Air Force, Army, and Navy?
  AF, RM, and VM
  AF, AR and VV
  A, R and VV

## Slide 47: Knowledge Check
What is the call sign for the Administrator of the FAA?
  “ADMINISTRATOR ONE”
  “FAA ONE”
  “SAFEAIR ONE”

## Slide 48: Words and Phrases
Controllers and pilots need to speak the same language
Use the words or phrases in radio and interphone communications contained in the Pilot/Controller Glossary

## Slide 49: Emphasis for Clarity
Emphasize digits, letters or similar sounding words to aid in distinguishing similar sounding call signs
  Notify each pilot concerned when in communications with aircraft having similar sounding call signs
  Notify the operations supervisor/CIC of any duplicate flight identification numbers or phonetically similar-sounding call signs when the aircraft are operating simultaneously within the same sector

## Slide 50: Monitoring Requirements
Monitor interphones and assigned radio frequencies continuously
Maintain adequate volume to hear all calls

## Slide 51: Pilot Acknowledgement
Ensure acknowledgement from the pilot for all clearances or instructions issued
If no acknowledgement is received, attempt to re-establish contact

## Slide 52: Authorized Interruptions
  As necessary, a pilot may be authorized by ATC to interrupt the communications guard
    A time limit for the pilot to be off frequency should be issued by the controller
    The pilot should inform the controller of the frequency that will be monitored
    The controller should instruct the pilot to report back on the sector frequency

## Slide 53: Authorized Transmissions
Transmit only those messages:
  Necessary for air traffic control
  That contribute to air safety

## Slide 54: False or Deceptive Communications
Take action to prevent, and report false, deceptive, or phantom controller communications
  Correct false information
  Broadcast an alert
  Collect pertinent information regarding the incident
Notify supervisor/CIC

## Slide 55: Authorized Relays
“DELTA TREE SIXTY CONTACT YOUR COMPANY FOR A MESSAGE.”
“DELTA TREE SIXTY, WILCO.”

## Slide 56: Radio Message Format
“DELTA TWO TWENTY-TWO, MEMPHIS CENTER, THE MEMPHIS ALTIMETER TWO NINER NINER SEVEN.”
“MEMPHIS CENTER, DELTA TWO TWENTY-TWO, LEVEL AT ONE SEVEN THOUSAND.”

## Slide 57: Abbreviated Transmissions
“NOVEMBER TWO TREE TANGO…”
N7823T
N6723T

## Slide 58: Knowledge Check
When may a pilot interrupt their communication guard?
  When at cruise altitude
  When authorized by ATC
  Only in two pilot aircraft

## Slide 59: Interphone Priorities
First priority
  Emergency messages
Second priority
  Clearances and control instructions
Third priority
  Movement and control messages
Fourth priority
  Movement messages on VFR aircraft

## Slide 60: Priority Interruption
To interrupt a lower priority message when you have an emergency or control message to transmit, use the words:
  EMERGENCY
  Example: “BREAK FOR EMERGENCY”
  CONTROL
  Example: “BREAK FOR CONTROL”

## Slide 61: Interphone Message Format
“SECTOR FORTY-TWO, TULSA LOW POINT OUT.”
“ONE TWO MILES NORTHWEST OF BARTLESVILLE, CODE TWO TWO SIX ONE AT SEVEN THOUSAND DIRECT FORT SMITH.”
“SECTOR FORTY-TWO, GO AHEAD.”
“F.X.”
“CODE TWO TWO SIX ONE, POINT OUT APPROVED, G.T.”

## Slide 62: Loss of Communications
  Loss of communications for more than 5 minutes requires notification to the supervisor/CIC
  Note the time of last communication
  Inform the Supervisor what steps have been taken to reestablish communications with the aircraft

## Slide 63: Knowledge Check
If a pilot does not acknowledge your clearance, and your attempts to reestablish communications are not successful, what action must you take?
  Consider that the clearance was not issued
  Advise the supervisor/CIC
  Relay the clearance through other aircraft

## Slide 64: Good Communication Skills
Confirm message understood
Relay critical info
Speak up when needed
Give specific info
Talk to each other
Careful stripmarking
Speak…
Explicitly! Specifically!
Clearly! Slowly!

## Slide 65: Barriers to Communication
Use of non-standard phraseology
Using complicated or unfamiliar terms
Lack of attention, interest, or distractions
Differences in perception and viewpoint
Interpersonal barriers

## Slide 66: Controller Responsibilities In Communication
Speaking
Listening
Professional attitude
Assertive communication
Appropriate communication for the type of pilot

## Slide 67: Practice Exercise 4: Communications Skills
Purpose
  Identify and understand common barriers to communication
Materials
  Practice exercise 4: Communication Skills
  Pen or pencil
Directions
  Listen to the audio files and write down the strengths and weaknesses of each controller’s communications

## Slide 68: Practice Exercise 4: Communications Skills
This exercise contains seven audio recordings of controller communication
Listen to the situations and write down your impression of each
Situation 1
Situation 2
Situation 3
Situation 4
Situation 5
Situation 6
Situation 7

## Slide 69: Practice Exercise 5: Listening for Readback Errors
Purpose
  Identify readback errors in ATC communications
Materials
  Practice exercise 5: Listening for Readback Errors
  Pen or pencil
Directions
  Listen to the audio files and write down any readback errors

## Slide 70: Practice Exercise 5: Listening For Readback Errors
This exercise contains eight audio recordings of situations in which clearances are issued
Listen for the readback errors and write them down
Clearance 1
Clearance 2
Clearance 1 corrected
Clearance 2 corrected

## Slide 71: Practice Exercise 5: Listening For Readback Errors (Cont’d)
This exercise contains eight audio recordings of situations in which clearances are issued
Listen for the readback errors and write them down
Clearance 3
Clearance 4
Clearance 3 corrected
Clearance 4 corrected

## Slide 72: Practice Exercise 5: Listening For Readback Errors
This exercise contains eight audio recordings of situations in which clearances are issued
Listen for the readback errors and write them down
Clearance 5
Clearance 6
Clearance 5 corrected
Clearance 6 corrected

## Slide 73: Practice Exercise 5: Listening For Readback Errors
This exercise contains eight audio recordings of situations in which clearances are issued
Listen for the readback errors and write them down
Clearance 7
Clearance 8
Clearance 7 corrected
Clearance 8 corrected

## Slide 74: Lesson Summary
This lesson covered:
Phraseology for communicating
Communications procedures

## Slide 75: The End