## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify:
Duty priority
Expeditious compliance
Operational priorities
Requirements for reporting essential information
General control procedures

## Slide 3: ATC Service
Prevent Collisions
Safe
Orderly
Expeditious

## Slide 4: ATC Service (Cont’d)
Provide Additional Services
  Not optional
Services may be precluded by:
  Volume of traffic
  Frequency congestion
  Quality of surveillance
  Controller workload
  Higher priority duties
  Physical inability to scan and detect situations falling in this category

## Slide 5: ATC Service (Cont’d)
Control in accordance with JO 7110.65
  Unless a deviation to conform with:
    ICAO Documents
    National Rules of the Air
    Special agreements where the U.S. provides air traffic control outside the U.S. and its possessions
  Other procedures/minima prescribed LOA, FAA directive, or a military document
  A deviation is necessary to assist an aircraft when an emergency has been declared

## Slide 6: Duty Priority
Separate aircraft and issue safety alerts
Support national security and homeland defense activities
Provide and/or solicit weather information
Provide additional services

## Slide 7: Procedural Preference
Use automation procedures in preference to non-automation procedures
Use radar separation in preference to nonradar separation when it will provide an operational advantage
Use nonradar separation in preference to radar separation when an operational advantage will be gained

## Slide 8: Knowledge Check
Nonradar separation cannot be used within a radar environment.
  True
  False

## Slide 9: Knowledge Check
What is the first duty priority of an air traffic controller?
  Solicit weather information
  Separating aircraft and issuing safety alerts
  Support to national security
  Provide additional services

## Slide 10: Expeditious Compliance Terms
Use the word “IMMEDIATELY” to avoid an imminent situation
  Include the reason if time permits
Use the word “EXPEDITE” for prompt action to avoid the development of an imminent situation
  Include the reason if time permits

## Slide 11: Safety Alerts
Issue a safety alert if you are aware of an aircraft at position or altitude which places it in unsafe proximity to:
  Terrain
  Obstruction
  Another aircraft
Do NOT assume another controller has acted to correct the unsafe situation
  Inform the controller responsible for issuing the safety alert

## Slide 12: Knowledge Check
Which statement is correct about safety alerts?
  Safety alerts are a pilot’s responsibility
  Safety alerts have equal priority with separation
  Safety alerts are advisory in nature

## Slide 13: Knowledge Check
What term is used to specify prompt action in a clearance?
  Expedite
  Immediately
  Promptly

## Slide 14: Knowledge Check
Which of the following has the highest priority?
  Relaying control information
  Issuing a safety alert to a VFR aircraft
  Providing airport weather information

## Slide 15: Operational Priority
Aircraft in distress have the right of way
Provide air traffic on a “first-come, first-served” basis, except:
  Air ambulance flights
    Provide priority handling when the pilot verbally identifies the flight by stating MEDEVAC
  When verbally requested, provide priority handling to AIR EVAC, HOSP, and scheduled air carrier/air taxi flights
  Presidential or Vice Presidential aircraft and any escort aircraft

## Slide 16: Operational Priority (Cont’d)
  Search and Rescue (SAR) aircraft while performing a SAR mission
  Interceptor aircraft on active air defense missions
  NIGHT WATCH aircraft
  FLYNET (Flights, Nuclear Emergency Teams)
  GARDEN PLOT
  SAMP (Atmospheric Sampling for Nuclear Contamination)
  Special Air Mission aircraft “SCOOT”
  TEAL and NOAA

## Slide 17: Operational Priority (Cont’d)
  OPEN SKIES observation and demonstration flights
  Flight Check aircraft
  IFR aircraft over SVFR
  North American Route Program (NRP) are not subject to route limiting restrictions
  Diverted Flights
  FALLEN HERO flights

## Slide 18: Knowledge Check
Which of the following has the highest priority?
  Aircraft in distress
  FLYNET Nuclear Emergency Teams
  OPEN SKIES Aircraft
  NIGHT WATCH National Airborne Operations

## Slide 19: Knowledge Check
When is an AIR EVAC flight provided priority handling?
  When requested by the pilot
  When carrying patients as indicated in remarks
  Always

## Slide 20: Knowledge Check
What is the operational priority for providing air traffic control services?
  Arriving aircraft over departing aircraft
  SVFR aircraft over IFR aircraft
  First-come, first-served

## Slide 21: Knowledge Check
Which of the following normally would NOT receive priority handling?
  Turbojet arrival
  FLYNET mission
  Flight Check mission

## Slide 22: Reporting Essential Flight Information
Report, information concerning components of the NAS or flight conditions that may adversely affect air safety to the appropriate:
  FSS
  Airport manager’s office
  ARTCC
  Approach control facility
  Operations office
  Military office

## Slide 23: NAVAID Malfunctions
When an aircraft reports a NAVAID malfunction, request a report from another aircraft
  If second aircraft reports normal:
    Continue use
    Inform pilot making malfunction report
    Inform your supervisor/CIC

## Slide 24: NAVAID Malfunctions (Cont’d)
If second aircraft confirms malfunction, or if unable to get a second report:
  Request monitor facility to activate standby equipment
If normal operation is reported after going to standby equipment:
  Continue use of NAVAID
  Inform your supervisor/CIC

## Slide 25: GPS or WAAS Anomaly
Record the following:
  Aircraft make, model, and callsign
  Location or position, and altitude
  Date/time of occurrence
Request a report from a second aircraft
Inform your supervisor/CIC
Inform other aircraft of the anomaly

## Slide 26: Supervisory and Pilot Notification
Ensure supervisor/CIC is aware of conditions affecting sector operations, including:
  Weather
  Equipment status
  Potential sector overload
  Emergency situations
  Special flights/operations
  Possible suspicious aircraft/pilot activity

## Slide 27: Blue Lightning Events
Reports of possible human trafficking
  Ensure that the supervisor/CIC is notified

## Slide 28: Pilot Deviation Notification
When it appears that the actions of a pilot constitute a pilot deviation notify the pilot, workload permitting
    (Identification) POSSIBLE PILOT DEVIATION ADVISE YOU CONTACT (facility) AT (telephone number)

## Slide 29: Knowledge Check
A pilot reports not receiving a NAVAID signal. What is your next action?
  Immediately activate the standby system
  Request a report from another aircraft
  Log the report on FAA form 7230-4

## Slide 30: Formation Flights
Control formation flights as a single aircraft
  Issue control instructions to formation leader
  Ensure flight plan data accurately reflects the number of aircraft

## Slide 31: Coordinate Use of Airspace
MLU
APCH
Your
Sector
Coordinate before you control in or aircraft enters another’s jurisdiction
Before issuing:
  Headings
  Route
  Speed
  Altitude
  Unless specified in an LOA or facility directive
“BRAVO CENTER, REQUEST LOWER”
GLJ
LO

## Slide 32: Control Transfer
Transfer at:
  A prescribed or coordinated location, time, fix, or altitude; or
  Time a radar handoff and frequency change to the receiving controller have been completed
Control Transfer Fix
H/O Complete
SWA28
140 210
156 425
R
SWA28
140 210
156O-18
R

## Slide 33: Radio Comm Transfer
Transfer comm before entering the receiving controller’s area
Specify:
  Who to contact
  Frequency
Sector boundary
“SOUTHWEST TWENTY-EIGHT CONTACT BRAVO CENTER ONE TWO SIX POINT ZERO”
SWA28
140 210
156O-18
R

## Slide 34: Operational Request
Respond to a request from another controller, pilot
Restating the request in complete or abbreviated terms followed by “APPROVED”
“DELTA FORTY-TWO, DEVIATION RIGHT APPROVED”
“DELTA FORTY-TWO REQUEST RIGHT DEVIATION AROUND WEATHER”
DAL42
210C
062 438

## Slide 35: Knowledge Check
When may you issue control instructions in another controller’s area?
  After coordinating your actions
  Once you have established communications with the pilot
  When the target is radar identified

## Slide 36: Knowledge Check
Which statement is correct concerning formation flights?
  Control instructions must be issued and acknowledged by each aircraft within the formation
  Separation within the formation is the responsibility of the flight leader and the pilots in the flight
  Air traffic control must ensure separation between aircraft established within a formation

## Slide 37: Knowledge Check
What is the phraseology to disapprove a pilot request?
  “NEGATIVE YOUR PREVIOUS REQUEST”
  “REFUSING REQUESTED ACTION”
  “UNABLE DUE TO TRAFFIC”

## Slide 38: Knowledge Check
When should you transfer radio communications?
  Before the aircraft transitions the first NAVAID in the receiving controller’s area
  Before the aircraft crosses an imaginary line 10 miles or 2 minutes, whichever is farther, from the next controller’s area
  Before an aircraft enters the receiving controller’s area of jurisdiction

## Slide 39: Activity: Board Management Discussion
Purpose
  Review procedures for board management, such as:
    Sequencing
    Fix posting
    Local strip marking
Materials
  None
Directions
  This activity takes approximately 30 minutes to complete. Instructor will discuss board management procedures.

## Slide 40: Sequencing Flight Progress Strips
No standard procedures exist for sequencing or scanning flight progress strips
Common practices used by controllers will assist in understanding the board management example on the following pages

## Slide 41: Fix/Time Sequencing Example
Strips have been arranged with earliest time at the bottom
Scan strips and place a red “W” next to the altitude of each aircraft in conflict
ATY

## Slide 42: Summary
This lesson covered:
Duty priority
Expeditious compliance
Operational priorities
Requirements for reporting essential information
General control procedures
Procedures for board management