## Slide 2
Clearance requirements
Procedures for departing IFR aircraft
Procedures for IFR clearances

## Slide 3: ATC Clearances
Instructions issued by ATC to authorize flight within controlled airspace for the purpose of avoiding collision between known aircraft and/or terrain
Contains items such as:
  Clearance limit
  Route of flight
  Altitude data

## Slide 4: Clearance Structure
Aircraft ID
Clearance Limit
Mach number
Holding instructions
Altitude data
Standard Instrument Departure (SID)
Route of flight
Frequency and beacon code information
Any special instructions
Issue the following clearance items, as appropriate, in the order listed below:

## Slide 5: Aircraft Identification
All clearances begin with the proper aircraft identification
Examples:
“DELTA TWENTY-TWO CLEARED…”
“KINGAIR FOUR FOUR HOTEL KILO CLEARED…”

## Slide 6: Clearance Limit, Destination Airport
The point to which an aircraft is granted an air traffic control clearance
  Normally the airport of intended landing
  Include the airport name and the word “AIRPORT”
Examples:
“CLEARED TO DALLAS LOVE AIRPORT…”
“CLEARED TO SEDONA AIRPORT…”
“CLEARED TO LAGUARDIA AIRPORT…”

## Slide 7: Clearance Limit, Intermediate Fix
Under certain conditions, a short range clearance is issued to a NAVAID, intersection, or waypoint
  Include the type if known
If a delay is expected, issue complete holding instructions
If no delay expected, state NO DELAY EXPECTED
Examples:
“CLEARED TO YORK VORTAC, NO DELAY EXPECTED”
“CLEARED TO FORT UNION VORTAC HOLD NORTHEAST AS PUBLISHED…”

## Slide 8: Standard Instrument Departure (SID)
Assign a SID
  Include a transition if necessary
Example:
“STROUDSBURG ONE DEPARTURE”
“STROUDSBURG ONE DEPARTURE, SPARTA TRANSITION”

## Slide 9: Route of Flight
The route to be flown based on the altitude requested by the pilot
  Below FL180: Victor airways, T Routes
  FL180 and above: Jet Routes, Q Routes
  Any altitude: Course, heading, azimuth, arc, or vector
Also include:
  Routing expected if any part of the route beyond a short range clearance limit differs from that filed
Example:
“…EXPECT DIRECT TAOS VORTAC VICTOR EIGHTY-THREE…”

## Slide 10: Altitude Data
Issue altitude data in the order flown
  If the altitude assigned is different from the altitude requested inform the pilot when to expect climb or descent clearance to the requested altitude

## Slide 11: Mach Number
Assign speed adjustments using a Mach number, if applicable
Example:
“MAINTAIN MACH POINT SEVEN FOUR OR GREATER”
NOTE: The use of Mach numbers is restricted to turbojet aircraft with Mach meters.

## Slide 12: Holding Instructions
Issue the following:
  Clearance limit
  If any part of the route beyond a clearance limit differs from the last routing cleared, issue the route the pilot can expect beyond the clearance limit
  Holding instructions
    May be eliminated when no delay is expected
  Expect Further Clearance (EFC) time
    Do not specify this item if no delay is expected

## Slide 13: Special Information
Issue any special information needed

## Slide 14: Frequency and Beacon Code Information
Frequency
  Issue appropriate frequency
  Time or location for contacting ATC
Beacon Code
  Issue the Mode 3/A transponder code

## Slide 15: Clearance Example
UNITED FIFTY-FIVE, CLEARED TO O’HARE AIRPORT VIA AKUNA SEVEN DEPARTURE MCALESTER SPRINGFIELD JAY 105 WELTS SHAIN ONE. CLIMB AND MAINTAIN FIVE THOUSAND, EXPECT FLIGHT LEVEL THREE ONE ZERO, ONE ZERO MINUTES AFTER DEPARTURE. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO. SQUAWK THREE ONE SIX TWO.
Aircraft identification
Altitude data in order flown
Mach number, if applicable
Holding instructions, Any special instructions
Frequency
Clearance limit
Standard Instrument Departure
Route of flight
Beacon Code Information

## Slide 16: Clearances to USAF Aircraft
When issuing a clearance to an airborne USAF aircraft containing an altitude assignment, do not include more than one of the following in the same transmission:
  Frequency change
  Transponder change
  Heading
  Altimeter setting
  Traffic information containing an altitude

## Slide 17: Knowledge Check
You are issuing a short range clearance to a departing aircraft with a different route than filed. Which statement is correct?
  The pilot is responsible for further routing after the clearance limit
  Have the new route ready and wait for the pilot to request the route
  Include the new expected route in the clearance

## Slide 18: Knowledge Check
Which phraseology example is correct when issuing a clearance limit?
  "CLEARED TO DALLAS LOVE AIRPORT VIA...”
  "CLEARED TO DALLAS LOVE FIELD VIA...”
  "CLEARED TO DALLAS LOVE VIA…”

## Slide 19: Knowledge Check
Which statement is correct concerning clearances to airborne USAF aircraft that contain an altitude?
  Issue as many additional instructions as needed in the following order: frequency, transponder, heading, altimeter setting, traffic information containing an altitude
  Do not include more than one of the following: frequency, transponder, heading, altimeter setting, traffic information containing an altitude
  USAF aircraft have no restrictions

## Slide 20: Knowledge Check
What is the proper order to issue altitude information in a departure clearance?
  Issue starting at the requested altitude and work down
  Issue in the order flown
  Issue all the altitudes then include any restrictions

## Slide 21: Knowledge Check
Which statement is correct about issuing a short range clearance limit?
  Issue a short range clearance limit only when requested by the pilot
  Issue short range clearances only in a radar environment
  Issue complete holding instructions or “NO DELAY EXPECTED”

## Slide 22: Prefix Clearances for Relay
Clearances are relayed verbatim
Prefix with:
  “ATC CLEARS”
  “ATC ADVISES”
  “ATC REQUESTS”
FSS must prefix a clearance appropriately
“ATC CLEARS SKYLANE…”
“ATC CLEARS SKYLANE…”

## Slide 23: Departure Terminology
Avoid using:
  “TAKEOFF”
Use these terms when necessary:
  “DEPART”
  “DEPARTURE”
  “FLY”
Control Towers Only
“CLEARED FOR TAKEOFF RUNWAY…”

## Slide 24: Airspace Review
FL 600
18,000 MSL
Class E
1200 AGL
700 AGL
14,500 MSL
Class G
Class A
Class E surface Area
Notes: TIE-IN: …This is an expanded view showing how Class D/E Surface Areas are depicted on Sectional Charts

## Slide 25: Departure Instructions: Class D
“TWIN CESSNA TWO TWO, CLEARED TO DYERSBURG AIRPORT VIA DEPART NORTH, TURN LEFT, FLY HEADING THREE FIVE ZERO UNTIL JOINING VICTOR ELEVEN, VICTOR ELEVEN DYERSBURG. CLIMB AND MAINTAIN SEVEN THOUSAND, CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND, SQUAWK TWO FIVE FIVE TWO.”
350°

## Slide 26: Class E Surface Area: Solicit Pilot Concurrence
FSS: “REQUEST CLEARANCE FOR CESSNA TWO ONE TO JACKSON”
Controller: “WILL CESSNA TWO ONE ACCEPT A NORTH DEPARTURE WITH TURNS?”
FSS: “AFFIRMATIVE”
Controller: “CLEARANCE…”

## Slide 27: Class E Surface Area: Issue Clearance
“CESSNA TWO ONE CLEARED FROM VICKSBURG AIRPORT TO JACKSON AIRPORT VIA DEPART NORTH, TURN RIGHT, FLY HEADING ZERO FOUR ZERO UNTIL JOINING VICTOR FOUR SEVENTEEN, VICTOR FOUR SEVENTEEN MAGNOLIA VORTAC, THEN AS FILED. CLIMB AND MAINTAIN NINER THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK THREE FOUR TWO TWO. ADVISE CESSNA TWO ONE RELEASED FOR DEPARTURE.”

## Slide 28: Class E Surface Area: Verify Clearance
“CESSNA TWO ONE CLEARED FROM VICKSBURG AIRPORT TO JACKSON AIRPORT VIA DEPART NORTH, TURN RIGHT, FLY HEADING ZERO FOUR ZERO UNTIL JOINING VICTOR FOUR SEVENTEEN, VICTOR FOUR SEVENTEEN MAGNOLIA VORTAC, THEN AS FILED. CLIMB AND MAINTAIN NINER THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK THREE FOUR TWO TWO. VERIFY THIS CLEARANCE WILL ALLOW COMPLIANCE WITH TERRAIN OR OBSTRUCTION AVOIDANCE.”

## Slide 29: Departure Instructions: Other Airports
“CESSNA TWO FOUR CLEARED FROM LAKE PROVIDENCE AIRPORT TO MONROE AIRPORT. WHEN ENTERING CONTROLLED AIRSPACE, FLY HEADING TWO TWO ZERO UNTIL JOINING VICTOR FOUR TWENTY-SEVEN, VICTOR FOUR TWENTY-SEVEN. CLIMB AND MAINTAIN SIX THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK FIVE SIX SEVEN ZERO. VERIFY THIS CLEARANCE WILL ALLOW COMPLIANCE WITH TERRAIN OR OBSTRUCTION AVOIDANCE.”

## Slide 30: Instrument Departure Procedures
Some airports have few obstructions
Others are more hazardous

## Slide 31: Instrument Departure Procedures (Cont’d)
Preplanned IFR procedures provide obstruction clearance from the terminal area to the en route structure
  Obstacle Departure Procedures (ODP)
    Printed textually or graphically
    May be flown without clearance
  Standard Instrument Departures (SID)
    Always printed graphically
    Provide obstruction clearance
    ATC clearance must be received prior to flying

## Slide 32: Visual Climb Over Airport (VCOA)
Used in VMC equal to or greater than the specified visibility and ceiling
  Allows climbing turns over the airport to the published “at or above” altitude
If an ODP is included in the clearance and VCOA is requested by the pilot or assigned by ATC when it is the only procedure published in the ODP, include an instruction to remain within the published visibility of the VCOA

## Slide 33: Aircraft Performance Expectations

## Slide 34: ODP Examples
KVKS - Vicksburg Municipal Airport, Mississippi
KJAC - Jackson Hole Airport, Wyoming
KRUT - Rutland Regional Airport, Vermont

## Slide 35: Higher Takeoff Minimums, VCOA - KVKS
Vicksburg Municipal Runway
VICKSBURG, MS
VICKSBURG MUNI (VKS)
TAKEOFF MINIMUMS AND (OBSTACLE)
DEPARTURE PROCEDURES
AMDT 3 08NOV18 (18312) (FAA)
TAKEOFF MINIMUMS:
Rwy 1, std. w/min. climb of 290’ per NM to 800
or 900 2-1/2 for VCOA. Rwy 19, 300-2 or std.
w/min. climb of 425’ per NM to 400.
VCOA: Rwy 1, obtain ATC approval for VCOA
when requesting IFR clearance. Climb in
visual conditions to cross Vicksburg Muni
airport at or above 900 before proceeding
on course.

## Slide 36: Charted DP and SID - KJAC
Jackson Hole Runway

## Slide 37: Charted DP and SID - KJAC
(GEYSR6.NALSI) 21336
GEYSR SIX DEPARTURE (OBSTACLE)
(TETON3.KICNE) 16147
TETON THREE DEPARTURE (OBSTACLE)
(ALPIN3.KICNE) 21336
ALPIN THREE DEPARTURE

## Slide 38: Higher Takeoff Minimums, Runway Restriction, VCOA, Text DP - KRUT
Rutland Runways

## Slide 39: KRUT Airport
X
DYO
NDB
RUTLAND, VT
SOUTHERN VERMONT RGNL (RUT)
TAKEOFF MINIMUMS AND (OBSTACLE)
DEPARTURE PROCEDURES
AMDT 4A 07FEB13 (13038) (FAA)
TAKEOFF MINIMUMS:
Rwy 1, std. w/ min. climb of 439’ per NM to
3000, or 3600-3 for climb in visual conditions.
Rwy 13, NA-obstacles.
Rwy 19, std. w/ min. climb of 470’ per NM to
3300, or 3600-3 for climb in visual conditions.
Rwy 31, std. w/ min. climb of 500’ per NM to
4500, or 3600-3 for climb in visual conditions.
DEPARTURE PROCEDURE:
Rwy 1, climb on 013°course to DYO NDB, cross
DYO NDB at or above 6000, if not at 6000, depart
DYO NDB on bearing 325° to 6000 before
proceeding on course. For climb in visual
condition: cross Rutland-Southern Vermont RGNL
airport at or above 4300 before proceeding on
course. When executing VCOA, notify ATC prior to
departure.
DEPARTURE PROCEDURE:
Rwy 19, climb heading 194° to 1400, then
climbing right turn on 025° course to DYO NDB,
cross DYO NDB at or above 6000, if not at 6000,
depart DYO NDB on bearing 325° to 6000 before
proceeding on course. For climb in visual
condition: cross Rutland-Southern Vermont RGNL
airport at or above 4300 before proceeding on
course. When executing VCOA, notify ATC prior to
departure.
DEPARTURE PROCEDURE:
Rwy 31, climb heading 329° to 1600, then
climbing right turn on 025° course to DYO NDB,
cross DYO NDB at or above 6000, if not at 6000,
depart DYO NDB on bearing 325° to 6000 before
proceeding on course. For climb in visual
condition: cross Rutland-Southern Vermont RGNL
airport at or above 4300 before proceeding on
course. When executing VCOA, notify ATC prior to
departure.

## Slide 40: KRUT ODP Example
Pilot files KRUT EBERT…
You must protect ODP over DYO and 330° until at or above 6,000’
  KRUT to DYO 11NM
Pilots Flight Path
Cleared Route

## Slide 41: Assigning a SID
SIDs are primarily designed for system enhancement to expedite traffic flow and to reduce pilot/controller workload
  At busier airports they increase efficiency and reduce communications and departure delays
  Assign SIDs, as necessary, for traffic management and convenience
If it is necessary to assign a crossing altitude, which differs from the SID altitude, emphasize the change to the pilot

## Slide 42: Altitude Assignments
Issue one of the following:
  Altitude requested by the pilot
  Altitude as near as possible to altitude requested by the pilot
    Inform pilot when to expect requested altitude unless instructions are contained in the specified SID
    If the requested altitude is not expected to be available, inform the pilot what altitude can be expected and when/where to expect it

## Slide 43: Altitude Assignments (Cont’d)
When a SID:
  Does not contain published crossing restrictions and/or
  Is a SID with a Radar Vector segment, or
  Is a Radar Vector SID, or
  Is constructed with a Radar Vector segment and contains published crossing restrictions after the vector segment
Instruct aircraft to:
  MAINTAIN (altitude)
  or
  CLIMB AND MAINTAIN (altitude). EXPECT (requested altitude) AT (time or fix).

## Slide 44: Clearances to Air Force One
Clearance limit
  Do not specify the destination airport
  NOTE: Presidential detail is responsible for ensuring the accuracy of the destination airport.
  Phraseology: “…DESTINATION AS FILED”
Initial altitude
  9,000’ AGL or higher
  If unable the highest available altitude

## Slide 45: Knowledge Check
What is the proper way to issue departure headings to aircraft departing from airports within Class G airspace?
  “…DEPART NORTH, FLY HEADING…”
  “…FLY RUNWAY HEADING UNTIL ENTERING CONTROLLED AIRSPACE…”
  “…WHEN ENTERING CONTROLLED AIRSPACE, FLY HEADING…”

## Slide 46: Knowledge Check
What prefix phrase must you use to relay a clearance to an aircraft through another aircraft?
  “ATC CLEARS”
  “ATC RELAYS”
  “ATC WANTS”

## Slide 47: Knowledge Check
At airports within a Class E surface area where airport traffic control service is NOT provided, when can you specify the initial heading to be flown after takeoff?
  Anytime you decide, if necessary to expedite the departure
  After obtaining/soliciting the pilot’s concurrence concerning these items
  Only on pilot request

## Slide 48: Knowledge Check
You issue a departure clearance at an airport with a published Obstacle Departure Procedure (ODP). Which statement is correct?
  The pilot may fly the ODP when cleared for departure
  You must assign the ODP to all departures
  ODPs apply only to pilots unfamiliar with the local terrain

## Slide 49: Knowledge Check
What is the minimum altitude you should assign to Air Force One if traffic is not a factor?
  FL180
  9,000’ AGL
  9,000’ MSL

## Slide 50: Knowledge Check
Which example is the phraseology for issuing a departure direction?
  “TAKEOFF NORTH…”
  “DEPART NORTH…”
  “EXIT THE TRAFFIC PATTERN NORTH…”

## Slide 51: Knowledge Check
Which statement is correct concerning a Standard Instrument Departure (SID)?
  SIDs may be flown without a specific ATC clearance
  SIDs are never published in graphical form
  SIDs always provide terrain clearance

## Slide 52: Knowledge Check
You issue a departure clearance, but due to traffic, you cannot assign the requested altitude. What should you do?
  Issue a safe altitude and inform pilot when to expect clearance to the requested altitude
  Delay the departure until the requested altitude is available
  Issue the lowest safe altitude and wait for the pilot to request higher

## Slide 53: Knowledge Check
What is the proper way to issue a clearance limit to Air Force One?
  “CLEARED TO ANDREWS AIRPORT VIA…”
  “CLEARED TO ANDREWS AIR FORCE BASE VIA…”
  “CLEARED TO DESTINATION AS FILED"

## Slide 54: Knowledge Check
You are issuing a clearance through FSS/ARTCC Flight Data Units. What must be included in the clearance?
  Prefix “ATC CLEARS…”
  Airport of departure
  Time check if a clearance void time is used

## Slide 55: Knowledge Check
You issue a departure clearance with a climb via standard instrument departure but want the aircraft to stop below the highest published altitude. What is the phraseology?
  "CLIMB VIA SID EXCEPT MAINTAIN..."
  "CLIMB VIA SID STOP CLIMB AT..."
  "AMEND CLIMB VIA SID ALTITUDE TO..."

## Slide 56: Practice Exercise: Departure Clearances
Purpose
  Issuing departure clearances using appropriate phraseology
Materials
  Practice Exercise: Departure Clearances
  Pencil or pen
Directions
  This exercise will take approximately 30 minutes to complete. The instructor will present traffic situations and specific departure criteria. You will be required to write out a clearance incorporating these criteria in the proper format. Each situation will be presented individually and reviewed before proceeding to the next.

## Slide 57: Practice Exercise: Departure Clearances
1.

## Slide 58: Practice Exercise: Departure Clearances
CESSNA ONE ONE CLEARED TO STARKSVILLE AIRPORT VIA DEPART SOUTH FLY HEADING ONE TWO ZERO UNTIL JOINING VICTOR TWO SEVENTY-EIGHT, VICTOR TWO SEVENTY-EIGHT CLOUT INTERSECTION DIRECT. CLIMB AND MAINTAIN SEVEN THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK TWO FIVE THREE THREE.
1.

## Slide 59: Practice Exercise: Departure Clearances
2.

## Slide 60: Practice Exercise: Departure Clearances
Obtain/solicit pilot concurrence for direction of takeoff and turn, OR at end of clearance “Verify this clearance will allow compliance with terrain or obstruction avoidance.”
SUNDOWNER ONE TWO CLEARED FROM VICKSBURG AIRPORT TO MONROE AIRPORT VIA DEPART NORTH, TURN LEFT, FLY HEADING THREE ZERO FIVE UNTIL JOINING VICTOR FOUR SEVENTEEN, VICTOR FOUR SEVENTEEN MONROE. CLIMB AND MAINTAIN EIGHT THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK THREE THREE FIVE SEVEN. ADVISE SUNDOWNER ONE TWO RELEASED FOR DEPARTURE.
2.

## Slide 61: Practice Exercise: Departure Clearances
3.

## Slide 62: Practice Exercise: Departure Clearances
MOONEY ONE THREE CLEARED TO GREENVILLE AIRPORT VIA SIDON VORTAC VICTOR TWO SEVENTY-EIGHT GREENVILLE DIRECT. CROSS SIX MILES WEST OF SIDON AT OR BELOW FOUR THOUSAND, CLIMB AND MAINTAIN EIGHT THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK FOUR TWO SEVEN ONE.
3.

## Slide 63: Practice Exercise: Departure Clearances
4.

## Slide 64: Practice Exercise: Departure Clearances
SKYHAWK ONE FOUR CLEARED TO ARGUW INTERSECTION VIA SIDON VORTAC VICTOR FIVE FIFTY-FIVE NO DELAY EXPECTED. EXPECT FURTHER ROUTING VIA VICTOR FIVE FIFTY-FIVE JACKSON VORTAC DIRECT. CLIMB AND MAINTAIN FIVE THOUSAND, EXPECT SEVEN THOUSAND AT ARGUW. NINER THOUSAND IS NOT AVAILABLE. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK ZERO SEVEN TWO ONE.
4.

## Slide 65: Practice Exercise: Departure Clearances
5.

## Slide 66: Practice Exercise: Departure Clearances
CESSNA ONE FIVE CLEARED FROM LAKE PROVIDENCE AIRPORT TO LAUREL AIRPORT. WHEN ENTERING CONTROLLED AIRSPACE FLY HEADING ONE FOUR ZERO UNTIL JOINING VICTOR FOUR TWENTY-SEVEN, VICTOR FOUR TWENTY-SEVEN JACKSON VICTOR ELEVEN LAUREL. CLIMB AND MAINTAIN SEVEN THOUSAND. CONTACT BRAVO CENTER ONE TWO FIVE POINT ZERO LEAVING THREE THOUSAND. SQUAWK ONE FOUR ZERO SIX. VERIFY THIS CLEARANCE WILL ALLOW COMPLIANCE WITH TERRAIN OR OBSTRUCTION AVOIDANCE.
5.

## Slide 67: Abbreviated Departure Clearance
“JET BLUE FIVE TWENTY-THREE CLEARED TO LOS ANGELES AIRPORT VIA KENNEDY FIVE DEPARTURE COATE TRANSITION, THEN AS FILED. CLIMB AND MAINTAIN FIVE THOUSAND, EXPECT FLIGHT LEVEL THREE TWO ZERO ONE ZERO MINUTES AFTER DEPARTURE. CONTACT DEPARTURE ONE TWO FIVE POINT ZERO. SQUAWK ZERO SEVEN TWO ONE.”
“JET BLUE FIVE TWENTY-THREE CLEARED TO LOS ANGELES AIRPORT VIA KENNEDY FIVE DEPARTURE COATE TRANSITION Q-FOUR THIRTY-SIX RAAKK Q FOUR THIRTY-EIGHT RUBYY DABJU KILO GOLF SEVEN EIGHT KILO, KILO PAPA SEVEN FIVE GOLF, KILO DELTA SIX NINE ALPHA, KILO DELTA SIX SIX YANKEE, KILO DELTA SIX ZERO WHISKY, TAYLR KILO DELTA FOUR EIGHT SIERRA, TOADD JASSE Q-NINETY DNERO ANJLL FOUR. CLIMB AND MAINTAIN FIVE THOUSAND, EXPECT FLIGHT LEVEL THREE TWO ZERO, ONE ZERO MINUTES AFTER DEPARTURE. CONTACT DEPARTURE ONE TWO FIVE POINT ZERO. SQUAWK ZERO SEVEN TWO ONE.”

## Slide 68: Abbreviated Departure Clearance Modifications to Route
If route must be modified include one of the following in remarks
  FRC
  FRC/(fix)
    Issue full route to specified fix or destination airport
    Always first item of intracenter remarks

## Slide 69: Abbreviated Departure Clearance
Nonradar environment, specify one, two, or more fixes as necessary to identify the initial route of flight
Do not apply these procedures when a pilot requests a detailed clearance or to military operations conducted within:
  ALTRVs
  Stereo routes
  Operations above FL600
  Other military operations requiring special handling

## Slide 70: Knowledge Check
What is an abbreviated departure clearance?
  Departure clearance containing no altitude information
  Departure clearance using “Cleared as filed…”
  Departure clearance for ALTRVs

## Slide 71: Knowledge Check
What does “FRC/OVR” in remarks signify?
  Fly Right Course Over the airport
  Full Return Capable Overseas Flight
  Full Route Clearance to OVR

## Slide 72: Knowledge Check
Which flight group is authorized to receive an abbreviated departure clearance?
  Operations above FL600
  General aviation aircraft
  Stereo Routes

## Slide 73: Departure Restrictions
Assign the following to separate departures from other traffic or to restrict or regulate the departure flow:
  Departure release
  Release time
  Hold for release
  Expect departure clearance time
  Call for release
  Clearance void time
  Ground stop

## Slide 74: Departure Release
“…ADVISE NOVEMBER TWO THREE FOUR RELEASED FOR DEPARTURE”

## Slide 75: Release Time
“…RELEASED FOR DEPARTURE AT ONE SIX ONE EIGHT…”

## Slide 76: Hold For Release
Used by ATC to delay an aircraft for traffic, weather, volume, etc.
  Hold for release instructions are used to inform a pilot or a controller that an IFR departure clearance is not valid until a release time or additional instructions have been received

## Slide 77: Expect Departure Clearance Time
Runway release time assigned to an aircraft in a traffic management program

## Slide 78: Call For Release (CFR)
When aircraft take a delay on the ground
  Issue departure clearances in the order in which the requests were made
Inform approach control facilities and/or towers of anticipated departure delays

## Slide 79: Clearance Void Time
“…CLEARANCE VOID IF NOT OFF BY TWO TWO THREE FIVE. IF NOT OFF BY TWO TWO THREE FIVE, ADVISE BRAVO CENTER NOT LATER THAN TWO TWO FOUR FIVE OF INTENTIONS.”

## Slide 80: Ground Stop
Requires aircraft meeting specific criteria to remain on the ground
  The criteria may be:
    Airport specific
    Airspace specific
    Equipment specific
Do not release aircraft on an EDCT if a ground stop applicable to that aircraft is in effect

## Slide 81: Coordination with Receiving Facility
Coordinate if less than 15 minutes flying time from the transferring facility’s boundary
  If automatic transfer of data between automated systems will occur flying time may be reduced to 5 minutes
24 NM
12 Min.

## Slide 82: Information Forwarded to Receiving Facility
Forward the following information to the receiving facility:
  Aircraft identification
  Number of aircraft
  Assigned altitude and ETA over last reporting point/fix
  Altitude entering receiving facility
  True airspeed
  Point of departure
  Route of flight
  Destination airport and clearance limit
  ETA at destination airport
  Altitude requested if differs from requested altitude
  Beacon code
  Longitudinal separation, if needed
  Additional information

## Slide 83: VFR Release of IFR Departures
Aircraft on an IFR flight plan requests a VFR departure through a terminal facility, FSS, or air/ground communications station:
  You may authorize an IFR flight planned aircraft to depart VFR
  Inform the pilot of the proper frequency
  State where or when to contact the facility
If unable to issue clearance, inform pilot and:
  Suggest delay be taken on the ground
  If pilot insists on departing VFR inform the facility/sector holding the flight plan

## Slide 84: Knowledge Check
Who must issue a time check for clearance void times?
  FBO at the departure field
  Facility issuing the clearance to the pilot
  Flight dispatcher

## Slide 85: Knowledge Check
What is the departure window associated with a Call For Release (CFR)?
  2 minutes prior and ends 1 minute after the assigned time
  5 minutes prior and ends 5 minutes after the assigned time
  10 minutes prior and ends 5 minutes after the assigned time

## Slide 86: Knowledge Check
What should be included with a HFR time?
  High flow route clearance
  A clearance void time
  Departure delay information

## Slide 87: Knowledge Check
Actual departure times must be forwarded to an external facility if assumed departure time differs by what amount?
  3 minutes
  5 minutes
  10 minutes

## Slide 88: Knowledge Check
A pilot with an IFR flight plan requests a VFR departure but due to volume, you know a clearance cannot be issued in the near future. What should you do?
  Issue a provisional SVFR clearance to aid the pilot
  Clear the pilot to depart “AT YOUR OWN RISK”
  Suggest a delay be taken on the ground

## Slide 89: Knowledge Check
What must be issued to departures from airports without an operating control tower?
  Wind and altimeter check
  Departure release
  Runway heading alignment confirmation

## Slide 90: Through Clearance
You may clear aircraft through intermediate stops
  Issue departure restrictions as necessary
Cleared for approach and through to final destination
To Destination

## Slide 91: Airfile Aircraft Guidelines
Process airfile aircraft as follows:
  Ensure aircraft is within your area of jurisdiction, unless coordinated
  Obtain information necessary to provide IFR service
  Issue clearance to:
    Destination airport
    Short range clearance limit
  Instruct pilot to contact FSS if flight plan cannot be processed

## Slide 92: IFR to VFR
Clear an aircraft planning IFR operations for the initial part of the flight and VFR for the latter part to the fix at which the IFR part ends

## Slide 93: VFR to IFR
Treat an aircraft planning VFR operations for the initial part of the flight and IFR for the latter part as a VFR departure
  Issue a clearance to this aircraft when it requests IFR clearance approaching the fix where it proposes to start IFR operations

## Slide 94: North American Route Program (NRP)
If the aircraft is moved due to weather, traffic, or other tactical reasons
  “NRP” must be retained in remarks
If the route is altered due to a pilot request
  “NRP” must be removed from remarks
“NRP” must not be entered in the remarks unless:
  Prior coordination is accomplished

## Slide 95: Route Structure Transitions
Transitions within or between route structures, may be accomplished via multiple methods. Clear aircraft by one or more of the following:
  Vector aircraft:
  Assign a SID/STAR
  Clear departing or arriving aircraft:
    To climb or descend via radials, courses, or azimuths of the ATS route assigned
    Direct to or between the NAVAIDs forming the ATS route assigned

## Slide 96: Route Structure Transitions (Cont’d)
  Clear aircraft to climb or descend via:
    ATS route, specified radials, courses, or azimuths of NAVAIDs
  Clear RNAV aircraft between designated or established ATS routes via random RNAV routes to a NAVAID, waypoint, airport or fix on the new route
  Provide radar monitoring to RNAV equipped aircraft transitioning via random RNAV routes
  Offset from published or established ATS route at a specified distance and direction for random (impromptu) RNAV Routes

## Slide 97: DME Arcs of NAVAIDS
Flight track a constant distance from the station or waypoint
Predicated on DME collocated with a facility
  Cannot be based on an ILS or LOC DME source
  DME arcs on approach plates will have a lead radial
Assign a DME arc by stating
  Distance from the NAVAID followed by “MILE ARC”
  Direction from the NAVAID
  Eight principal points of the compass
  “OF,” and the name of the NAVAID

## Slide 98: Radius of a NAVAID
Courses, azimuths, bearings, quadrants, or radials within a radius of a NAVAID
  State direction from NAVAID in terms of the quadrant; e.g., NE, SE, SW, NW
    Quadrant - A quarter part of a circle, centered on a NAVAID, oriented clockwise from magnetic north as follows:
      NE quadrant 000-089
      SE quadrant 090-179
      SW quadrant 180-269
      NW quadrant 270-359

## Slide 99: Knowledge Check
What is the definition of “quadrant” from the Pilot/Controller Glossary?
  Four-part departure with 90º turns
  Quarter part of a circle centered on a NAVAID
  Military Operations Area shaped like a square

## Slide 100: Knowledge Check
A flight with “NRP” in remarks changes the route of flight at the pilot’s request. What is the proper procedure?
  Deny all route requests from “NRP” aircraft
  Allow the New Route Possible request and leave “NRP” in the remarks
  Remove “NRP” from remarks

## Slide 101: Knowledge Check
What is the phraseology used to issue a DME arc south of Pendleton VORTAC at 15 miles?
  “ONE FIVE MILE ARC SOUTH OF PENDLETON VORTAC”
  “DME ARC SOUTH OF PENDLETON VORTAC AT ONE FIVE MILES”
  “DME ARC OF PENDLETON VORTAC AT ONE FIVE MILES SOUTH”

## Slide 102: Knowledge Check
What is the phraseology to clear an aircraft to fly a parallel course to an air traffic service route?
  “OFFSET EIGHT MILES RIGHT OF VICTOR SIX”
  “PARALLEL VICTOR SIX EIGHT MILES RIGHT”
  “FLY ALONG SIDE VICTOR SIX BY EIGHT MILES”

## Slide 103: Knowledge Check
What magnetic radials make up the southeast quadrant of a NAVAID?
  100-180°
  120-200°
  090-179°

## Slide 104: Knowledge Check
What is a key factor when issuing a clearance to airfile aircraft?
  Displaying the current altimeter
  Ensure the aircraft is within your area of jurisdiction
  Advise the pilot to remain clear of clouds

## Slide 105: Substitute Routes
When any part of an airway or route is unusable because of NAVAID status, clear aircraft that are not RNAV capable via one of the following alternative routes:
  Route depicted on current U.S. Government charts/publications
    Use the word “substitute” immediately preceding the alternative route in issuing the clearance
  Route defined by specifying NAVAID radials, courses, or azimuths
  Route defined as direct to or between NAVAIDs
  Vectors

## Slide 106: Class G Airspace
Include routes through Class G airspace only when requested by the pilot
  Flight plans filed for random RNAV routes through Class G airspace are considered a request by the pilot
  Flight plans containing military training route segments in/through Class G airspace are considered a request by the pilot

## Slide 107: Clearance Amendments
Amend route of flight in a previously issued clearance by one of the following:
  State which portion of the route is being amended, and then state the amendment
  State the amendment to the route, and then state that the rest of the route is unchanged

## Slide 108: Arrival Information
If flight is within a surface area for which the tower has responsibility:
  Coordinate with the nonapproach control tower
    Unless otherwise specified in a letter of agreement
Transfer radio communications
  Before an aircraft enters the receiving controller’s area
If an IFR aircraft intends to land at an airport not served by a tower or FSS
  Approve a change to the advisory service frequency when you no longer require direct communications

## Slide 109: Knowledge Check
What is the phraseology used when you no longer require direct communication to aircraft landing at an airport without a tower or FSS?
  “CHANGE TO ADVISORY FREQUENCY APPROVED”
  “CONTACT UNICOM FREQUENCY”
  “CALL YOUR ARRIVAL ON THE CTAF FREQUENCY”

## Slide 110: Knowledge Check
What is the phraseology used at the end of a route change clearance to indicate the remainder is the same as the current route of flight?
  “…REMAINDER OF ROUTE IS THE SAME”
  “…REST OF ROUTE UNCHANGED”
  “…NO CHANGE TO REST OF ROUTE”

## Slide 111
Clearance requirements
Procedure for departing IFR aircraft
Procedures for IFR clearances