## Slide 2
Procedures for issuing altimeter settings
Requirements for altitude assignments
Phraseology for altitude assignments
Requirements for minimum altitudes

## Slide 3: Altimeter Settings
An Altimeter Setting is the barometric pressure reading used to adjust a pressure altimeter for variations in existing atmospheric pressure, or to the standard altimeter setting of 29.92
The current setting shall be obtained from:
  Direct reading instruments
  Weather reporting stations

## Slide 4: Altimeter Setting Issuance
Issue the current altimeter setting to:
  All en route aircraft operating below FL180 at least one time while operating within your area of jurisdiction
  Arriving aircraft approximately 50 miles from destination if airport is not served by an approach control facility
    Issue the destination altimeter setting
  Aircraft cleared below the lowest usable flight level
    Issue an altimeter setting obtained from weather reporting station nearest point aircraft will descend through lowest usable flight level

## Slide 5: Lowest Usable Flight Level
The lowest usable flight level is determined by atmospheric pressure in the area of operation
  Use the following table to determine the lowest usable flight level to clear aircraft at or above 18,000’ Mean Sea Level (MSL)
Altimeter Setting | Lowest Usable Flight Level
29.92 or higher | 180
29.91 to 28.92 | 190
28.91 to 27.92 | 200

## Slide 6: Knowledge Check
  Which altimeter setting should be issued?
    Destination
    Napa
    Oakland
Napa Weather Station
Oakland Weather Station
Destination
100 MILES
FL180
FL180

## Slide 7: Altitude for Direction of Flight
Below 3,000’ Above Ground Level (AGL)
  Assign any altitude for any direction of flight
At and below FL410
  On course of 0 through 179 degrees magnetic, use odd cardinal altitudes
  NOTE: Mnemonic “NEOD” - North/East Odd
  On course of 180 through 359 degrees magnetic, use even cardinal altitudes
  NOTE: Mnemonic “SWEVEN” - South/West Even

## Slide 8: RVSM Procedures
RVSM airspace is exclusively for RVSM capable aircraft
  Certain approved types of non-RVSM aircraft may be accommodated workload permitting
Aircraft not approved for RVSM operations may transition through RVSM airspace to operate above or below it
Apply appropriate separation standards and remove any aircraft from RVSM airspace that advises unable RVSM due to equipment

## Slide 9: VFR-On-Top Altitudes
Aircraft operating VFR-On-Top (OTP) more than 3,000’ AGL, up to but not including FL180
  On course 0 through 179 degrees magnetic:
    Odd cardinal altitudes plus 500’
  On course 180 through 359 degrees magnetic:
    Even cardinal altitudes plus 500’

## Slide 10: Exceptions to Flight Direction Rule
With prior approval from the affected sector or facility, you may assign an altitude regardless of flight direction when:
  Traffic conditions prevent the assignment of an appropriate altitude
  Aircraft is experiencing meteorological conditions such as icing, turbulence, or weather activity
  Military aircraft is operating on a random route
  Pilot informs you the available appropriate altitude exceeds the aircraft’s operational limitations

## Slide 11: Knowledge Check
An IFR aircraft is flying a magnetic course of 330 degrees; what is an appropriate altitude for direction of flight?
  7,000’
  7,500’
  8,000’

## Slide 12: Altitude Assignment Phraseology
“DELTA TEN, MAINTAIN ONE THREE THOUSAND UNTIL ONE EIGHT ONE TWO, CLIMB AND MAINTAIN ONE FIVE THOUSAND, TIME ONE EIGHT ONE ZERO”
“AMERICAN TWO FIFTY, CLIMB AND MAINTAIN FLIGHT LEVEL TWO SEVEN ZERO”
“NOVEMBER TWO TWO LIMA, CRUISE SIX THOUSAND”
“SKYMASTER FIVE ONE PAPA, CROSS RED BLUFF AT OR ABOVE ONE FOUR THOUSAND, MAINTAIN ONE SIX THOUSAND”

## Slide 13: Pilot’s Discretion
Pilot’s Discretion Examples:
  “AMERICAN TEN, DESCEND AT PILOT’S DISCRETION, MAINTAIN ONE TWO THOUSAND”
  “SOUTHWEST FIVE TWELVE, DESCEND NOW TO FLIGHT LEVEL TWO EIGHT ZERO, THEN DESCEND AT PILOT’S DISCRETION TO FLIGHT LEVEL TWO ZERO ZERO”
Cancelling Pilot’s Discretion:
  “SPEEDBIRD TWO, AMEND ALTITUDE MAINTAIN FLIGHT LEVEL TWO FOUR ZERO”

## Slide 14: Block Altitudes
Allows the assignment of more than one altitude to an aircraft
When issuing a block altitude, issue the lower altitude first
  Example: “ASPEN ONE TWO, MAINTAIN BLOCK ONE TWO THOUSAND THROUGH ONE FOUR THOUSAND”

## Slide 15: Vertical Navigation SIDs/STARs
Vertical Navigation (VNAV) - A function of area navigation (RNAV) equipment which calculates, displays, and provides vertical guidance to a profile or path
When assigned, allow the pilot to climb or descend via an assigned procedure while complying with any crossing restrictions and/or assigned speeds published in the procedure

## Slide 16: Vertical Navigation SIDs/STARs
FEXXX
FL230
17000
16000
BANKI
AWLIN
RUIZE
260K
ROBUC
FL230
FL210
FL190
12000
“…DESCEND VIA ROBUC THREE ARRIVAL”

## Slide 17: Vertical Navigation SIDs/STARs
FEXXX
FL230
17000
16000
BANKI
AWLIN
RUIZE
260K
ROBUC
FL230
FL210
FL190
12000
“…DESCEND VIA ROBUC THREE ARRIVAL, EXCEPT CROSS AWLIN AT FLIGHT LEVEL TWO TWO ZERO”
FL220

## Slide 18: Time to Climb or Descend
When a time restriction is issued on a climb or descent:
  Reference the UTC clock reading with a time check
  If issued through an authorized communications provider, such as Flight Service, advise the operator to issue the current time to the pilot

## Slide 19: Altitude Assignment
“UNITED TEN CROSS LINCOLN AT AND MAINTAIN FLIGHT LEVEL TWO THREE ZERO”
FL240
LNK
VORTAC
FL290
FL230
FL250
“UNITED TEN CAN’T MAKE THAT RESTRICTION”
“UNITED TEN DESCEND AND MAINTAIN FLIGHT LEVEL TWO FIVE ZERO”
“UNITED TEN DESCEND AND MAINTAIN FIGHT LEVEL TWO FIVE ZERO”
FL250

## Slide 20: Anticipated Altitude Change
“…EXPECT HIGHER IN TWO ZERO MILES”
17,000’
Active SAA FL180 and above
Inform aircraft when to:
  Expect climb/descent clearance
  Request altitude change from another facility

## Slide 21: Knowledge Check
Which is the phraseology for issuing more than one altitude to a single aircraft?
  “MAINTAIN FIVE THOUSAND THROUGH SEVEN THOUSAND”
  “MAINTAIN BLOCK TWO THOUSAND TO FIVE THOUSAND”
  “MAINTAIN BLOCK SIX THOUSAND THROUGH EIGHT THOUSAND”

## Slide 22: Altitude Confirmation - Nonradar
Request the pilot to confirm assigned altitude:
  On initial contact
  On each position report
Exceptions:
  The pilot states the assigned altitude on initial contact
  If assigning a new altitude to a climbing or descending aircraft

## Slide 23: Minimum En Route IFR Altitude (MEA)
MEA 6000
MEA 4000
MEA changes NOT at NAVAIDs

## Slide 24: Global Navigation Satellite System (GNSS) MEA
Minimum IFR altitude on ATS routes which ensures GNSS reception and obstacle clearance requirements

## Slide 25: Minimum Crossing Altitude (MCA)
MEA 6000
V113
MEA 4500
V113 MCA
6000 NW
X

## Slide 26: MEA for Route Segment without MCAs
MEA 6000
MEA 4000
MEA 10000
MEA 8000

## Slide 27: Minimum Obstruction Clearance Altitude (MOCA)
MOCA 2800
MEA 5500
22 NM
Nonradar Procedures usable here
NAVAID reception not assured in this area

## Slide 28: Knowledge Check
What two actions must be taken when clearing an aircraft to the MOCA while using radar procedures?
  Provide altitude instructions and issue alternate routing
  Provide radar guidance and issue lost communication procedures
  Provide traffic information and issue alternate routing

## Slide 29: Minimum Reception Altitude (MRA)

## Slide 30: Knowledge Check
When may an aircraft be cleared to the lower MEA along a route segment?
  Prior to reaching the fix where the lower MEA applies
  Within 22 NM of the NAVAID where the lower MEA applies
  When the aircraft is over or past the fix where the lower MEA applies

## Slide 31: No MEA Established
Clear aircraft at or above the Minimum Safe Altitude (MSA) for IFR operations prescribed by CFR 91.177
  Mountainous areas
    2,000’ above the highest obstacle within a horizontal distance of 4 NM from the course being flown
  Any other areas
    1,000’ above the highest obstacle within a horizontal distance of 4 NM from the course being flown

## Slide 32: Knowledge Check
When no MCA is established, when must an aircraft be cleared to climb to meet a higher MEA?
  Prior to, or immediately after passing the fix where the new MEA applies
  Only after crossing the fix where the new MEA applies
  Only before crossing the fix where the new MEA applies

## Slide 33: Knowledge Check
When no MEA is established for a route segment, how can you ensure an aircraft cleared on that route would meet obstacle clearance requirements?
  Clear the aircraft at or above the MSA
  Clear the aircraft at or above the MCA
  Reroute the aircraft

## Slide 34: Lesson Summary
This lesson covered:
Procedures for issuing altimeter settings
Requirements for altitude assignments
Phraseology for altitude assignments
Requirements for minimum altitudes

## Slide 35: The End