## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify:
Characteristics of an Instrument Approach Procedure (IAP) chart
Requirements for approaches
Procedures for approaches

## Slide 3: Definition
INSTRUMENT APPROACH PROCEDURE (IAP) - A series of predetermined maneuvers for the orderly transfer of an aircraft under instrument flight conditions from the beginning of the initial approach to a landing or to a point from which a landing may be made visually. It is prescribed and approved for a specific airport by competent authority.
  IAP Types
  U.S. Civil Standard Instrument Approach
  U.S. Military Standard Instrument Approach
  Special Instrument Approach

## Slide 4: IAP Types
U.S. Civil Standard Instrument Approach Procedure:
  Instrument approach procedure that is approved by the FAA as prescribed under 14 CFR Part 97 and are available for public use

## Slide 5: IAP Types (Cont'd)
U.S. Military Standard Instrument Approach Procedure:
  Instrument approach procedure that is approved and published by the Department of Defense (DOD)

## Slide 6: IAP Types (Cont'd)
Special Instrument Approach Procedure:
  Approved by the FAA for individual operators
  Is not published for public use
    Pilots planning flights to locations served by special instrument approach procedures should obtain advance approval from the owner of the procedure
  Some special instrument approach procedures:
    Require certain crew qualification training in order to execute the approach
    Are based on privately owned NAVAIDS

## Slide 7: Definitions
PRECISION APPROACH PROCEDURE - A standard instrument approach procedure in which an electronic glideslope or other type of glidepath is provided.
NONPRECISION APPROACH PROCEDURE -
  A standard instrument approach procedure in which no electronic glideslope is provided.
APPROACH WITH VERTICAL GUIDANCE (APV) -
  RNAV approach procedures that provide lateral and vertical guidance, but do not meet the requirements to be considered a precision approach.

## Slide 8: Knowledge Check
Which type of instrument approach procedure is approved by the FAA for individual operators?
  U.S. Civil Standard
  U.S. Military Standard
  Special

## Slide 9: Knowledge Check
Which type of approach has no electronic glideslope?
  Precision Approach
  Nonprecision Approach
  Instrument Landing System (ILS)

## Slide 10: IAP Chart Layout
Planview
Pilot Briefing Information
Profile Box
Missed Approach Icons
Minimums
Airport Sketch Box
Margin Information
Margin Information

## Slide 11: Margin Information
Top Margin
Bottom Margin
LOC I-SUS 110.55
APP CRS 079º
Rwy ldg 7414 TDZE 462 Apt Elev 463
AL-5400 (FAA)
ST. LOUIS, MISSOURI
Amdt 14B 29MAR18
ST. LOUIS, MISSOURI
ILS or LOC RWY 8R
ILS or LOC RWY 8R
38°40’N — 90°39’W
SPIRIT OF ST. LOUIS (SUS)
SPIRIT OF ST. LOUIS (SUS)
City and State
Reference Number and Approving Authority
Procedure Name
Procedure Name
Airport Name
Airport Identifier
Procedure Version
Airport Coordinates
City and State

## Slide 12: Pilot Briefing Information
ST. LOUIS APP CON 126.5 254.3
CLNC DEL 133.1
ST. LOUIS RADIO 122.95
SPIRIT TOWER 124.75 (CTAF) 257.2
MISSED APPROACH: Climb to 1500 then climbing left turn to 2400 direct FTZ VORTAC and hold.
LOC I-SUS 110.55
APP CRS 079º
Rwy ldg 7414 TDZE 462 Apt Elev 463
Primary NAVAID Information
Approach Course
Notes And Limitations
Full Text Description Of Missed Approach
A
A
5
Touchdown Zone and Airport Elevations
Available Landing Distance
MALSR
Approach Lighting
ATIS 134.8
GND CON 121.7
ST. LOUIS CLNC DEL 121.7 (when tower closed)
Icons indicating any nonstandard alternate and/or takeoff minimums
Frequencies - Listed In Normal Order Of Use
When local altimeter not received, use St Louis Lambert Intl altimeter setting…

## Slide 13: Planview
10 NM
MM
2300
3100
043°
MSA SU 25 NM
253°
ST. LOUIS
117.4 STL
Chan 121
…
. ..
2400 224° (18.8)
1070
751
759
..
SNOOP
326 SU
…
LOM/IAF
RADAR
682
708
992
925
1128
970
2400 186° (15.8)
SADEN
1251
100°
280°
R-280
2400 NoPT to LOM 143° (5.5)
R-143
259°
079°
214°
034°
NAVAID
River
Distance Circle - 10 NM
Locator Outer Marker
Approach NAVAID
Runways
Missed Approach
Procedure Turn
Obstruction (MSL)
Localizer
Inbound Course
Outbound Radial
Transition Route
IAF
FORISTELL
110.8 FTZ
Chan 45
.. .
..
…
..
…
LOCALIZER 110.55
I-SUS
..
Minimum Safe Altitude
Navigation Frequency Information
Holding Pattern
Mileage Information
Altitude Information
IAP Notes Area

## Slide 14: Minimum Safe Altitude (MSA)
Minimum Altitude in the Northern Portion of the Area
Minimum Altitude in the Southern Portion of the Area

## Slide 15: Terminal Arrival Area (TAA)
STRAIGHT-IN AREA
Right Base Area
Left Base Area
30NM Radius Centered on the Initial Approach Fix
Altitudes Provide at Least 1,000’ Obstacle Clearance

## Slide 16: Airport Sketch Box
ELEV 463
Rwy 8R ldg 7245’
HIRL Rwy 8R-26L
L
FAF to MAP 5.2 NM
Knots
60
90
120
150
180
Min:Sec
5:12
3:28
2:36
2:05
1:44
Airport Elevation
Touchdown Zone Elevation
Runway Lighting Aids Available
FAF Distance
Time/Speed Table
Rwy 26L ldg 7004’
MIRL Rwy 8L-26R
L
5000 x 75
P
8L
from FAF
5.2 NM
076°
8R
26L
7485 x 150
V
V
TDZE 462
747
624
A
5
26R
A
5
581
Approach Lighting Symbols
Obstructions
V
Displaced Threshold
Notes

## Slide 17: Missed Approach
1500
2400
FTZ
Climb Straight Ahead to 1500
Followed by a Climbing Left Turn to 2400
Then Direct FTZ
MISSED APPROACH: Climb to 1500 then climbing left turn to 2400 direct FTZ VORTAC and hold.
Textual Description
Icons

## Slide 18: Profile View - Precision Approach
Remain
within 10 NM
2400
GS 3.00°
TCH 55
2400
SU LOM
RADAR
2185
259°
MM
079°
4.7 NM
0.5
Glideslope Angle
Glideslope Intercept Altitude
Glideslope
Missed Approach Track
Procedure Turn Completion Altitude
Glideslope Altitude At LOM
Final Approach Fix
Course
1500
2400
FTZ

## Slide 19: Knowledge Check
On an approach chart, what does an altitude without horizontal lines above or below the numbers indicate?
  Minimum altitude
  Mandatory altitude
  Recommended altitude

## Slide 20: Knowledge Check
Where can symbols used on an IAP chart be found within U.S. Terminal Procedures Publications?
  Legend
  Margin
  Profile View

## Slide 21
Remain
within 10 NM
2400
2400
LOM
259°
5.2 NM
079°
Minimum Altitude Over FAF
Missed Approach Point
Missed Approach Track
1500
2400
FTZ
3.46°
TCH 45
Visual Descent Angle
079°
Maximum Distance Of Procedure Turn From LOM
Profile View - Nonprecision Approach

## Slide 22: Landing Minimums
The landing minimums section describes:
  The lowest altitude to which the approaching aircraft may descend in IFR conditions before the missed approach procedure must be executed
  The lowest visibility needed to execute the approach procedure
    Visibility may be in statute miles or hundreds of feet

## Slide 23: Precision Minimums Section
CATEGORY
A
B
C
D
S-ILS 8R
S-LOC 8R
CIRCLING
1100-1
880/24 418 (500-½)
662/24 200 (200-½)
880/40 418 (500-3/4)
1120-1¾
657 (700-1¾)
1140-2¼
677 (700-2¼)
637 (700-1)
Aircraft Categories
Decision Height
Visibility
Height of DH Above Touchdown Zone [AGL]
Military Minimums
Minimum Descent Altitude (MDA)
Height of MDA Above Touchdown Zone [AGL]
Height of MDA Above Airport [AGL]
Approach Procedure Variations

## Slide 24: Nonprecision Minimums Section
CATEGORY
A
B
C
D
S-12R
CIRCLING
1100-1 529 (600-1)
1100-1 540 (600-1)
1100-1½
529 (600-1½)
1140-2
569 (600-2)
1100-1¼
540 (600-1¼)
S-12R
CIRCLING
1000-1
429 (500-1)
940-1 380 (400-1)
1040-1½
469 (500-1½)
1140-2
569 (600-2)
Aircraft Categories
Approach Procedure Variations
Variations Of Approach Procedure (With Specific Airborne Equipment Required)
Minimum Descent Altitude
Height of MDA Above Touchdown Zone [AGL]
Visibility
Circling MDA
Height of MDA Above Airport [AGL]
DUAL VOR OR VOR/DME MINIMA
1040-1
469 (500-1)

## Slide 25: Knowledge Check
CATEGORY
A
B
C
D
S-ILS 29
S-LOC 29
CIRCLING
1340-1 465 (500-1)
1300/24 429 (500-½)
1071/24 200 (200-½)
1300/40
429 (500-¾)
1300/50
429(500-1)
1340- 1½
465 (500-1½)
1520-2
645 (700-2)
For a category B civilian aircraft, what is the DH for a straight-in ILS runway 29 approach?
  200’
  1,071’
  2,400’

## Slide 26: Knowledge Check
Controllers are responsible for determining that landing minimums exist prior to allowing an aircraft to execute an approach.
  True
  False

## Slide 27: Knowledge Check
What is the altitude for a precision approach at which a missed approach must be initiated if the required visual reference to continue the approach has not been established?
  Minimum Descent Altitude (MDA)
  Decision Height (DH)
  Height Above Airport (HAA)

## Slide 28: Approach Clearance
APPROACH CLEARANCE - Authorization by ATC for a pilot to conduct an instrument approach.
Issue an approach clearance only after the preceding aircraft has landed or cancelled IFR, except when applying:
  Radar procedure
  Timed or visual approaches

## Slide 29
“LEAR FOUR SEVEN PAPA LIMA CLEARED APPROACH, CONTACT SEMINOLE TOWER ONE ONE EIGHT POINT TWO PROCEDURE TURN.”
N47PL
LJ24/L
T450 G450
02
131 03
KSRE
20
15
OKC
1509
130
APCH
1513
APCH
20
3737
CTL
KOKC OKC KSRE
CPT
Pilot’s Choice of Approach
  FSS Location
  VFR Tower Location
N55LW
C421/G
T220 G228
02
131 01
KMIO
KICT V350 CNU OSW KMIO
10
17
OSW
1700
150
1720
APCH
1707
APCH
23NW/1707
10
3737
S
180
CPT
“NOVEMBER FIVE FIVE LIMA WHISKEY, CLEARED APPROACH MIAMI AIRPORT, CONTACT MIAMI RADIO PROCEDURE TURN.”

## Slide 30
RCH215
H/C17/L
T420 G454
02
421 03
KCQB
KOKC OKC V14 TOTES KCQB/1625
30
16
OKC
1605
90
APCH
1620
APCH
“REACH TWO ONE FIVE CLEARED:
V-O-R APPROACH.”
I-L-S RUNWAY THREE SIX APPROACH.”
TACAN APPROACH.”
A-D-F APPROACH.”
R-NAV APPROACH.”
30
5526
30W/1620
Phraseology for Various Types of Approaches

## Slide 31: Communications Release
If an IFR aircraft intends to land at an airport not served by a tower or FSS, approve a change to advisory frequency when you no longer require direct communications
  Permits the aircraft to receive timely local airport traffic information

## Slide 32: Aircraft on an Unpublished Route
V40
ABC
V23
V68
4,000’ PEAK
N1 @ 10,000’
APPROACH
PROCEDURE

## Slide 33: GPS Testing and Anomalies
When GPS TESTING NOTAMS are published and testing is actually occurring:
  Inform pilots requesting or cleared for a RNAV approach that GPS may not be available and request intentions
  Do not resume RNAV approach operations until certain that GPS interference is no longer a factor or such GPS testing exercise has ceased

## Slide 34: Altitude Assignment
Specify altitude in the approach procedure when necessary for separation
  Example:
  “MAINTAINED FOUR THOUSAND UNTIL ESTABLISHED ON THE LOCALIZER”

## Slide 35: Knowledge Check
What is the phraseology to release an aircraft to change to advisory frequency?
  “CHANGE TO ADVISORY FREQUENCY APPROVED”
  “CHANGE TO ADVISORY FREQUENCY”
  “CHANGE TO ADVISORY”

## Slide 36: Knowledge Check
What is the phraseology for giving a pilot the choice of which approach to fly?
  “…CLEARED FOR ANY APPROACH”
  “…CLEARED PILOT’S CHOICE”
  “…CLEARED APPROACH”

## Slide 37: Approach Information
Provide current approach information to aircraft at airports for which you provide approach control services
Include the following information, if needed:
  Approach clearance or type of approach to expect
  Runway
  Surface wind
  Ceiling and visibility
  Altimeter for destination airport

## Slide 38: Pilot Unfamiliar with Approach
Specify the following in the approach clearance if the pilot is unfamiliar with the procedure:
  Initial approach altitude
  Direction and distance from the holding fix within which procedure turn is to be completed
  Altitude at which the procedure turn is to be made
  Final approach course and altitude
  Missed approach procedures if considered necessary

## Slide 39: Contact Approach
Requirements:
  Must be requested by pilot
  Reported ground visibility must be at least one statute mile
  Standard or Special IAP must be published and functioning for airport
  Approved separation must be applied between other IFR or Special VFR aircraft
  Issue alternative clearance when weather conditions are such that a contact approach may be impracticable

## Slide 40: Visual Approach
An approach conducted on an IFR flight plan that authorizes the pilot to proceed visually and clear of clouds to the airport
Pilot must, at all times, have either the airport or the preceding aircraft in sight
Must be authorized and under the control of the appropriate air traffic control facility
Reported weather at the airport must be VFR

## Slide 41: Unsuccessful Visual Approach
Visual Approach is not an Instrument Approach Procedure
No missed approach segment
If aircraft is unable to complete visual approach:
  Aircraft should overfly the runway while climbing to traffic pattern altitude and enter the traffic pattern via the crosswind leg (i.e., go around)
  ATC must maintain applicable IFR separation

## Slide 42: Vectoring for Visual Approach
Radar controllers may vector aircraft for a visual approach at airports
  With weather reporting service, if:
    Ceiling is at least 500’ above Minimum Vectoring Altitude/ Minimum IFR Altitude (MVA/MIA); and
    Visibility is 3 miles or greater
Without weather reporting service, if:
  There is reasonable assurance (e.g., area weather reports, PIREPs, etc.) descent and flight to airport can be made visually, and
  Pilot informed weather information not available

## Slide 43: Visual Approach Procedures
Controller may initiate, or pilot may request, a visual approach even when being vectored for an instrument approach and the pilot subsequently reports:
  Airport in sight at airports without a control tower
  Airport or runway in sight at airports with operating control towers
ARTCC
“November Four Two FOUR VICTOR, cleared visual approach.”
“Which one?”
Jekyl Island
St. Simons Island
Visual Approach: Airports in Close Proximity

## Slide 44: Visual Approach: Pilot Responsibilities
Advise ATC if a visual approach is not desired
Proceed to the airport in a normal manner or follow designated traffic
Remain VFR at all times
Maintain a safe landing interval behind preceding traffic
Accept responsibility for wake turbulence separation
Contact ATC as soon as possible if unable to land
Advise ATC if unable to:
  Continue following designated traffic
  Remain in VFR conditions

## Slide 45: Knowledge Check
An aircraft unable to complete a visual approach should do what?
  Overfly the runway while climbing to MSA and attempt another visual approach
  Overfly the runway while climbing to last assigned altitude and request further routing
  Overfly the runway while climbing to traffic pattern altitude and enter the traffic pattern via the crosswind leg

## Slide 46: Knowledge Check
Which statement is not true of a contact approach?
  Reported ground visibility must be at least one statute mile
  Controller may initiate or pilot may request
  Standard or Special IAP must be published and functioning for airport

## Slide 47: Timed Approaches
Glide
Path
NO. 3
LOM
LMM
NO. 2
NO. 1 Aircraft Passed LOM @ 1000
5 Miles
Approximately
NO. 3 Aircraft Will Depart The LOM @ 1004
NO. 2 Aircraft Passed LOM @ 1002

## Slide 48: Timed Approaches (Cont'd)
Interval Minima
  Use 2 minute or a 5 mile radar interval as the minimum between successive approaches
Wake Turbulence Interval Minima
  Heavy behind Super - 3 minutes or 6 miles
  Large behind Super - 3 minutes or 7 miles
  Small behind Super - 4 minutes or 8 miles
  Small behind Heavy - 3 minutes or 6 miles

## Slide 49: Example - Timed ILS Approaches
Timed approaches using an ILS and applying longitudinal separation only
Using an interval of two minutes, #1 and #2 aircraft have already passed the LOM on final approach.
Profile View
Top-down View
#3 aircraft has been cleared for approach and to depart LOM two minutes after #2 aircraft reported leaving LOM inbound on final approach.

## Slide 50: Example - Timed NDB Approaches
Timed approaches using a bearing of an NDB and longitudinal and vertical separation
#1 aircraft sighted by tower, enabling approach clearance to #2 aircraft at point A.
#2 aircraft departed fix inbound at designated time, maintaining 2,000’ until cleared for approach at point A
#3 aircraft instructed to descend to 2,000’ after #2 aircraft reported departing fix inbound and leaving 2,000’ at point A.

## Slide 51: Timed Approaches - Missed Approach
Missed Approach: FAR VOR/DME
Alternate Missed Approach: KENIE LOM
ILS or LOC RWY 18
FARGO (KFAR)

## Slide 52: Knowledge Check
What type of facility must service an airport in order to use timed approaches?
  Tower
  Flight service station
  Approach control

## Slide 53: Knowledge Check
If an alternative missed approach procedure is not available and weather conditions are less than required, clear the succeeding aircraft for an approach when the preceding aircraft has_________ .
  Landed or canceled its IFR flight plan
  Passed the final approach fix inbound
  Passed the outer marker on the approach

## Slide 54: Knowledge Check
When conducting timed approaches, what must be issued before specifying a time to leave the initial approach fix inbound?
  An Expect Further Clearance (EFC) time
  Altitude restriction
  Time check

## Slide 55: Cancellation of IFR Flight Plan
If arriving at an airport not served by a tower or FSS, instruct pilot how to cancel IFR flight plan before instructing pilot to change to the Common Traffic Advisory Frequency (CTAF)

## Slide 56: Frequency Changes for Military Aircraft
Military single piloted turbojet aircraft conducting an approach wholly, or partly in IFR conditions, or at night:
  Avoid frequency and radar beacon code changes to the maximum extent that communications capabilities and traffic will permit

## Slide 57: Circling Approach
May only be given for aircraft landing at airports with operational control towers
Include in the approach clearance instructions to circle to the runway in use if landing will be made on a runway other than that aligned with the direction of instrument approach
  CIRCLE TO RUNWAY (number)

## Slide 58: Missed Approach
An approach clearance automatically authorizes the aircraft to execute the missed approach procedure depicted for the instrument approach being flown
An alternate missed approach procedure as published may be assigned when necessary

## Slide 59: Practice Approach
Ensure that neither VFR nor IFR practice approaches disrupt the flow of other arriving and departing IFR or VFR aircraft
  EXCEPTION: Military aircraft operating at military airfields
Authorize, withdraw authorization, or refuse to authorize practice approaches as traffic conditions require
  Approaches in progress should not be terminated

## Slide 60: Practice Approach Separation
Apply approved IFR separation minima to:
  IFR aircraft practicing instrument approaches until
    The aircraft lands and flight is terminated, or
    Pilot cancels flight plan
  VFR aircraft practicing instrument approaches where procedures require application of IFR separation

## Slide 61: Practice Approach: Missed Approach
IFR aircraft are automatically authorized to execute missed approach depicted for instrument approach being shown
  Unless alternative instructions have been issued
VFR aircraft are NOT automatically authorized to execute missed approach procedure

## Slide 62: Knowledge Check
Which is true of circling approaches?
  May only be given for aircraft landing at airports with operational control towers
  May only be given at airports with operational control towers or Flight Service Stations
  May be given at any airport

## Slide 63: Knowledge Check
When is approved IFR separation minima applied to IFR aircraft practicing approaches?
  Never
  Until the aircraft lands and flight is terminated
  Until the VFR tower gets the aircraft in sight

## Slide 64: Lesson Summary
This lesson covered:
Characteristics of an Instrument Approach Procedure (IAP) chart
Requirements for approaches
Procedures for approaches

## Slide 65: The End