## Slide 2
Requirements for forwarding control information
Procedures for forwarding control information

## Slide 3: Flight Plans
Record flight plan information
  Use authorized abbreviations when possible
Flight plans filed directly with the center:
  Record all items given by the pilot either on a flight progress strip or flight data entry, or voice recorder
  If a voice recorder is used
    Enter in block 26 of the flight progress strip the sector or position number to identify where the information may be found in the event search and rescue (SAR) activities become necessary

## Slide 4: Flight Plans (Cont’d)
Except during EAS FDP operation, forward the flight plan information to the appropriate ATC facility, FSS, or BASOPS
During EAS FDP operation, the above manual actions are required in cases where the data is not forwarded automatically by the computer
Forward proposed tower en route flight plans and any related amendments to the appropriate departure terminal facility

## Slide 5: IFR Flight Progress Data
Forward control information from controller to controller within a facility, then to the receiving facility as the aircraft progresses along its route
  Use computer equipment in lieu of manual coordination procedures
    When appropriate, use voice communication
    Do not use the remarks section of flight progress strips to pass control information

## Slide 6: IFR Flight Progress Data (Cont’d)
Ensure that flight plan and control information are correct and up-to-date
Forward flight plan information at least 15 minutes before the aircraft is estimated to enter the receiving facility’s area
  When covered by a letter of agreement/facility directive, the time requirement may be reduced

## Slide 7: IFR Flight Progress Data (Cont’d)
Forward the following information:
Type of aircraft and equipment suffix,
number of aircraft if more than one,
heavy indicator “H/” (if appropriate)
Aircraft identification
Altitude at which aircraft will enter receiving facility’s area if other than assigned
Assigned altitude and ETA over last reporting point/fix in your sector
True airspeed
Point of departure and remaining route of flight
Destination airport, and clearance limit if other than destination airport
Requested altitude
ETA at destination airport
Longitudinal separation being used in nonradar operations between aircraft at the same altitude
Additional nonroutine information
Assigned Beacon Code

## Slide 8: Position Reports
Forward position reports over the last reporting point in the transferring facility’s area if any of the following conditions exist:
  Time differs by more than 3 minutes from estimate
  Requested by receiving facility
  Agreed to between facilities

## Slide 9: Knowledge Check
How many minutes must flight plan and control information precede an aircraft entering another facility's area?
  3
  10
  15

## Slide 10: Knowledge Check
Which block of the flight progress strip is used to record sector numbers for flight plan information saved on voice recorders?
  24
  26
  28

## Slide 11: Knowledge Check
If the coordinated estimate time differs by more than __ minutes from the actual position report, you are required to forward the new time.
  2
  3
  4

## Slide 12: Error in Transmission
The Unsuccessful Transmission Message (UTM) provides notification that a flight plan related message transmission is unsuccessful due to a hardware error or no response condition

## Slide 13: Amended Data or Unsuccessful Transmission Message
Forward any amended data concerning previously forwarded flight plans
  IFR Flight Progress Data, need only be forwarded when the time differs by more than 3 minutes from the estimate given
  Revisions to ETA information
    Not required for military or scheduled air carrier aircraft

## Slide 14: Amended Data or Unsuccessful Transmission Message (Cont’d)
Computer acceptance fulfills requirement for sending amended data
Forward amended control information and record action on flight progress strip

## Slide 15: Arrival Information - Approach Controls
Forward the following information:
Type of aircraft, aircraft equipment suffix
Aircraft identification
Clearance limit if other than destination airport
Control transfer point
“YOUR CONTROL LEAVING ONE ZERO THOUSAND”
ETA and altitude over clearance limit

## Slide 16: Arrival Information - Nonapproach Control Towers/FSSs
Forward the following information:
Type of aircraft
Aircraft identification
Type of instrument approach procedure the aircraft will execute
ETA

## Slide 17: Time Parameters
Coordinate with nonapproach control tower:
  Before issuing a clearance within a surface area for which the tower has responsibility
    Unless otherwise specified in a letter of agreement
  For transit authorization when you are providing radar traffic advisory service to an aircraft that will enter another facility’s airspace

## Slide 18: Communications Transfer
Transfer radio communications and control responsibility:
  Early enough to allow the receiving facility to clear an aircraft beyond the clearance limit before the aircraft reaches it
  Prior to operation within a surface area for which the tower has responsibility

## Slide 19: Strip Marking
Indicate coordination by circling altitude and time in red

## Slide 20: Altitude Reservations (ALTRV)
Forward only those items necessary to properly:
  Identify the flight
  Update flight data, or
  Revise previously given information
Forward departure times of ALTRV aircraft
In a nonradar environment
  Pilot must advise if fix timing will be more than plus or minus 5 minutes from the planned ALTRV estimate

## Slide 21: Military Flight Plan Coordination
Forward to FSSs the following information:
  Change in destination, including:
    Aircraft identification and type
    Departure point
    Original and new destinations
    Position and time
    ETE
    Remarks including change in fuel exhaustion time
  Revised ETA
  Change in fuel exhaustion time
  New IFR flight plans and VFR flight plans that change to IFR

## Slide 22: Knowledge Check
When should communications transfer take place for operations within a surface area controlled by a tower?
  Prior to entering the surface area
  Once the aircraft reports inside the surface area
  Only if requested by the controlling facility

## Slide 23: Knowledge Check
Why must changes to military flight plans be coordinated with FSS?
  To ensure proper terrain separation
  FSS will brief the pilots about possible weather along the new route of flight
  Makes current information available for use by centers in the event of two-way radio communications failure

## Slide 24: Knowledge Check
When must a pilot in an Altitude Reservation (ALTRV) flying in nonradar environments notify you of fix time changes?
  If fix times differ by more than 5 minutes
  When requested by the controller
  Anytime fix times change more then 3 minutes

## Slide 25: Knowledge Check
How would you indicate the data on a flight strip was forwarded?
  Underline the data
  Circle the data in red
  Draw a red box around the data

## Slide 26: Knowledge Check
When should communication transfer take place if a flight has a short-range clearance limit?
  Early enough to allow the facility to clear the aircraft beyond the clearance limit before the aircraft reaches it
  After one turn in the hold and established on the inbound leg
  Once the pilot reports established safely at the clearance limit

## Slide 27: Knowledge Check
A.
B.
C.
What is the coding for an Unsuccessful Transmission Message (UTM)?

## Slide 28
Requirements for forwarding control information
Procedures for forwarding control information