## Slide 2
Pilot procedures for a communications failure
Unmanned Aircraft Systems (UAS) lost link procedures
ATC procedures for a communications failure

## Slide 3: Pilot Procedures
If a communications failure occurs in VFR conditions, or if VFR conditions are encountered after the failure, the pilot must continue under VFR and land as soon as practicable
It is not intended that the requirements to land as soon as practicable be construed to mean as soon as possible. Pilots retain the prerogative of exercising their best judgement

## Slide 4
If a communications failure occurs in VFR conditions, the pilot must:
  Continue the flight under VFR conditions
  Squawk Code 7600
  Land as soon as practicable
IFR Aircraft In VFR Conditions

## Slide 5
If a communications failure occurs in IFR conditions, the pilot must continue the flight according to the following:
  Last route assigned
  On a radar vector:
    Direct route to the fix, route, or airway specified
  No assigned route:
    Route in EFC
  No assigned route or EFC:
    Route filed in the flight plan
IFR Conditions - Route

## Slide 6
A pilot who experiences communications failure must maintain the highest of the following altitudes for the route segment being flown:
  Altitude assigned in the last ATC clearance
  Minimum altitude for IFR operations
  Altitude ATC has advised may be expected in an EFC
IFR Conditions - Altitude

## Slide 7
If an EFC with a higher or lower altitude has been received:
  Maintain the highest of the following until time or fix:
    Last assigned altitude, or
    Minimum altitude for IFR operations
  Upon reaching the time or fix, commence climb or descent to altitude advised to expect
  If failure occurs after the time or fix, the altitude to be expected is not applicable
IFR Conditions - Altitude (Cont’d)

## Slide 8: Depart Clearance Limit
If clearance limit is a fix from which an approach begins:
  Commence descent and approach as close as possible to the EFC time
  If no EFC time, commence descent and approach as close as possible to the Estimated Time of Arrival (ETA)

## Slide 9: Depart Clearance Limit (Cont’d)
If clearance limit is not a fix from which an approach begins:
  Depart clearance limit at EFC time
    Proceed to a fix from which an approach begins
    Commence descent and approach as close as possible to ETA
  If no EFC time, depart clearance limit upon arrival over clearance limit
    Proceed to a fix from which an approach begins
    Commence descent and approach as close as possible to ETA

## Slide 10: IFR COM Failure - NAVAID Voice
The pilot should monitor the NAVAID voice feature, then attempt to reestablish communications:
  On previously assigned frequency, or
  With an FSS

## Slide 11: Reestablishing Communications
Contact ATC on the previously assigned frequency
Contact an FSS
  Advise radio communications have been lost
  Request further clearance from the controlling facility
Monitor 121.5/243.0 Mhz
Use any other means of communications, e.g., contract datalink service provider

## Slide 12: Knowledge Check
What is one method of issuing a clearance to an aircraft when two-way communications have been lost?
  Use NAVAID text feature
  Issue clearances through Search and Rescue
  Use NAVAID voice feature

## Slide 13: Knowledge Check
N482W
BE20/G
T275
08
FJS
KSAC SAC V23 BTG
KVUO
EFC V495 BTG
F
160
OED
RBL
1649
17
08
6335
N482W was cleared to FJS and advised to expect further clearance via the routing indicated. If communications failure occurs, what action should the pilot take?
  Hold indefinitely at FJS
  Proceed to BTG via V23
  Proceed to BTG via FJS V495

## Slide 14: Knowledge Check
N15M
BE36/G
T160
1502
KRDD P1500
KRDD RBL V332 HNW
KJAQ
D-A
70
PNC
70
4566
N15M experienced a communications failure after departing from KRDD on an IFR flight plan. The aircraft reached VMC at 7,000 feet. What should the pilot do?
  Descend in IFR conditions and land at KRDD
  Continue in VMC conditions and land as soon as practicable
  Maintain 7,000’ to KJAQ

## Slide 15: Knowledge Check
N13P experienced communications failure. At what time will the pilot commence an approach?
  1328Z
  1321Z
  1323Z
N31P
BE36/L
T160
13
KRDD
KSAC V23 RBL KRDD
NE
1328
RBL
1304
21
60
23
H
4314

## Slide 16: UAS Lost Link
When you observe LLNK, do the following:
  Determine lost link procedure, as outlined in Special Airworthiness Certificate or Certificate of Waiver or Authorization (COA)
  Coordinate, as required, to allow UAS to execute lost link procedure
  Advise supervisor/CIC, when feasible, so event can be documented

## Slide 17: Global Hawk Lost Link
Global Hawk aircraft may be unable to squawk 7400
If the aircraft is unable to squawk 7400, it will squawk 7600
ATC must apply the same procedures whether 7400 or 7600 is squawked

## Slide 18: Knowledge Check
What code may be displayed by unmanned aircraft systems (UAS) when the control link between the aircraft and the pilot is lost?
  7300
  7400
  7700

## Slide 19: Unacknowledged Clearances - Controller Actions
When a clearance has been issued, but not acknowledged by the pilot, you must protect:
  If an altitude was issued, all altitudes between the previously cleared, and the newly issued altitudes
  If a route was issued, the previously cleared, and newly issued routes
Verbally coordinate with any controllers on the route of flight, that the clearance was not acknowledged

## Slide 20: Reestablish Communications
Attempt to reestablish communications using:
  Emergency frequencies
  NAVAIDs with voice capability
  Flight Service Station (FSS)
  Datalink service provider
  Aircraft Communications Addressing and Reporting System (ACARS)
  Selective calling

## Slide 21: Receiver Only Aircraft Acknowledgement
If one way communications are established, have the aircraft do any of the following to acknowledge a clearance:
  IDENT
  Squawk Code 7600
  Squawk STANDBY
  Issue turns

## Slide 22: Suspicious Activity Coordination
If communications have not been (re)established after 5 minutes:
  Consider the aircraft’s or pilot’s activity to be suspicious
  Report it to your supervisor/CIC

## Slide 23: Overdue Aircraft - Traffic Restrictions
Suspend IFR traffic for 30 minutes from:
  Time approach clearance issued
  EFC
  Arrival time at NAVAID serving destination airport
  Release time or clearance void time
  Current estimate, (controller’s or pilot’s), whichever is later, at:
    Appropriate en route NAVAID or fix
    NAVAID serving the destination airport

## Slide 24: Overdue Aircraft - Lighting Requirements
At nontower or non-FSS locations, request airport management to light all:
  Runway lights
  Approach lights
  Other required airport lighting systems
Lighting requirements begin
  30 minutes before the ETA of the aircraft
Lighting requirements end
  When aircraft has been located, or
  30 minutes after its fuel supply is estimated to be exhausted

## Slide 25: Overdue Aircraft - Traffic Resumption
Resume airport operations after a 30 minute suspension, with other pilots or aircraft operators concurrence
Concurrence must be maintained for 30 minutes after the suspension period has expired

## Slide 26: Knowledge Check
An en route aircraft is maintaining FL290 and requests to climb to FL330. The clearance is issued, but the pilot does not acknowledge. What IFR altitude(s) must be blocked?
  FL290 only
  FL290-FL330
  FL330 only

## Slide 27: Knowledge Check
How long must airports lights be left on for an overdue aircraft?
  30 minutes past aircraft fuel exhaustion time
  3 hours past aircraft fuel exhaustion time
  6 hours past the aircraft ETA at destination airport

## Slide 28: Knowledge Check
When an aircraft is overdue, other IFR traffic shall be suspended or restricted for 30 minutes after the ________.
  Time that the approach clearance was delivered to the pilot
  Time the aircraft is located
  Estimated fuel exhaustion time

## Slide 29: Knowledge Check
If radio communications have not been (re)established with the aircraft after _____ minutes, consider the aircraft’s or pilot’s activity to be suspicious and report it to the supervisor/CIC.
  15
  20
  5

## Slide 30: Lesson Summary
This lesson covered:
Pilot procedures for a communications failure
UAS lost link procedures
ATC procedures for a communications failure