## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify the characteristics of:
Primary radar systems
Radar beacon systems
Digitized radar systems
Automatic Dependent Surveillance Broadcast (ADS-B) Systems
Area of Interest (AOI)

## Slide 3: Definitions
RADAR - A radio detection device which provides information on range, azimuth and/or elevation of objects
PRIMARY RADAR - A radar system which uses reflected radio signals
SECONDARY RADAR – A radar system in which a radio signal transmitted from a radar station initiates the transmission of a radio signal from another station (transponder)

## Slide 4: Primary Radar
Pulse
Pulse Echo
Slant Range
Primary Targets
Situation Display
Primary Target, good quality, not paired to a flight plan
Primary Target , not good quality, not paired to a flight plan
Primary Target paired to a flight plan

## Slide 5: Range
Slant Range
Radar Site*
Slant Range
Altitude
Range
* Radar Site symbols are locally adaptable
Situation Display

## Slide 6: Azimuth
Target On 310° Bearing
Reference Line
Target On 030° Bearing
270°
090°
180°
360°
310°
030°
Situation Display
+
+

## Slide 7
What is the term used for distance measured by radar, from directly below the aircraft to the radar antenna?
  Mileage
  Range
  Slant range

## Slide 8
What two items of information are furnished by primary radar?
  Altitude and distance
  Azimuth and altitude
  Azimuth and range

## Slide 9
Which is the term for the bearing of a target measured clockwise from a reference line?
  Azimuth
  Range
  Offset

## Slide 10: Radar Beacon System
Situation Display
Triggered Transponder Reply Pulse
Interrogator Pulse
Paired Limited Data Block
Unpaired Limited Data Block
Paired Limited Data Block Eligible for Reduced Separation

## Slide 11: Radar Beacon Modes
Modes 1 and 2 - Military use only
  Mode 1 provides 2 digit 5 bit mission code
  Mode 2 provides 4 digit octal unit code
Mode 3/A
  Used by ATC for target tracking and identification
  Provides a 4 digit octal identification code for the aircraft
Mode C
  Provides the aircraft’s altitude in 100’ increments and is usually combined with Mode 3/A
Mode S (Select)
  Transmits information about the aircraft to the Secondary Surveillance Radar (SSR) system, to TCAS receivers and to the ADS-B system

## Slide 12
What is the type of radar that relies on an interrogator pulse and return, not a reflected signal from the aircraft?
  Primary
  Secondary
  Digitized

## Slide 13: Digitized Radar System
Uses surveillance information from all sources
Combined with flight plan information in ERAM
Displays digital target symbol and data in alphanumeric form (data block)
Radar Antenna
Processor
Display

## Slide 14: Characteristics of Digitized Radar
Data Block and Target
  Visual altitude information
  Visual ground speed
  Conflict alert detection
  Minimum Safe Altitude Warning (MSAW)
  Flight plan modification (Trackball reroute)
  Automatic flight plan updating

## Slide 15: Characteristics of Digitized Radar (Cont’d)
Situation Display
  Uniform target and data size
  Uniform display intensity
  Automatic target tracking
  Automatic pairing of target with active flight plan
  Digitized weather
  Mode C Intruder function

## Slide 16: Factors Affecting Radar Data Display
Target Fades
Intermittent or weak targets caused by:
  Antenna tilt
  Terrain
  Weather
  Marginal radar coverage
Electronic Attack (EA) or Jamming
Interference with radar for military purposes
EA types:
  Electronic (Strobing)
  Chaff

## Slide 17: Automatic Dependent Surveillance Broadcast (ADS-B)
  A surveillance system in which an aircraft to be detected is fitted with cooperative equipment in the form of a data link transmitter

## Slide 18: ADS-B System
SBSS
Radio Station
SBSS
Control Station
Radar
FAA Facilities

## Slide 19: ADS-B Link Options
SBSS
Radio Station
SBSS
Control Station
Radar
FAA Facilities

## Slide 20: ADS-B Broadcast Services
UAT & 1090ES
1090ES
UAT or
1090ES
Tx/Rx

## Slide 21: Area of Responsibility (AOR)

## Slide 22: Flight Planning Area of Interest (AOI)
Flight Planning AOI

## Slide 23: Aircraft Problem Detection Area
Aircraft Problem Detection Area

## Slide 24: Surveillance Area of Interest (AOI)
Surveillance AOI

## Slide 25: ERAM Adapted Boundary Areas
Flight Planning Area of Interest (AOI) - The area outside the center boundary where flight plan data is available from other ERAM facilities
Aircraft Problem Detection Area - The area inside the Flight Planning AOI that will receive Conflict Probe alerts. Includes information from the Flight Planning AOI
Surveillance AOI - Area where the controllers will see targets, safety alerts, and data blocks. Includes information from the Aircraft Problem Detection Area and the Flight Planning AOI

## Slide 26: Lesson Summary
This lesson covered:
Primary radar systems
Radar beacon systems
Digitized radar systems
Automatic Dependent Surveillance Broadcast (ADS-B) systems
Area of Interest (AOI)

## Slide 27: The End