## Slide 2
Radar symbols
Full Data Blocks (FDB)
Limited Data Blocks (LDB)
Display views
Weather displays
Miscellaneous displays

## Slide 3: Map Symbols
SYMBOL | Map Symbol Name
 | VOR
 | TACAN
 | Intersections and Waypoints
 | Major Airport
 | Satellite Airport
 | Emergency Airport
 | Obstruction

## Slide 4: Tracking and Pairing Definitions
TARGET
The indication shown on a display resulting from a primary radar return, a radar beacon reply, or an ADS-B report. The specific target symbol presented to ATC may vary based on the surveillance source and automation platform
TRACK
Information associated with surveillance reports, including position, and if available, Mode C altitude and beacon code
PAIRING
Association of flight data within track

## Slide 5: Tracking and Pairing
Paired FDB being tracked
Unpaired LDB being tracked
Coast track unpaired and not being tracked
DAL235
150N
227 CST
0520
016
AAL532
370C
342 410

## Slide 6: Target Symbols
AAL532
370C
342 410
SYMBOL | Target Symbol Name
 | Correlated primary
 | Reduced separation (3-mile)
 | Weak primary
 | Uncorrelated beacon
 | Correlated beacon
 | Uncorrelated primary
 | Identing beacon
 | VFR
 | Mode C Intruder (MCI)
Example target symbol

## Slide 7: Position Symbols
AAL532
370C
342 410
SYMBOL | Position Symbol Name
 | Coast Track
 | Flight Plan Aided Track (Flat track)
 | Free Track
 | Frozen Track
 | Hold Track
Example position symbol with
target symbol

## Slide 8: Velocity Vector Line
DAL235
150C
227 405

## Slide 9: Leader Line
Direction: QN d <FLID>
Length: QN /d <FLID>
Direction/Length: QN d/d <FLID>
DAL235
150C
227 405

## Slide 10: Distance Reference Indicator (Halo)
5 Mile
3 Mile

## Slide 11: Knowledge Check
Which map symbol is used to depict an obstruction?

## Slide 12: Knowledge Check
What type of Distance Reference Indicator is displayed when an aircraft is in a reduced separation area and the system is receiving radar from a preferred sensor?
A
C
B

## Slide 13: Knowledge Check
Which map symbol is used to depict an emergency airport?

## Slide 14: Full Data Block (FDB)
SWA212 310C 413 425 KLGA
R
Line 0
P
Line 1
Line 2
Line 3
Line 4
Column 0
Portal Fence
Data Area
Portal Area

## Slide 15: FDB Fields
SWA212 310 280 413 425 KLGA
R
P
Field A
Field C
Field E
Field F
(Fourth Line Data)
Field D
Field B

## Slide 16: FDB – Line 0
Proposed GIM-S Speed
Point Out Approved
Point Out Indicator

## Slide 17: Line 1
SWA212 310C 413 425 KLGA
R
P
X
Prefix Field
FDB Field A
SatComm Indicator
Suffix Field

## Slide 18
Line 1 Prefix Field

## Slide 19: Line 1 Field A
SWA212 310C 413 425 KLGA
R
P
X

## Slide 20: Line 1 SatComm Indicator
SWA212 310C 413 425 KLGA
R
X
P

## Slide 21: Line 1 CPDLC Indicator Suffix Field
SWA212 310C 413 425 KLGA
R
P
X
TOC In Progress Transfer
TOC Abnormal Transfer
Held TOC Single
Held TOC Multiple
Held TOC Abnormal

## Slide 22: Line 2 Field B1-B3
Altitude Uplink Indications
Assigned Altitude
VFR
OTP
ABV
SWA235
330C
532 405
N12345
ABV/135
532 205
Timeout
SWA235
330 310
532 405
Abnormal
SWA235
330 310
532 405
In Progress
SWA235
330 310
532 405
N12345
VFR/135
532 205
N12345
OTP/135
532 205

## Slide 23: Line 2 Field B4
Field B4 Examples
SWA235
330C
532 405
AAL532
160L200
225 350
DUDE32
220B220
222 300
N235A
200+208
202 275

## Slide 24: Line 2 Field C Special Coding
IC Mismatch
Single Altitude
IC Mismatch Block Altitude
Abnormal CAA
Controller Reported
Lost Mode C
Exceptional Vertical Rate
CAA

## Slide 25: Line 3 Field D
In Progress
Timeout
Abnormal
Route Uplink Indicators
XAPOH
370 296
413 450
KLGA
AAL002
370 296
413 450
KLGA
AAL003
330 296
413 450
KLGA

## Slide 26: Line 3 Field E
AAL002
370C
413EMRGKLGA
Code 7700
Field E Examples
Frozen
Handoff is failing
DAL005
370C
235FRZN
KLGA
SWA235
110C
413FAIL
KLGA
AAL802
370C
083 445 KJFK
DAL425
370C
268U455
KCLT
Locally Adapted Single Character Destination
Ground Speed

## Slide 27: Line 3 Field E (Cont’d)
Field E Data | Explanation
EMRG | 7700 beacon return - emergency code
HIJK | 7500 beacon return - hijack code
LLNK | 7400 beacon return - UAS lost link
RDOF | 7600 beacon return - radio communications failure
EFC | Expect Further Clearance (only if locally adapted)
FAIL | Handoff is failing
OLD | Crosstell track data has timed out (no track update messages)
MSAW | E-MSAW alert for an aircraft
MIFF | E-MSAW alert indefinitely suppressed
MOFF | E-MSAW alert is suppressed on a track for a specific alert

## Slide 28: Line 3 Field E (Cont’d)
Field E Data | Explanation
HUNK | Track is being transferred to an unknown (UNK) facility
OUNK | Track control transfer has been accepted by an unknown (UNK) facility
CST | Coast status
dddd | The beacon code received, if it is different from the facility assigned code
NONE | The track has an assigned beacon code, but a beacon code is not received
Ddd, CAS: (d)dd, MAS: Mdd | The ground speed (range 001 to 999). Accepted GIM-S speed
<code> | Temporarily displays the primary beacon code when an alert condition (e.g., 7700) is causing a special beacon code to be displayed
FRZN | Frozen status
SIDE | A side stream, ERAM to ERAM handoff
PLAN | A multiple FP condition exists for an aircraft which needs to be manually resolved
DATA | An interfacility handoff does not have complete radar data for the flight and a paired track is not established

## Slide 29: Line 3 Field E (Cont’d)
Field E Data | Explanation
H-dd, O-dd, K-dd | Transferred to sector dd intracenter
HLdd, OLdd, KLdd | Transferred intercenter or from a STARS facility. L will contain the receiving center’s one letter designator, and dd will contain the two digit ID of the receiving sector.
HLLL, OLLL | Transferred to a STARS facility where LLL is the facility identifier
HL | Intercenter, automatically or manually transferred with sector 00 entered
HLdL, OLdL, KLdL | Intercenter or from a STARS facility. L will contain the receiving center’s one letter designator, and dd will contain the two-digit ID of the receiving sector.
HLLdL, OLLdL | Transferred to a specific position dL in a STARS facility (first L)
HLLx, OLLx, KLLx | Transferred to a position x in a STARS facility LL
LLdd | Host-Non-Host (HNH) qualified track is in crosstell status from an external STARS facility. The first L is the one letter, external STARS facility identifier, the second L will be the one letter receiving NAS center identifier, and dd will be the sector to which the handoff is routed.

## Slide 30: Line 3 Field E (Cont’d)
Display priority for timesharing items:
Handoff
Beacon data
MSAW
Interfacility supplemental data
Side stream handoff
Plan data display item
Hold and ground speed, or destination

## Slide 31: Line 3 Field E (Cont’d)
Flight Event List (FEL) Display Indicator
Displayed for:
  24-BIT MISMATCH
  DUPLICATE 24-BIT
  MULTIPLE CODES
  CALLSIGN MISMATCH
Heading or Speed or Free Form Text (HSF) Display or Suppress Indicator
Toggles heading, speed, free form text
DAL235
150C
227 436

## Slide 32: Line 4
Heading and/or Speed
SWA235
310C
532 405
H240 M75
Free Form Text
SWA235
310C
532 405
RQ/NEUTO
Aircraft Data
SWA235
310C
532 405
B738/L
Destination
SWA235
310C
532 405
KPHL
GIM-S Indicator
SWA235
310C
532 405
H240 M75
En Route Usage
SWA235
310C
532 405
D20L

## Slide 33: Column 0
SWA235
110C
532 305
SWA235
110C
532 305
SWA235
110C
532 305
R
SWA235
110C
532 305
Manual VCI
Auto VCI
Line 3
Line 2
Auto Handoff Inhibited Indicator (Caret ^)
Not Your Control Indicator

## Slide 34: Other FDB Indicators
N235KY
220C
325 205
N235KY
220C
325 205
A
T 28.3
0743 6
Non-ADS-B Indicator
Scheduled Time
of Arrival (STA)
Delay Countdown Time (DCT)
Continuous Range Readout (CRR)
TFM Reroute Indicator

## Slide 35: Knowledge Check
If automatic handoff has been inhibited, what character is displayed in column 0?
  ^
  #
  *

## Slide 36: Knowledge Check
What character would be displayed in Field B4 if an aircraft’s Mode C is unreliable or not being received?
  ABV
  X
  T

## Slide 37: Knowledge Check
When may a Portal Fence be displayed?
  It is only displayed when an aircraft is in handoff
  It is always displayed
  When there is at least one indicator eligible to be displayed in the Portal Area

## Slide 38: Limited Data Block (LDB)
Paired LDB
• ACID and altitude
N1532
201
Unpaired ADS-B LDB
• ACID and altitude
N235SK
201
Unpaired LDB
• Beacon code and altitude if known
Unpaired Beacon
1723
095
1537
EMRG
RDOF
3226
060
035
Unpaired Beacon No Mode C
VFR
Emergency
Radio Failure
Mode C Intruder

## Slide 39: Conflict Data Block
Tracked ﬂight in conﬂict with a Mode C intruder
  Same as first two lines of FDB
  Vertical Rate Indicator (VRI)
  Position symbol
  Intruder track number
  Velocity vector line
FDB elements
Position symbol
Velocity vector line
Intruder track number
VRI

## Slide 40: Knowledge Check
What type of data block is displayed when a tracked flight is in conflict with a Mode C Intruder?
  Range Data Block
  Mode C Intruder Data Block
  Conflict Data Block

## Slide 41: Practice Exercise
Purpose
  Interpret and record information displayed in ERAM data blocks
Materials
  Practice exercise from Lesson 4 handout
Directions
  Exercise consists of twelve data block examples
  Read the questions provided for each data block
  Write your answers in the spaces provided

## Slide 42
Slide 1
SWA24
350C
348 482
B738/L
H
G
F
E
D
B&C
A

## Slide 43
Slide 2
N734DW
270 197
159 345
B350/G
H
G
F
E
D
B&C
A

## Slide 44
Slide 3
R
UAL561
250T227
157 415
A319/L
UAL561
250T227
1574521
A319/L
H
G
F
E
D
B&C
A

## Slide 45
Slide 4
SLAM24
250B260
311H-16
F15/I
SLAM24
250B260
311 510
F15/I
H
G
F
E
D
B&C
A

## Slide 46
Slide 5
R
N36TT
90 101
256 255
E55P/L
N36TT
90 101
256O-22
E55P/L
H
G
F
E
D
B&C
A

## Slide 47
Slide 6
R
N70KC
70-66
146 165
M20T/G
N70KC
70-66
146K-16
M20T/G
H
G
F
E
D
B&C
A

## Slide 48
Slide 7
N270L
110N
476 CST
PA31/G
H
G
F
E
D
B&C
A

## Slide 49
Slide 8
N54CR
110A
209FAIL
C421/G
N54CR
110A
209 256
C421/G
H
G
F
E
D
B&C
A

## Slide 50
Slide 9
AAL1106
250 350
203 390
H090 M.77
H
G
F
E
D
B&C
A

## Slide 51
Slide 10
DAL739
250+255
311 480
KORD
H
G
F
E
D
B&C
A

## Slide 52
Slide 11
N376CS
110 65#
309 124
C172/X
H
F
E
D
B&C
A
G

## Slide 53
Slide 12
LOBO32
125
LOBO32
110N130
448FRZN
A10/I
LOBO32
110N130
448O-47
A10/I
H
G
F
E
D
B&C
A

## Slide 54: Views Menu
View Menu button
View Title
View Close button
View
Menu Items
Tear-off
Scroll Bar
Example View
Toolbar

## Slide 55: Altimeter Settings View (ALTIM SET)
Station identifier
Observation time
Altimeter setting
Stale
Missing
Too old to use
Below 29.92
Tear-off

## Slide 56: Departure List View (DEPT)
Sublist title - Departure airport
Call sign
Requested altitude

## Slide 57: Auto Handoff Inhibit View (AUTO HO INHIB)
Enter: QA 20
Inhibits all automated handoffs to sector 20
Re-enter: QA 20
Enables all automated handoffs to sector 20
Facilities
Sectors

## Slide 58: Continuous Flight Plan Readout View (CFR)
Display a Flight Plan (FP):
QF <FLID>
QF SWA473

## Slide 59: Group Suppression View (GROUP SUP)
Flights of Group 01
Group Suppression ID
SubscribedSector IDs

## Slide 60: Beacon Code View (CODE)
System
Codes
Manually
Entered
Codes

## Slide 61: Hold View (HOLD)
CAT
Destination (DEST) or Alternate Airport (ALA)
Landing category
Expect Further Clearance time
Conflict
Block altitude
Holding fix
Present position
Runway
Visual Range
Aircraft ID
Non-RVSM indicator
Altitude

## Slide 62: Conflict Alert View (CONFLICT ALERT)
Controlling facility or sector
Suppression indicator
Distance between targets
Conflicting aircraft pairs
Suppress or request conflict alert:
CO <FLID>/<FLID>

## Slide 63: Inbound List View (INBND)
ACID
Altitude
Sublist Title (Fix)
Beacon Code

## Slide 64: CPDLC Message History View

## Slide 65: Meter Reference Point View (MRP)
Stream Name
Stream fix
GIM-S Accepted Speed
GIM-S Proposed Speed
Remove an aircraft from the list QP M <FLID>
Manually Swap MW <FLID> <FLID>
Resequence Aircraft SQ <FLID> <FLID>

## Slide 66: CPDLC Message Out View
Special Area
Normal Area

## Slide 67: Special Activity Airspace Filter View (SAA FILTER)
SAA FILTER
-
COLD HOT DISPLAY
BAL
BL
BAL
BL
BA
B
B
BLUE RIDGE SOARING
CHESSIE A
CHESSIE A1
CHESSIE B
CAPELLA TRACK
CHESSIE B1
SAA Display button
SAA Filter Setting
Tear-off buttons
SAA label

## Slide 68: Update Area View (UA)
Message Waiting Indicator

## Slide 69: Continuous Range Readout View (CRR)
M
CRR
-
ABBEY
UAL167
DAL352
N133A
GSG
SWA123
POT
UAL456
SWA235
Create a group:
LF //<FIX> (label)
Create a group and add aircraft:
LF //<FIX> (label) <CID>(/CID)(/CID)(/CID)
Add aircraft to a preexisting group:
LF <FIX or label> <CID>(/CID)(/CID)(/CID)
112.6
38.4
14.7
98.4
30.1
12.5
Group

## Slide 70: Weather Station Report View (WX)
Weather information
Weather station
Time of report

## Slide 71: Knowledge Check
How can you create a new CRR list and add aircraft to it in one command?
  LF //<FIX> (label)
  LF //<FIX> (label) <CID>(/CID)(/CID)(/CID)
  LF <FIX or label> <CID>(/CID)(/CID)(/CID)

## Slide 72: Knowledge Check
Which view is used to manage conflict alert suppression groups and manipulate group suppression information?
  GROUP SUP
  CA
  CA GRP SUP

## Slide 73: Knowledge Check
In the beacon code view, what does a “.” after a code indicate?
  System generated code
  Manually entered code
  Unusable code

## Slide 74: Weather Displays
NEXRAD Weather
ATC Weather
(Blue)
Moderate
(Blue-Cyan)
Heavy
(Cyan)
Extreme
Moderate
Precipitation
Heavy to
Extreme
Precipitation
Combination
of above

## Slide 75: Knowledge Check
How is heavy precipitation depicted on a NEXRAD weather display?
  Checkered red
  Checkered blue-cyan
  Green Hs

## Slide 76: Outage View Button
BUTTON | Definition
 | No outages, view suppressed
 | Unacknowledged outage changes, view suppressed
 | Critical outage, red coding has precedence over yellow coding and will display when both types of outages exist
 | View displayed
 | Acknowledged outage exists, view suppressed

## Slide 77: Outage View
Unacknowledged critical outage
Unacknowledged normal outage
Outage that has been returned to service
FLIGHT DATA DOWN
ABC/BCN OTS
TYR/BCN OTS
NEXRAD UP
Acknowledged normal outage
OUTAGE12

## Slide 78: OLD Coding

## Slide 79: Status View (STATUS)
Position Status Information
Additional Settings and Outages
Current Channel & Mode
Alert Settings
Alternate Channel if in BACKUP Mode
Critical Outages
TBP or TBE to Expand Sublist

## Slide 80: Position Relief Checklist (POS CHECK)

## Slide 81: Emergency Checklist (EMERG CK)

## Slide 82: Time View
Sector Message
Notification Area
Current UTC Time

## Slide 83: Message Composition Area (MCA)
QZ 240 UAL12
Feedback Area
Preview Area
X REJECT - SECTOR 20 HAS CONTROL
ASSIGNED ALT UAL12
QZ 240 UAL12
_

## Slide 84: Response Area
Coral “A” -
non-ADS-B
Indicator
Cyan “T” -
TFM-pending
reroute notification
Flight Plan Readout
0020
A 049 SWA235 B38M/L 2477 467 KPHL E0025 340 T
KPHL..PTW.PTW320.SARAA
.J64.HLC.J80.OAL.MOD9
.KSFO
Display flight plan in ICAO format:
QF I <FLID>
QF I 330
0346
330 SAM500 FLR I WAK L
EQP DGVWJ4R SRV EB1 OTH
++PBN/ D1 DAT/
1FANSPER2PDC REG/ SAM500
CODE/ 00062A++ ADB 260B
RNV D1A1E1
Display a flight plan:
QF <FLID>
QF SWA235

## Slide 85: Route Display
Route Display
Display/remove specific route:
QU <FLID>
Route with specific minutes:
QU <1 to 99> <FLID>
Remove displayed lines:
QU
DAL235
201
AAL532
584
Re-entrant Data
Block Overlap
Route Display
Display/remove specific route:
QU <FLID>
Route with specific minutes:
QU <1 to 99> <FLID>
Remove displayed lines:
QU
DAL235
201
Re-entrant Data Block
DAL235
DAL235
AAL532
DAL235

## Slide 86: Position Failure

## Slide 87: Failure of ADS-B Radio Station
ADS-B Radio Station Outage Indicator

## Slide 88: Knowledge Check
Which view shows the active channel?
  Position Failure View
  Status View
  Channel Display View

## Slide 89: Knowledge Check
Which display is used to enter messages from the R Position and is divided into the Preview and Feedback areas?
  Message Composition Area
  Message Preview Area
  Message Feedback Area

## Slide 90: Knowledge Check
What does a cyan “T” in the response area denote?
  Transponder equipped aircraft
  Track update in progress
  TFM-pending reroute

## Slide 91: Part-Task Exercise
Purpose
  Perform the following tasks:
    Identify and interpret symbology from the ERAM situation display
    Identify and manipulate data from selected ERAM display views
Materials
  TTL part-task exercise: Radar Position Situation Display
Directions
  This exercise takes approximately 30 minutes to complete. Each student must complete the checklist tasks. No headsets are required

## Slide 92: Lesson Summary
This lesson covered:
Radar Symbols
Full Data Blocks
Limited Data Blocks
Display Views
Weather Displays
Miscellaneous Displays

## Slide 93: The End