## Slide 2
At the end of this lesson, you will be able to identify:
Function of key automation systems via which Controller Pilot Data Link Communications (CPDLC) messages flow between controllers and aircraft
Sector requirements for exchanging CPDLC messages
Characteristics of basic Transfer of Communication (TOC)
Characteristics of Altimeter Setting uplinks
Lesson Objectives

## Slide 3: Controller Pilot Data Link Communications (CPDLC)
ATC UPLINK
1923Z
1/1
STATUS
OPEN
CROSS BENKY AT AND MAINTAIN 11000 FT
<WILCO
<STANDBY
UNABLE>
-------------------------------
<PRINT
LOG>
A two-way digital communications system that conveys textual air traffic control messages between controllers and pilots using ground or satellite-based radio relay stations.
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 4: Key Automation Systems
FANS 1/A
Equipped Aircraft
DCNS
Local CPDLC
National CPDLC
(NAP)
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 5: Coverage Area
16,000’
12,000’
10,000’
2,500’
60 nm
40 nm
20 nm
National Coverage
TDLS Coverage
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 6: Pilot Response Options
ATC UPLINK
1923Z
1/1
STATUS
OPEN
CLIMB AND MAINTAIN FL310
<WILCO
<STANDBY
UNABLE>
-------------------------------
<PRINT
LOG>
WILCO
ROGER
STANDBY
UNABLE
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 7: Knowledge Check
What is the minimum altitude at which CPDLC coverage is guaranteed nationally?
  10,000’
  12,000’
  16,000’

## Slide 8: Knowledge Check
What basic responses can a pilot reply to CPDLC messages with?
  ROGER, WILCO, HOLD, UNABLE
  ROGER, WILCO, STANDBY, UNABLE
  ROGER, WILCO, WAIT, UNABLE

## Slide 9
CPDLC session must be established with the aircraft
Sector must be assigned CPDLC eligibility for the aircraft
Aircraft must be marked on frequency
Requirements for Exchanging CPDLC Messages

## Slide 10
Ground System
Virtual connection established between the ground system and an aircraft for CPDLC message exchange.
CPDLC Session

## Slide 11
AAL544 330C 431 400
R
431
AAL544
B738/L
330
4112
NDA Session
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 12
AAL234 350C 123 400
123
AAL234
B752/L
350
3624
CDA Session
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 13
Ground System
CPDLC Eligibility

## Slide 14
AAL234 350C 123 400
123
AAL234
B752/L
350
3624
CDA Session With Eligibility Indicator
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 15: Voice Communication Indicators
Automatically marked on
Manually marked on
010
AAL003
B752/L
370
3624
009
AAL002
B752/L
370
5223
AAL002 370C 009 400
AAL003 370C 010 400
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 16
Knowledge Check
431
AAL544
B738/L
330
4112
What type of session is indicated by the white triangle to the left of the call sign?
  VCI
  NDA
  CDA

## Slide 17
Knowledge Check
123
AAL234
B752/L
350
3624
What does the white square to the left of the call sign indicate?
  CDA session without eligibility
  CDA session with eligibility
  Terminated CDA session

## Slide 18: Knowledge Check
009
AAL002
B752/L
370
5223
Can the controller communicate with this aircraft using CPDLC?
  Yes
  No
NOTE: Two of the three requirements for exchanging CPDLC messages have been satisfied, but the aircraft has not been marked on frequency.

## Slide 19: Knowledge Check
009
AAL002
B752/L
370
5223
What does the green symbol to the left of the alert boxes indicate?
  Off frequency
  Manually marked on frequency
  Automatically marked on frequency

## Slide 20: Knowledge Check
What are the three requirements that must be satisfied in order for a sector to be able to exchange CPDLC messages with an aircraft?
Answer: The aircraft must have a session established; the sector must be assigned eligibility; and the aircraft must be marked on frequency.

## Slide 21
Basic Transfer of Communication (TOC)
For CPDLC aircraft, every track control change results in the system creating a Held TOC entry
  Controller may release it at the operationally appropriate time
    System latency should be considered
  When released by the controller, the system builds and uplinks the appropriate frequency change message

## Slide 22: TOC Uplink Message
ATC UPLINK
1923Z
1/1
STATUS
OPEN
CONTACT WASHINGTON CTR AT 122.500
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOG>
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 23: Held TOC Entry
AAL002
X
HELD TOC
17
122.50
Destination Control Position (e.g., sector)
Automatically Selected Frequency
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 24: Held TOC Indicators
Single Held TOC Indicator
Multiple Held TOC Indicator
423
AAL002
B752/L
350
3624
(17)
526
SWA212
B737/L
310
4253
(23)
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 25: Releasing a Held TOC
AAL002 350C 423O-17
R
TBE
TBE
423
AAL002
B752/L
350
3624
(17)
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 26: Releasing a Held TOC (Cont’d)
423
AAL002
B752/L
350
3624
(17)
AAL002 350C 423O-17
R
1. TBP
1. TBP
AAL002
X
HELD TOC
17
122.50
2. TBP or TBE
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 27: Releasing a Held TOC (Cont’d)
UH 423
UH <FLID>
UH <Sector/Position> <FLID>
UH <Sector/Position> <Frequency> <FLID>
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 28: TOC In Progress Indicator
Transferring Sector
Receiving Sector
423
AAL002
423
AAL002
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 29: TOC In Progress Timeout Indicator
Only displayed at transferring sector
SWA427 280C 225 300
225
SWA427
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 30: Contact TOC - Handoff Initiated
AAL234 350C 123
AAL234 350C 123
Transferring Sector
Receiving Sector
R
H-17
H-17
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 31: Contact TOC - Handoff Accepted
AAL234 350C 123
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
O-17
O-17
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 32: Contact TOC - Held TOC Released
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 33: Contact TOC - WILCO Response
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 34: Contact TOC - Manual VCI
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 35: Conditions for a Monitor TOC
ATC UPLINK
1923Z
1/1
STATUS
OPEN
MONITOR MEMPHIS CENTER 126.85 MHZ, CONFIRM ASSIGNED ALTITUDE
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOG>
Intra-facility handoff
Sector preference set to MONITOR
System selected frequency adapted for receiving sector
Aircraft RVSM capable
IC service enabled
Assigned altitude is a single altitude
No procedure altitude
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 36: Monitor TOC - Handoff Initiated
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
H-17
H-17
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 37: Monitor TOC - Handoff Accepted
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
O-17
O-17
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 38: Monitor TOC - Held TOC Released
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 39: Monitor TOC - WILCO Response
AAL234 350C 123 400
AAL234 350C 123 400
Transferring Sector
Receiving Sector
R
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 40: Initial Contact (IC)
ATC UPLINK
1923Z
1/1
STATUS
OPEN
MONITOR MEMPHIS CENTER 126.85 MHZ, CONFIRM ASSIGNED ALTITUDE
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOG>
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 41: CAA In Progress Indicator
123
AAL234
425
SWA427
Combined altitude and TOC downlink
Split altitude and
TOC downlinks
SWA427 330C 425 400
AAL234 350C 123 400
Upon receipt of matching altitude downlink
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 42: Knowledge Check
Which indicator is a single Held TOC?
  Green symbol to the left of the alert boxes
  White square to the left of the ACID
  White triangle with an orange line to the right of the ACID
423
AAL002
B752/L
350
3624
(17)

## Slide 43: Knowledge Check
423
AAL002
B752/L
350
3624
What does the white triangle to the left of the call sign indicate?
  Transferring sector TOC In Progress
  Receiving sector TOC In Progress
  Multiple Held TOC

## Slide 44: Knowledge Check
What does the white triangle and two orange lines to the right of the call sign indicate?
  Multiple Held TOC
  Transferring sector TOC in progress
  Mismatch
543
DAL324
B752/L
350
3624
(20)

## Slide 45: Knowledge Check
What does the white triangle to the right of the call sign indicate?
Answer: It is an indication to the transferring sector that there is a TOC in progress and the system is waiting for a pilot response.
3624
123
AAL234
B752/L
350
3624
(14)

## Slide 46: Knowledge Check
What does the white triangle to the right of the CID indicate?
Answer: It is a CAA In Progress indicator when the downlinked altitude is separate from the TOC response.
009
AAL002
B752/L
370
5223

## Slide 47
Automatic Altimeter Setting Uplink
  Following receipt of a WILCO to a Monitor TOC and the cleared altitude displayed in the data block is below FL180
  When a controller uplinks an altitude clearance and the new altitude is below FL180
  Manual Altimeter Setting Uplink
  Sent using the UA Command
Altimeter Setting Uplink

## Slide 48: Automatic Altimeter Setting Uplink
ATC UPLINK
1923Z
1/1
STATUS
OPEN
KRSW LOCAL ALTIMETER.
ALTIMETER 29.94 IN.
<STANDBY
<UNABLE
ROGER>
-------------------------------
<PRINT
LOG>
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 49: Altimeter Not Automatically Uplinked
ATC UPLINK
1923Z
1/1
STATUS
OPEN
KRSW LOCAL ALTIMETER MORE
THAN ONE HOUR OLD.
ALTIMETER 29.94 IN.
<STANDBY
<UNABLE
ROGER>
-------------------------------
<PRINT
LOG>
Missing
Greater than 31.00
Over 2 hours old
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 50: Manual Altimeter Setting Uplink
UA ORD 434
UA <FLID>
UA <Reporting Station> <FLID>
UA Command
Notes: ICD-section 1.2 _ AMPM 1.1
Mention the Freeze horizons and RMD parameters will be covered later in this lesson

## Slide 51
SWA427 330C 425 400
425
SWA427
B737/L
330
5223
Generic Uplink In Progress

## Slide 52
What two conditions result in the system attempting to automatically uplink an altimeter setting?
Answer: 1) Receipt of a WILCO to a MONITOR TOC and the cleared altitude displayed in the FDB is below FL180; 2) Altitude clearance uplink descending through FL180
Knowledge Check

## Slide 53: Knowledge Check
What three altimeter data conditions prevent the automatic uplink of an altimeter setting?
Answer: Missing altimeter; altimeter greater than 31.00; altimeter is over two hours old

## Slide 54
Knowledge Check
Which command will manually uplink an altimeter and let the system determine the appropriate reporting station based on the aircraft’s current location?
  UA <FLID>
  AS <FLID>
  US <FLID>

## Slide 55: Part-Task Exercise
Purpose
  Perform tasks as follows:
    Identify basic CPDLC indicators
    Release a Held TOC
    Manually uplink an altimeter setting
Materials
  TTL part-task exercise: Introduction to CPDLC
Directions
  This exercise takes approximately 45 minutes to complete. Each student must complete the checklist tasks. No headsets are required.

## Slide 56: Lesson Summary
This lesson covered:
Function of key automation systems via which Controller Pilot Data Link Communications (CPDLC) messages flow between controllers and aircraft
Sector requirements for exchanging CPDLC Messages
Characteristics of Basic Transfer of Communication (TOC)
Characteristics of Altimeter Setting uplinks

## Slide 57: The End