## Slide 2
Lesson Objectives
At the end of this lesson, you will be able to identify characteristics of:
Keyboard route amendments
Route Menu amendments
Traffic Flow Management (TFM) Reroutes
CPDLC route uplinks

## Slide 3: Route Definitions
Preferential Departure Route (PDR) - A specific departure route from an airport or terminal area to an en route point where there is no further need for flow control. It may be included in an Instrument Departure Procedure (DP) or a Preferred IFR Route.
Preferential Arrival Route (PAR) - A specific arrival route from an appropriate en route point to an airport or terminal area. It may be included in a Standard Terminal Arrival (STAR) or a Preferred IFR Route.
Preferential Departure and Arrival Route (PDAR) - A route between two terminals which are within or immediately adjacent to one ARTCC’s area.

## Slide 4: Keyboard Track Reroute Commands (QU)
Syntax: QU <FIX> (FIX)…(FIX) <FLID>
  Maximum of 17 fixes
  Examples:
QU JOT STL270010 3727/8942 FAM KCGI 746
QU SEA PMD090005 KLAX AAL521
QU 2832/8119 CRG DBN KATL * DAL2040

## Slide 5: QU Commands - Uplinked
/<Reason>
/FRC
/U
Composition:
  CPDLC fields can be entered in any order
  Spaces are optional between CPDLC fields
Examples: QU MCN /U /TFC /FRC 334 QU MCN /FRC/U/TFC 334
QU MCN /FRC/U /TFC 334
  Route element(s) can be before, in between, or after CPDLC fields
Examples: QU /U /WX MCN AMG /FRC 334
QU /U /WX /FRC MCN AMG 334
Track Reroute (QU) command provides the ability to amend the route and uplink it to CPDLC eligible aircraft by inserting /U into the command
A Due to Reason may be inserted for the clearance by using one of the following:
  /TFC - Due to traffic
  /RES - Due to airspace restriction
  /WX - Due to weather

## Slide 6: Acknowledge Embedded Route Text
To acknowledge embedded route 1. TBH
2. TBP
Cyan Box
Cyan Brackets
ACL embedded route text:
If preferential route needs to be issued:
  Cyan box around the entire Route field, and
  Cyan brackets around a cyan embedded route
If sector is not eligible for cyan coded text
  Muted brackets around muted embedded route
  Preferential route cannot be acknowledged
Muted Brackets around Muted Route
Resulting Amendment

## Slide 7: Amendment Template - Route Change
3. TBP or TBE and type to insert amended route
4. TBP Send button or KBE
1. TBP
2. TBP

## Slide 8: Knowledge Check
How is an unissued embedded route displayed in the route field?
A.
B.
C.

## Slide 9: Knowledge Check
Which of the following is not a valid QU amendment?
  QU SAV CAE090005 KCLT ↓ AAL521
  QU 2832/8119 CRG DBN KATL DAL2040
  QU 746 JOT090005

## Slide 10: Route Menu
The purpose of the Route Menu is to provide the user with a method for creating a trial plan or amending a FP route of flight
The three types of route amendments available in the Route Menu are:
  Manually typing in a new route in the typing buffer
  Selecting a direct-to-fix option
  Selecting an ATC preferred route option

## Slide 11: Accessing the Route Menu
Or TBP: Accesses the Route Menu in one step
2. TBP
3. TBP
1. TBP

## Slide 12: Route Menu Layout
Direct-to-Fix/ ATC Intended Route Section
Bottom Section
Selection Boxes Section
APR Section
Top Section

## Slide 13: Top Section - Buttons
Uplink
Due To Chevron
Amend
Trial Plan
Aircraft ID and Aircraft Type/Equipment

## Slide 14: Top Section - Due To Chevron
Due To Chevron Button
Due To Reasons

## Slide 15: Top Section - Pending Reroute and Typing Buffer
Pending Reroute
Second row displays Pending Reroute in yellow text, but only if there is a pending reroute for the aircraft
Third row displays the pending reroute, but only if:
  A pending reroute has been trial planned and selected, and
  Route Menu was opened from the Plans Display/Plan Options Menu
Fourth Row: Typing Buffer
Non-Editable Element

## Slide 16
not displayed
Before Pending Reroute is applied:
Typing buffer route includes applied TFM Reroute
Applied TFM Reroute
After TFM Reroute has been applied:
displayed
Top Section - TFM Reroute Applied

## Slide 17: Top Section - Usage
To amend a route:
Complete the amendment using Route Menu:
Typing Buffer, or
Direct-to-Fix section, or
ATC Preferred Route section
TBP Due to Chevron
TBP Uplink or Amend
TBP Due to Reason
Selected by default

## Slide 18: Top Section - Typing Buffer Amendment
Typing Buffer
1. TBP Amend
2. Enter revised route string
3. KBE completes amendment

## Slide 19: Selection Boxes Section
Include PAR selection box
  Only active if the route to be amended includes an adapted Preferential Arrival Route (PAR)
  Selecting this box prior to selecting the downstream fix results in an amendment from the current position to the selected downstream fix, and includes the appropriate PAR

## Slide 20: Selection Boxes Section (Cont’d)
Prohibits application of an adapted Equipment Restricted Route (ERR)
Prohibits application of an adapted route
Uplinked route will contain a Full Route Clearance (FRC)
Append ✱, Append ⊕, FRC

## Slide 21: Direct-to-Fix / ATC Intended Route Section
ATC Intended Route
Direct-to-Fixes

## Slide 22: ATC Intended Route - Coding
Coding | Condition for Application | Example(s)
Cyan characters | Items are part of an unissued adapted route (AAR, ADAR, or ADR) | 
White characters in white brackets | Item is part of an auto route with non-field 10 alphanumerics | 
Underlined coral characters | Flight is not eligible for the item in the route | 
Cyan characters with coral underline | Items are part of an unissued AAR, ADAR, or ADR for which the flight is not eligible | 
Yellow chevrons | Surround TFM protected portion of route when TFM reroute is pending for the flight | 
White chevrons | Surround TFM protected portion of route when a TFM reroute is in effect for the flight | 
XXX or ??? | Incomplete route indicator | 

## Slide 23: Direct-to-Fix - Coding
Coding | Condition for Application | Example
White chevrons | Fix is part of TFM-protected portion of route | 
Cyan characters | Fix is part of an unissued AAR that is expected to be issued in a clearance by the local facility and the item is not the route destination | 
Cyan characters within cyan parentheses | Fix is an part of an unissued AAR that is not expected to be issued in a clearance by the local facility (i.e., expected to be issued by a down route facility) and the item is not the route destination | 
Gray characters | Fix was generated from a non-field 10 adapted route | 
Underlined coral characters | Flight is ineligible for this fix | 
Cyan characters with coral underline | Fix is part of an uncleared AAR, ADAR, or ADR for which the flight is not eligible | 

## Slide 24: Direct-to-Fix - Amend Route
Use the areas outlined here to amend a route using a Direct-to-Fix

## Slide 25
Direct-to-Fix - Include PAR Not Selected
Not selected
White Fix Selected
Resulting ACL Route Field
Beginning ACL Route Field
Not selected
Selected (White Fix)
Beginning ACL Route Field
Resulting ACL Route Field
[MANGE..THHMP.CAVLR4.] is the suppressed ERR PAR
[MATOX..FAK.COATT5.] is the applied non-ERR PAR.
Not selected
Selected (White Fix)
Beginning ACL Route Field
Resulting ACL Route Field
NOTE: No PAR applied.

## Slide 26
Direct-to-Fix - Include PAR Not Selected (Cont’d)
Not selected
Blue Fix Selected
Resulting ACL Route Field
Beginning ACL Route Field
Not selected
Selected (Blue Fix)
Beginning ACL Route Field
Resulting ACL Route Field
[DORRN.CAVLR4.] is the suppressed ERR PAR
[FAK.COATT5.] is the applied non-ERR PAR
Not selected
Selected (Blue Fix)
Beginning ACL Route Field
Resulting ACL Route Field
NOTE: No PAR applied.

## Slide 27
Direct-to-Fix - Include PAR Selected
Selected
White Fix Selected
Resulting ACL Route Field
Beginning ACL Route Field
Selected
Blue Fix Selected
Resulting ACL Route Field
Beginning ACL Route Field

## Slide 28: APR Section
ELIGIBLE tab (selected)
ALL tab
No Eligible APRs

## Slide 29
APR Section - ELIGIBLE Tab
Lists sector specific eligible ATC Preferred Routes (APRs)
NOTE: Eligible APR(s) are indicated by a blue departure point in the ACL route of flight.

## Slide 30: APR Section - All Tab
When no APRs are available: APR Section Removed
All Available APRs

## Slide 31
Eligible Advanced APR
Eligible Non-Advanced APR
Ineligible APRs
APR Section - Sort Order

## Slide 32: APR - Amend Route
Use the areas outlined here to amend a route using an APR

## Slide 33: APR - Removal of Blue Departure Point from ACL

## Slide 34: Bottom Section
Bottom Section

## Slide 35: Previous Route
Aircraft ID
TFM-Protected Segment of Previous Route
TFM-Protected Segment Message
Current Coordination Fix & Time
Previous Route
Apply Previous Route Button
Exit Button

## Slide 36: Knowledge Check
The Append ✱ selection box inhibits what type of adapted routes?
  Equipment Restricted Routes (ERR)
  Non-ERR
  All

## Slide 37: Knowledge Check
In the Route Menu ATC Intended Route, what do the cyan coded elements represent?
  Unissued preferential route
  Pilot requested route
  TFMS Request

## Slide 38: Knowledge Check
In which area may you edit the route of flight?
A
B

## Slide 39: Knowledge Check
What are the CPDLC Due to Reasons that may be uplinked?
  Airspace; Congestion; Weather
  Traffic; Weather; Airport closure
  Weather; Traffic; Airspace restriction

## Slide 40: Knowledge Check
Which is an advanced eligible ATC Preferred Route?
  Top one
  Top two
  All

## Slide 41: TFM Reroutes

## Slide 42: TFM Quick View
TBP or TBE
To open TFM Quick View
TFM Indicator Field

## Slide 43: TFM Quick View Layout
Pending Reroute
Header

## Slide 44: TFM Quick View Layout (Cont’d)
Pending Remarks

## Slide 45: TFM Quick View Layout (Cont’d)
TFM Quick View Buttons

## Slide 46: TFM Reroute Menu Access
TBP
Or
TBP

## Slide 47: TFM Reroute Menu
Header
Current Route Section
Pending TFM Reroute Section
Direct-to-Fix Section

## Slide 48: TFM Reroute Menu (Cont’d)
Pending TFM Reroute Title
Typing Buffer
Pending Remarks
Pending TFM Reroute
Direct-to-Fix Section

## Slide 49: TFM Reroute Menu Buttons
TFM Reroute Menu Buttons

## Slide 50: TFM Reroute Menu Coding
Data | Coding | Condition for Application | Example
Protected Segment Symbols - Current Route | White chevrons | Current route contains protected segment | 
Protected Segment Symbols - Pending Reroute | Yellow chevrons around protected portion of route | Pending TFM reroute contains protected segment | 
Divergent Fix - Pending Reroute | Point (fix) at which aircraft joins reroute or divergent point is in white text | Divergent point is a fix within current flight plan route | 
Convergent Fix - Pending Reroute | Point (fix) at which aircraft joins current flight plan route or convergent point is in white text | Convergent point is a fix within current flight plan route | 

## Slide 51: TFM Reroute Menu Coding (Cont’d)
Data | Coding | Condition for Application | Example
Pending Reroute String | Cyan text | Portion of route that is not on current route flight plan | See Below
Flight Beyond Divergent Fix Warning | Yellow text | Flight is past divergent fix | See Below
Protected Segment Symbols in Direct-to-Fix List | Each fix that is part of TFM-protected portion of route is displayed with chevrons pointing inward towards the fix, which is white | Fix is part of TFM-protected portion of the route (protected segment) | 
Menu Item | Underlined coral characters | Flight is ineligible for route fix | 

## Slide 52: TFM Reroute Menu - Apply Reroute
1. TBP
3. TBP
2. TBP and edit

## Slide 53: TFM Reroute - Reject Confirmation Pop Up
1. TBP
Sector has track control
2. TBP

## Slide 54: TFM Reroute - Reject Eligibility Pop Up
Sector does not have track control
1. TBP
2. TBP

## Slide 55
TFM - Send AM Confirmation Pop Up
Provides notification to the controller that there has been a reroute cancellation while one of the following is open:
  TFM Reroute menu
  TFM Quick View menu
  Plans Display (reroute trial plan)
Provides the means to choose whether to continue to send or cancel an amendment

## Slide 56
TFM Reroute Warning Pop Up
TBP

## Slide 57
When a pending TFM Reroute becomes invalid:
  Cyan “T” to the left of the route field in the ACL is removed
  Route is no longer available to be applied
TFM Reroute Becomes Invalid

## Slide 58
1. TBP
TFM Reroutes Invalidated
2. TBP

## Slide 59
TFM Reroute Remarks

## Slide 60
TFM Reroute Remarks Functionality
A TFM pending reroute may add or remove remarks in a flight plan

## Slide 61: Knowledge Check
How may the TFM Quick View be accessed?
  TBP the flight ID
  TBP the “T” in the TFM indicator field
  TBP the blue coding in the route field

## Slide 62
Knowledge Check
What is true of TFM Pending Reroute remarks?
  All remarks may be edited
  All remarks except the TMI ID may be edited
  This field is not selectable and cannot be edited

## Slide 63
Knowledge Check
SARAA in the Pending TFM Reroute is the point at which the aircraft will _____ .
  begin protected route segment
  diverge from TFM reroute and join current route
  diverge from current route and join TFM reroute

## Slide 64
CPDLC Route Uplink Considerations
Capability to uplink four different types of route clearances
EAS will validate the command, and if valid update the flight plan
  After flight plan is updated, the system builds and sends an uplink message

## Slide 65
CPDLC Route Clearance Types
ATC UPLINK
1923Z
1/1
STATUS
OPEN
PROCEED DIRECT TO FAK, REST OF ROUTE UNCHANGED
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOAD>
PROCEED DIRECT TO <Position>
CLEARED TO <Position> VIA <Route>
CLEARED <Route>
AT <Position> CLEARED <Route>

## Slide 66
Route Uplink - In Progress
280
5223
/
RDU..ROA..EKN..IHD.N
SWA427
280C
225 300

## Slide 67
Route Uplink - Processing
Controller enters route command
EAS validates the command
If command passes validation route will be amended in EAS
CPDLC will build the uplink and evaluate route for any FMS loadability issues
If no FMS loadability issues are identified, CPDLC will uplink the message

## Slide 68
Route Uplink - FMS Loadability Issues
Example: BWI LOCAL ADAPTATION IN ROUTE

## Slide 69
Route Uplink - System Latency
Do NOT use CPDLC if there is a chance the aircraft will be past the first fix in the route amendment before a response is received from the pilot
CRG
CHS
DIW
SAV
Cleared Route: KMIA./.CRG..SAV..CHS..ILM..DIW..KJFK
Do not uplink direct ILM
SWA123
TOO CLOSE
ILM

## Slide 70
Route Uplink - Timeout Indicators
280
5223
/
RDU..ROA..EKN..IHD.N
SWA427
280C
225 300

## Slide 71
Knowledge Check
A CPDLC route amendment is always uplinked if the amendment passes validation and is recorded in ERAM.
  True
  False

## Slide 72
Knowledge Check
What does the white triangle with green underline indicate?
  Route Timeout
  Altitude Uplink In Progress
  Route Uplink In Progress
280
5223
/
RDU..ROA..EKN..IHD.N

## Slide 73
280
5223
/
RDU..ROA..EKN..IHD.N
Knowledge Check
What does the white-bracketed triangle indicate?
  Route Timeout
  Altitude Timeout
  Pilot Timeout

## Slide 74: Part-Task Exercise
Purpose
  Perform route amendment tasks, which include CPDLC uplink and Traffic Flow Management Reroute functionality
Materials
  TTL part-task exercise: Route Amendments
Directions
  This exercise takes approximately 45 minutes to complete. Each student must complete the checklist tasks. No headsets are required.

## Slide 75: Lesson Summary
This lesson covered:
  Keyboard route amendments
  Route Menu amendments
  Traffic Flow Management (TFM) Reroutes
  CPDLC route uplinks

## Slide 76: The End