## Slide 2
Alert indicators and colors
Alerts on the Graphic Plan Display (GPD)
Automated Problem Detection (APD)
Rules for conflict notification
Stop Probe functionality
Airspace Status View functionality

## Slide 3: Alert Indicators
ACL
Plans Display
Graphic Plan Display

## Slide 4: Alert Indicators - Red
When two aircraft are predicted to have less than 5 miles lateral separation
  Alert box changes to red
  Red number indicates total conflicts

## Slide 5: Alert Indicators - Muted Red
When two aircraft are predicted to have less than 5 miles lateral separation and where an altitude change is planned but not issued
  Alert box changes to muted red
  Muted red number indicates total conflicts
  Highest level alert is always shown in the alert box

## Slide 6: Alert Indicators - Yellow
When two aircraft are predicted to have between 5 and 12 miles lateral separation
  Alert box changes to yellow
  Yellow number indicates total conflicts

## Slide 7: Alert Indicators - Muted Yellow
When two aircraft are predicted to have between 5 and 12 miles lateral separation where an altitude change is planned but not issued
  Alert box changes to muted yellow
  Muted yellow number indicates total conflicts

## Slide 8: Alert Indicators - Orange
Aircraft-to-airspace violation predicted within 3 miles of active or scheduled Special Activity Airspace (SAA)
  Alert box changes to orange
  Orange number indicates total conflicts

## Slide 9: Alert Boxes - Brown X
Brown X in all three alert boxes with brown flight ID signifies that entry is not being probed by system
Flights not probed:
  VFR
  OTP
  ABV
  Untracked

## Slide 10: Alert Boxes - Brown S
Brown S in all three alert boxes signifies stop probe is in effect for flight

## Slide 11: Alert Boxes - Brown H
Brown H in all three alert boxes signifies aircraft is in hold status
  Flight is not probed

## Slide 12: Alert Boxes - Brown F
A brown F in all three alert boxes signifies that a flight is frozen with a QH F command
  Flight is not probed

## Slide 13: Alert Indicators - Plans Display
FLID color matches the alert
Yellow Alert
Red Alert
No Conflicts
Conflicting Aircraft or SAA
Estimated Time of Conflict
Time Until Conflict

## Slide 14: Alert Indicators - GPD Data Block
Line 0 contains a number for each alert type designator assigned to the sector
  Red/muted red
  Yellow/muted yellow
  Orange
Alert Indicators

## Slide 15: Knowledge Check
What color alert indicates that two aircraft are predicted to have less than 5 miles lateral separation?
  Red
  Yellow
  Muted red

## Slide 16: Knowledge Check
What color alert indicates that an aircraft is predicted to come within 3 miles of scheduled Special Activity Airspace?
  Red
  Yellow
  Orange

## Slide 17: Knowledge Check
What color indicates that a conflict between 5 and 12 miles is predicted during a portion of the flight where an altitude change is planned, but the aircraft has not yet been cleared for the change?
  Muted red
  Muted yellow
  Orange

## Slide 18: Knowledge Check
What does a brown H in all three alert boxes on the ACL indicate?
  Aircraft is in handoff status
  Aircraft is commanded frozen
  Aircraft is in a hold status

## Slide 19: Knowledge Check
The route line color on the GPD indicates the most critical conflict unless _________?
  an aircraft is in hold
  alerts are suppressed
  a lesser alert is selected in Line 0

## Slide 20: Point of Violation
Initial Point of Violation
Initial Points of Violation
GPD depicts results of Trial Plans and conflict probe in graphical form
Initial Points of Violation

## Slide 21: Green Route of Flight
Aircraft is not predicted to have any violations

## Slide 22: Special Activity Airspace
Orange alert indicator displayed in Line 0 when aircraft is predicted to fly within 3 miles of active or scheduled Special Activity Airspace
Alert Indicator

## Slide 23: Show Alert Using ACL
The ACL Show button displays the aircraft’s current route and any alert(s) assigned to your sector
1. TBP
2. TBP

## Slide 24: Show Alert Using GPD
2. TBP
1. TBP

## Slide 25: Show All Alerts Using ACL
TBE

## Slide 26: Show All Alerts Using GPD
TBE
TBE on GPD entry call sign to display all alerts

## Slide 27: Acknowledge Selected Conflict
To acknowledge a selected conflict:
1. TBH
2.TBP
3. TBP
Result: Acknowledged Alert (White)

## Slide 28: Acknowledge All Conflicts
To acknowledge all conflicts:
1. TBH
2.TBP
Result: Acknowledged Alerts (White)

## Slide 29: Knowledge Check
How is a Point of Violation shown on the GPD?
  Dashed line where the conflict is predicted
  Blue line where the conflict is predicted
  Bold line where the conflict is predicted

## Slide 30: Knowledge Check
What color is the route of flight when it is displayed for an aircraft that is not predicted to have any violations?
  Orange
  Yellow
  Green

## Slide 31: Knowledge Check
What color is the numbered alert indicator in the GPD data block that predicts an airspace violation within 3 miles of active or scheduled Special Activity Airspace?
  Red
  Muted yellow
  Orange

## Slide 32: Knowledge Check
Which button is used to graphically display or remove a selected aircraft’s Current Plan and any specific alert(s) assigned to your sector?
  Alert
  Show All
  Show

## Slide 33: Knowledge Check
What color does an alert indicator change to when all alerts of that type are acknowledged?
  Red
  Muted yellow
  White

## Slide 34: Automated Problem Detection (APD)
Automated Problem Detection (APD) compares trajectories to predict conflicts
  Checks Current Plan trajectory
  Checks Trial Plan trajectory
  Checks Current and Trial Plans against other current plans and airspaces
Neither Current Plans nor Trial Plans are checked against other Trial Plans

## Slide 35: APD - Plans Display
Current Plan entries include CID and FLID
Trial Plan entries appended with .T(#)
  Indicates the number of Trial Plans
Current Plans
Trial Plan

## Slide 36: APD Ineligible
Aircraft not probed, no alerts for flight
Reason displayed in Plans Display
APD Ineligible Reasons

## Slide 37: APD Separation Values
5 NM Total
Lateral Separation
Longitudinal Separation
Vertical Separation
Minimum Separation below FL410 = 400’
300’
300’
3 NM Total
Minimum Separation between FL410-FL600 = 1400’
Minimum Separation

## Slide 38: APD Separation Buffer
Depending on type of SAA,
conflict occurs at either:
Airspace boundary, or
Separation buffer
40 minutes
SAA

## Slide 39: APD Inhibited Areas
APDIA
Trajectory Probed
Trajectory Not Probed
Trajectory Exits APDIA

## Slide 40: Knowledge Check
When does Automated Problem Detection (APD) probe a new Trial Plan against other Trial Plans?
  When there are Current Plans to probe against
  Only if there is a conflict
  Never

## Slide 41: Knowledge Check
When an aircraft is ineligible to be probed, where is the notification displayed?
  Automatic Problem Detection (APD)
  Aircraft Situation Display
  Plans Display

## Slide 42: Knowledge Check
Which type of plan shows the flight the aircraft is currently expected by EAS to fly?
  Trial Plan
  Current Plan
  Future Plan

## Slide 43: Knowledge Check
Which type of plan is used to test whether a proposed change to the Current Plan will be conflict free?
  Trial Plan
  Current Plan
  Test Plan

## Slide 44: Rules for Conflict Notification
Although APD may detect a conflict, sector may not be notified immediately
When an alert is provided:
  Only one sector receives the alert at a time
  Aircraft-to-aircraft alerts
    Notification is generally provided to the sector where the conflict is first predicted to occur
    Transferred to the next sector upon handoff
  Aircraft-to-airspace alerts
    Sector controlling the aircraft receives the alert

## Slide 45: Rules of Sector Control During Conflict Notification - Rule 1
Initial Points of Violation

## Slide 46: Rules of Sector Control During Conflict Notification - Rule 2
Initial Points of Violation

## Slide 47: Rules of Sector Control During Conflict Notification - Rule 3
Conflict Intersection

## Slide 48: Rules of Sector Control During Conflict Notification - Rule 4
Initial Points of Violation

## Slide 49: Rules of Sector Control During Conflict Notification - Rule 5

## Slide 50: Rules of Sector Control During Conflict Notification - Rule 6
Active
SAA

## Slide 51: Knowledge Check
Which sector will receive a conflict notification when an aircraft conflict is predicted to occur?
  Every sector that has control of a problem aircraft
  All sectors that the aircraft are flying through
  Sector where the conflict is first predicted to occur

## Slide 52: Knowledge Check
If points of violation are located in different sectors, and only one of these sectors controls an aircraft involved in conflict, which sector would receive conflict notification?
  Every sector that has control of a problem aircraft
  Sector containing a point of violation and currently controlling one of the aircraft
  Sector where the conflict is first predicted to occur

## Slide 53: Knowledge Check
Which sector will receive a conflict notification when an aircraft-to-airspace conflict is predicted to occur?
  Every sector that has an FDB displayed for the problem aircraft
  All sectors that the aircraft is flying through
  Sector that has track control of the aircraft

## Slide 54: Stop Probe Menu
Access the Stop Probe Menu in Plan Options menu
1. TBP
2. TBP
3. TBP
Present Position
Future Fixes

## Slide 55: Present Position Stop Probe
4. TBP
3. TBP
2. TBP
1. TBP

## Slide 56: Future Fix Stop Probe
4. TBP
3. TBP
2. TBP
1. TBP
55

## Slide 57: Stop Probe - ACL
When a present position stop probe is in effect, a brown S appears in the three alert boxes
When a stop probe will take effect at a future fix, a brown S appears to the right of the three alert boxes

## Slide 58: Stop Probe - GPD
When Stop Probe is in effect for an aircraft, on the GPD data block:
  Brown SSS occupies Line 0
  All text is brown

## Slide 59: Resume Probe
3. TBP
2. TBP
1. TBP

## Slide 60: Knowledge Check
How is a future fix Stop Probe shown on the ACL?
  Brown H next to the alert boxes
  Yellow S next to the alert boxes
  Brown S next to the alert boxes

## Slide 61: Knowledge Check
To stop probe at a future fix TBP FLID, then TBP the Plan Options Menu, then ________.
  TBP Stop Probe
  TBP fix name
  TBP Stop Probe, then TBP fix name

## Slide 62: Airspace Status View - Accessing
1. TBP
2. TBP

## Slide 63: Airspace Status View
View can be expanded or compressed from the Airspace Status View menu
Compressed view displays only the first line of each SAA’s data
TBP or TBE for Menu
TBP or TBE to Compress View
TBP or TBE
Can display SAA of selected adjacent facilities
Expanded View

## Slide 64: Airspace Status View - Buttons and Labels
Radio Buttons
White Buttons
Gray Buttons
Column Labels

## Slide 65: Airspace Status View - REQ
TBP or TBE
TBP or TBE
Results
64

## Slide 66: Airspace Status View - Pending SAA
Select Altitude Range in a Pending SAA

## Slide 67: Airspace Status View - ON
1. TBP or TBE
3. TBP or TBE
Results
2. Enter Altitude Range

## Slide 68: Airspace Status View - OFF
OFF Button

## Slide 69: Airspace Status View - SCH
SCH Button
Pending Status
SCH button filled in when an SAA is scheduled active within the next 48 hours

## Slide 70: Knowledge Check
Which view is used to see the status of Special Activity Airspace up to 48 hours in advance?
  Options
  Airport Stream Filter
  Airspace Status View

## Slide 71: Knowledge Check
Which button is selected to view planned use of Special Activity Airspace?
  PLAN
  ON
  SCH

## Slide 72: Part-Task Exercise
Purpose
  Perform Alert and Airspace Status View tasks
Materials
  TTL part-task exercise: Alerts and Airspace Status View
Directions
  This exercise takes approximately 30 minutes to complete. Each student must complete the checklist tasks. No headsets are required.

## Slide 73: Lesson Summary
This lesson covered:
Alert indicators and colors
Alerts on the GPD
Automated Problem Detection (APD)
Rules for conflict notification
Stop Probe functionality
Airspace Status View functionality

## Slide 74: The End

## Slide 75: APD Separation Buffer
Depending on type of SAA,
conflict occurs at either:
Airspace boundary, or
Separation buffer
40 minutes
SAA