## Slide 2
Altitude reporting transponder and ADS-B requirements
Characteristics of the National Beacon Code Allocation Plan
Beacon code requirements
Beacon code commands

## Slide 3: Transponder and ADS-B Out Requirements
Some aircraft must be equipped with a transponder and/or Automatic Dependent Surveillance-Broadcast (ADS-B) Out equipment

## Slide 4
  In all airspace of the 48 contiguous states and the District of Columbia at and above 10,000’ MSL:
    Excluding airspace at and below 2,500’ Above Ground Level (AGL)
    Unless a glider or balloon
  Above the ceiling and within the lateral boundaries of Class B or C airspace designated for specific airports up to 10,000’ MSL
  In Class A, B, and C airspace
  Within 30 miles and from the surface up to 10,000’ Mean Sea Level (MSL) of specific airports
    Gliders and balloons may operate outside of Class A, B, or C airspace within 30 miles if they meet specific criteria
Requirements apply to all aircraft operating:
Operations Requiring Transponder

## Slide 5
    In Class E airspace at and above 3,000’ MSL over the Gulf of Mexico from the coastline of the U.S. out to 12 miles
    Above the ceiling and within the lateral boundaries of Class B or C airspace designated for a specific airport up to and including 10,000’ MSL
  Class E airspace within the the 48 contiguous states and the District of Columbia at and above 10,000’ MSL, excluding airspace at and below 2,500’ AGL
    Unless a glider or balloon
  In Class A, B, and C airspace
  Within 30 miles and from the surface up to 10,000’ MSL of specific airports
    Gliders and balloons may operate outside of Class A, Class B, or Class C airspace within 30 miles if they meet specific criteria
Requirements apply to all aircraft operating:
Operations Requiring ADS-B Out

## Slide 6: Inflight Deviation Requests
For VFR aircraft with an inoperable transponder or Mode C, or not equipped with Mode C, suggest that the aircraft do one of the following:
  Conduct flight in airspace not affected by 14 CFR Part 91.215
  File an IFR flight plan
  Provide a VFR route of flight and maintain radio contact with ATC
Must be made to the ATC facility having jurisdiction over the concerned airspace

## Slide 7
“TAYLOR LOW APREQ, BONANZA TWO THREE TANGO INOPERATIVE TRANSPONDER AND MODE C, ONE SEVEN THOUSAND”
“APPROVED AS REQUESTED, BC”
Inflight Deviation Requests (Cont’d)

## Slide 8: Failed Transponder or ADS-B Out
“NOVEMBER SIX SIX KILO GOLF OUR TRANSPONDER HAS FAILED. REQUEST FLIGHT LEVEL TWO ONE ZERO.”
“NOVEMBER SIX SIX KILO GOLF, UNABLE YOUR REQUEST FOR FLIGHT LEVEL TWO ONE ZERO DUE TO PRIMARY RADAR OUTAGE”

## Slide 9: Knowledge Check
Transponder requirements apply to all aircraft operating in what classes of airspace?
  Classes A, B, and C
  Classes B, C, and D
  Classes C, D, and E

## Slide 10: Knowledge Check
An IFR aircraft has no transponder. The pilot declares an emergency and requests a deviation that will fly through Class A airspace. Can you approve this change?
  Yes
  No

## Slide 11: National Beacon Code Allocation Plan
DISCRETE BEACON CODE - Any one of the 4096 selectable Mode 3/A aircraft transponder codes except, those ending in zero zero.
  Examples: 0010, 1201, 2317, 7777
Nondiscrete BEACON code - Any one of the 4096 selectable Mode 3/A aircraft transponder codes ending in zero zero.
  Examples: 0100, 1200, 7600, 7700

## Slide 12: Code Assignment
EXTERNAL CODES - codes reserved for computer assignment to a flight plan with one or more route segments that are not contained within a single domestic ARTCC’s airspace.
INTERNAL CODES - codes reserved for computer assignment to a flight plan where all route segments are contained within a single ARTCC’s airspace.
Beacon Code assignment - Distribution of codes to specific facilities and special activities based on the National Beacon Code Allocation Plan.

## Slide 13: Knowledge Check
Beacon codes that end in numbers other than zero zero are ___________ codes.
  mixed
  nondiscrete
  discrete

## Slide 14: Knowledge Check
How are discrete beacon codes assigned?
  By pilot request
  By the automation system
  By the facility manager at each ARTCC

## Slide 15: Assignment Criteria
Assign beacon codes to only ADS-B and/or transponder equipped aircraft
Issue beacon codes assigned by the computer

## Slide 16: Assignment Criteria – Code 4000
Code 4000 should be assigned when
  Operating on a flight plan specifying frequent or rapid changes in assigned altitude in more than one stratum or other category of flight not compatible with a discrete code assignment

## Slide 17: Code Changes
Do not request an aircraft change from the code it is squawking in the transferring facility’s area of responsibility, unless:
  Specified in an LOA, or
  Coordinated at the time of handoff

## Slide 18: Beacon Code Procedures During an Emergency
Assign code 7700 when pilot declares emergency and is not radar identified
After radar contact established, request aircraft to change from 7700 to appropriate code
SWA127
220C
024EMRG
SWA127
330C
024EMRG
SWA127
330C
024EMRG

## Slide 19: Radio Failure
Controller must apply lost communications procedures
If radio communications have not been (re)established with the aircraft after 5 minutes, consider the aircraft’s activity to be suspicious
If two-way communication is lost, pilot will squawk code 7600
  RDOF blinks in the data block
If an aircraft is hijacked, it may squawk code 7500

## Slide 20: Unmanned Aircraft Systems (UAS) Lost Link
Code 7400 may be displayed by UAS when control link between aircraft and operator is lost
Determine lost link procedure as outlined in Special Airworthiness Certificate or Certificate of Waiver or Authorization (COA)

## Slide 21: Hijacked Aircraft
ATC must honor clearance requests, traffic conditions permitting
If necessary, aid escort aircraft into position
If an aircraft is hijacked, it may squawk code 7500
  HIJK blinks in data block
Use normal flight following and handoff procedures

## Slide 22: Pressure Suit Flights and Flights above FL600
Code 4400 and discrete codes 4440 through 4465 are reserved for use by:
  Pressure suit flights
  Aircraft operations above FL600

## Slide 23: VFR Code Assignments
Assign appropriate function or computer-assigned codes to VFR aircraft receiving radar advisories

## Slide 24: Code Monitor Requirements
Manually inserted code
1200.
1202.
1255.
1277.
4000.
Continuously monitor beacon codes applicable to your area of operation or operations in adjacent airspace

## Slide 25: Knowledge Check
Assign beacon codes to _______ equipped aircraft only.
  transponder and ADS-B
  transponder and ADS-D
  transponder

## Slide 26: Knowledge Check
What is the beacon code for hijacked aircraft?
  7300
  7400
  7500

## Slide 27: Knowledge Check
What aircraft use beacon code 1200?
  Military aircraft during pressure suit flights
  VFR aircraft not being provided services by an ATC facility
  All aircraft flying above FL600

## Slide 28: Code Insert or Delete
Manually inserted code
QB either typed or inserted by pressing CODE button
Syntax: QB dddd

## Slide 29: Discrete Code Request
(RA Position Only)
or
or
Syntax: QB <FLID> (/FLID) (/FLID)
  Up to three flight IDs can be entered in one command
  Beacon code cannot be a FLID
Syntax: DQ <FLID>
  Single FLID only

## Slide 30: Discrete Code Request Results
System generates new code
New code appears in the MCA

## Slide 31: Manual Code Assignment
Syntax: QB <code> <FLID>
  FLID cannot be a beacon code
or

## Slide 32: Equipment Qualifier Modification
Syntax: QB <equipment qualifier> <FLID> (/FLID) (/FLID)
  Up to three flight IDs can be entered in one command, separated by a “/”
  Beacon code cannot be a FLID
or

## Slide 33: Equipment Template

## Slide 34: Knowledge Check
Why should you use the Equipment Template to modify an aircraft’s equipment code?
  Opens automatically when the CODE button is pressed
  Ensures ICAO data is not inadvertently deleted or amended
  Allows CPDLC command to be composed at the same time

## Slide 35: Knowledge Check
To request a new beacon code for an aircraft, use the _______command.
  BC <FLID>
  QB <FLID>
  QC <FLID>

## Slide 36: Lesson Summary
This lesson covered:
Altitude reporting transponder and ADS-B Out requirements
Characteristics of the National Beacon Code Allocation Plan
Beacon code requirements
Beacon code commands

## Slide 37: The End