## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify:
Terminology for transferring radar identification
Handoff and point out methods
Handoff procedures
Handoff command entry
Point out procedures
Point out command entry

## Slide 3: Definitions
HANDOFF
RADAR CONTACT
POINT OUT
POINT OUT APPROVED
AUTOMATED INFORMATION TRANSFER (AIT)
TRAFFIC
TRAFFIC OBSERVED

## Slide 4
Knowledge Check
What is the term used to inform the controller initiating a handoff that the aircraft is identified and approval is granted for the aircraft to enter the receiving controller’s airspace?
  RADAR HANDOFF
  RADAR HANDOFF APPROVED
  RADAR CONTACT

## Slide 5
Knowledge Check
What is the term used to inform the controller initiating a point out that the aircraft is identified and that approval is granted for the aircraft to enter the receiving controller’s airspace, as coordinated, without a communications transfer?
  POINT OUT APPROVED
  POINT OUT ACCEPTED
  POINT OUT ACKNOWLEDGED

## Slide 6: Handoff and Point Out Methods
Transfer Radar Identification

## Slide 7
Relay information for handoff, point out, and traffic restrictions in the following order:
  Target position
  Aircraft identification
  Assigned altitude
    Appropriate restrictions
    Information that the aircraft is climbing or descending
  Pertinent information
Order of Information

## Slide 8
“D-T”
“POINT OUT EAST OF NOWAY DELTA THREE TWENTY-FOUR, FLIGHT LEVEL THREE ONE ZERO, DIRECT SPARTANBURG”
Landline / Interphone
“DELTA THREE TWENTY-FOUR, POINT OUT APPROVED, U-K”
Sector 1
Sector 2
DAL324
310C
543 400
DAL324
310C
543 400
R

## Slide 9
Data Block Coordination During and After Handoff
If you change data in the flight plan or FDB after receiving a handoff from another ERAM facility, before the target leaves the transferring facility's Area of Interest (AOI)
  Any changes made are reflected in the data block and ACL at both facilities
AOR Boundary
Facility A
Facility B
Facility B Situation Display
SWA547
330T237
122 451
H240

## Slide 10
4th Line Data Block Usage
AOR Boundary
Facility A
Heading
Speed
Heading and Speed
Free Text
/

## Slide 11
Entry of Hdg/Spd removes Free Form Text
Hdg/Spd or Free Form Text
4th Line
Enter Command
Enter Command
Entry of Free Form Text removes Hdg/Spd

## Slide 12
Enter 4th Line Information
Keyboard commands
  Syntax: QS <Heading>/<Speed> <FLID>
  QS <Heading> <FLID>
  QS /<Speed> <FLID>
  QS <Free form text> <FLID>

## Slide 13
Enter 4th Line Information (Cont’d)
TBP

## Slide 14
Remove 4th Line Information
TBH

## Slide 15
Altitude Coordination
The altitude field(s) of the data block must always reflect the current status of the aircraft, unless otherwise specified in a facility directive or LOA
SWA547
330T237
122 451
R

## Slide 16
Knowledge Check
During a handoff by landline voice communication, what is true of altitude information?
  Only needs to be coordinated if inter/intrafacility automation is out of service
  Must be coordinated, unless facility directives ensure altitude information is known
  Must be coordinated, regardless of facility directives

## Slide 17
Knowledge Check
What is true of the altitude field(s) in a data block?
  Must always reflect current status of aircraft, unless otherwise specified in a facility directive
  There is no requirement to reflect temporary altitudes
  When strips are in use, they must always reflect status of aircraft but not the data block

## Slide 18
Transferring Controller
Complete a handoff prior to an aircraft entering the airspace delegated to the receiving controller
Receiving Controller
Transferring Controller
N309
150C
071 295
N309
150C
071H-20

## Slide 19
Handoff is failing
Assigned a beacon code but not received
Coast status
Transferring Controller (Cont’d)
Initiate verbal coordination before transferring control of a track when data block displays:
AAL002
370N
009 CST
SWA347
330C
045FAIL
DAL110
370N
160NONE

## Slide 20
Receiving Controller
Before accepting a handoff ensure:
  Target position corresponds with the position given by the transferring controller
Receiving Controller
Transferring Controller
“VERIFY POSITION NOVEMBER THREE SIX TANGO, ONE ZERO MILES NORTH OF JUDD”
“AFFIRMATIVE”
N36T
60 27
122DATA
R
R

## Slide 21
Either or both facilities do not have radar data
Assigned a beacon code but not received
Coast status
Receiving Controller (Cont’d)
Initiate verbal coordination prior to accepting control of a track when the following indicators are displayed in the data block:
SWA347
330N
814 CST
DAL110
370N
009NONE
N422
70C
244DATA
R
R
R

## Slide 22
Both Controllers
Within a reasonable amount of time, take appropriate action to establish or restore communications with all aircraft for which a communications transfer or initial contact is expected or required
Receiving Controller
Transferring Controller

## Slide 23
Interfacility Automated Information Transfer
Procedures are specified in AIT directives and LOAs

## Slide 24
Prearranged Coordination
Allowing aircraft under your control to enter another controller’s area of jurisdiction may only be approved provided procedures are established and published in a facility directive or LOA
Sector A
Sector B
“REQUEST RAINY AREA”
“RAINY AREA RELEASED”
Rainy Area
SWA650
410C
134 450

## Slide 25
Knowledge Check
Unless previously coordinated or covered in an LOA, you must transfer communications of an aircraft before it enters the receiving controller’s airspace.
  True
  False

## Slide 26
Knowledge Check
Which FDB indicators would require verbal coordination?
  CST, NONE, SIDE
  SIDE, FAIL, NONE
  CST, FAIL, NONE

## Slide 27
Initiate Handoff - Intrafacility
No function key entry required
Syntax:
<sector number or facility> <FLID>
Examples: 30 UAL26
30 526
UAL26
310C
526H-30
UAL26
310C
526 451
UAL26
310C
526 451
R
UAL26
310C
526O-30
R
Before:
After:

## Slide 28
Initiate Handoff - Interfacility
No function key entry required
Local facility adaptation can specify a single letter identifier for handoffs
Examples: D30 UAL26 D 526
UAL26
310C
526 451
UAL26
310C
526 451
R
UAL26
310C
526OD30
R
UAL26
310C
526HD30
Before:
After:

## Slide 29
Side Stream Handoff
Flight Plan Route
Facility B
Facility A
Facility C
Weather
Deviation
A side stream handoff can be directed to a sector in an adjacent center that the aircraft’s flight plan does not enter
UAL26
310T195
526SIDE

## Slide 30
Field E Data Upon Handoff
Field E Data | Description
H-dd | H/O to sector within facility
HLdd | H/O to sector other facility, or from a STARS facility
HLLL | H/O to STARS
HLdL | H/O to sector within STARS
FAIL | H/O is failing
MISM | Mismatch in target position between two facilities
DATA | An interfacility handoff where either or both the handoff origin facility or the handoff receiving facility does not have radar data for the flight and a paired track is not established
OLD | Crosstell track data has timed out
NONE | Track has an assigned beacon code, and a beacon code is not received
SIDE | Warning to both the initiating and receiving controller that an interfacility (ARTCC to ARTCC) handoff is a side stream handoff. The SIDE indicator is displayed starting when the handoff is initiated and will continue to flash and time share with handoff accept information for a locally adapted period of time.

## Slide 31: Knowledge Check
What does DATA appearing in Field E of data blocks indicate?
  There is a discrepancy in the target position between the two facilities
  Track is being handed off intercenter or from a STARS facility
  The handoff origin and/or receiving facility does not have radar data for this flight

## Slide 32: Knowledge Check
What does FAIL appearing in Field E of the data block indicate?
  Handoff was unsuccessful
  Transponder failed
  Radar is inoperative

## Slide 33
Accepting Handoff
No function key entry required
  Syntax: <FLID>
  Examples: UAL26
  526
UAL26
310C
526H-40
R
UAL26
310C
526 451
R
UAL26
310C
526O-40
UAL26
310C
526 451
Before:
After:

## Slide 34
Accept Handoff - QZ Command
QZ command may be used in place of QN command
  Syntax: QZ <FLID>
While accepting a handoff, the QZ command may also modify flight plan data by:
  Assigning an altitude
  Offsetting a data block
  Offsetting a data block and assigning an altitude

## Slide 35
Retract Handoff
No function key entry required
Examples: UAL26
  526
UAL26
310C
526 451
UAL26
310C
526O-55
UAL26
310C
526 451
UAL26
310C
526H-40
Before:
After:

## Slide 36
Automatic Handoff
Sector Boundary
Route
Adapted Handoff Point
UAL26
310C
526 410
UAL26
310C
526 410
UAL26
310C
526 410
UAL26
310C
526H-40
UAL26
310C
526 410

## Slide 37
Auto Handoff Command
Enable or Inhibit Handoff | Examples
Flight | QA AAL123
Sector | QA 34
STARS Facility | QA ABC
ARTCC | QA M
Multiple Sectors or Facilities | QA 34 ABC M

## Slide 38
Auto Handoff Inhibit View

## Slide 39
Caret Symbol
A white caret “^” is displayed left of Field D and the Portal Fence when auto handoff is inhibited
Auto Handoff Inhibit
DAL324
310C
543 400
KPIT

## Slide 40: Knowledge Check
What letter is displayed in Field E when a handoff has been initiated?
  O
  H
  K

## Slide 41: Knowledge Check
Where does a caret “^” appear when a specific aircraft has been inhibited for automatic handoff?
  Above the second character of Field A in a data block
  Left of the Portal Fence and Field D
  Right of the last character of Field E

## Slide 42: Knowledge Check
An aircraft is eligible for automatic handoff if it is in _______ Track.
  Flat
  Free
  either Flat or Free

## Slide 43
Point Out Procedures
“DELTA TWENTY-TWO TEN, POINT OUT APPROVED, P-J”
Sector 1
Sector 2
“R-W”
“POINT OUT, TWO ZERO MILES NORTHWEST OF TAYLOR, DELTA TWENTY-TWO TEN, CLIMBING TO FLIGHT LEVEL THREE FIVE ZERO, DIRECT CRAIG”
DAL2210
350 321
260 407
P

## Slide 44: Knowledge Check
After a flight has been pointed out, which controller is responsible for subsequent point outs?
  Initiating
  Receiving
  Both initiating and receiving

## Slide 45
Initiate Automated Point Out
QP Command
  Example: QP 77 260
  Point out sent to sector 77
Sector 77
DAL2210
330 321
260 407
R
P
DAL2210
321
Before:
After:

## Slide 46
FDB Automated Point Out Indicator -Initiating Sector
Sector 88 Situation Display after sector 30 acknowledged SWA505 point out
Sector 30
Sector 88
PO Initiated
SWA505
310 293
125 433
A
DAL2210
350 321
260 407
P
SWA547
330C
122 451
R
PO Acknowledged

## Slide 47
UAL1123
310C
266 450
P
FDB Initiating Sector Pop Up
Radar controller may display a pop up with all sectors receiving the point out
Sector Acknowledged PO
Unacknowledged PO

## Slide 48
ACL Automated Point Out Indicator - Initiating Sector
When a point out is initiated, the initiating sector’s ACL will display a yellow “P” followed by the receiving sector identification inside a box, both in yellow
When the point out is acknowledged by the receiving sector, the “P” and the sector ID will change to white and the box is removed
Acknowledged Point Out
Unacknowledged Point Outs

## Slide 49
ACL Point Out Column
Up to five sectors can be displayed in the point out column
When point outs exceed the set value, an asterisk “✱” will display instead of the “P”
PO Column Header
Asterisk

## Slide 50
FDB Automated Point Out Indicator - Receiving Sector
Sector 30 Situation Display after receiving automated point outs from sector 88
Sector 30
Sector 88
SWA547
330C
122 451
DAL2210
350 321
260 407
P
SWA505
310 293
125 433
P
R
R

## Slide 51
FDB Receiving Sector Pop Up
Radar controller may acknowledge point out(s)
Sector Initiating PO
Acknowledged PO
SWA505
310 293
125 433
P
R

## Slide 52
ACL Automated Point Out Indicator - Receiving Sector
When a point out is received, the ACL will display a cyan “P” followed by the initiating sector identification inside a box, both in cyan
Acknowledged Point Out
Unacknowledged Point Outs

## Slide 53
Acknowledge Point Out Command (QP)
QP A command can be used to acknowledge a point out
  Syntax: QP A <FLID>
Multiple point outs of the same aircraft must be acknowledged individually by adding a specific sector ID to the QP A command
  Syntax: QP A <sector ID> <FLID>

## Slide 54
Knowledge Check
What is the status of the point outs to sectors 02 and 03?
  02 has acknowledged point out and 03 has not
  03 has acknowledged point out and 02 has not
  03 has acknowledged point out and a point out is planned for 02

## Slide 55
Knowledge Check
What does it mean when an asterisk is displayed in the point out column?
  There are no point outs
  Automated point out failure
  Point outs exceed the set value of the column

## Slide 56
Knowledge Check
Will acknowledging a point out remove the pointed out FDB from the Situation Display?
  Yes
  No

## Slide 57
Knowledge Check
Which is a command to point out an FDB to multiple sectors?
  QP 30 T21 15 978
  QP 978 30 T21 15
  QP 30 978 T21 15

## Slide 58
Part-Task Exercise
Purpose
  Perform Radar Handoff and Point Out tasks as follows:
    Managing FDB Fourth Line Data
    Handoff Procedures
    Handoff and Point Out Command Entries
Materials
  TTL part-task exercise: Radar Handoff and Point Out
Directions
  This exercise takes approximately 30 minutes to complete. Each student must complete the checklist tasks. No headsets are required.

## Slide 59: Lesson Summary
This lesson covered:
  Terminology for transferring radar identification
  Handoff and point out methods
  Handoff procedures
  Handoff command entry
  Point out procedures
  Point out command entry

## Slide 60
The End