## Slide 1: En Route - Radar Associate Controller Training Part C: Advanced Concepts
Lesson 13: Radar Separation and Safety Alerts
Course - 55054003
Version - 1.0 2022.08

## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify:
Requirements for radar separation
Radar separation minima
Requirements for safety alerts

## Slide 3: Requirements for Radar Separation
Radar separation may be applied between:
  Radar-identified aircraft
  An aircraft taking off and another radar-identified aircraft
  A radar identified aircraft and one not radar-identified
  A radar identified aircraft and one not radar-identified that is in transit from oceanic airspace or non-radar offshore airspace

## Slide 4: Requirements for Radar Separation (Cont’d)
Target separation
  Apply radar separation:
    Between the centers of primary radar targets
    Between the ends of beacon control slashes
    Between the end of a beacon control slash and the center of a primary target
    For all digital displays, between the centers of digital targets

## Slide 5: Requirements for Radar Separation (Cont’d)
Radar separation must be applied to all RNAV aircraft operating at and below FL450 on Q routes or random RNAV routes, excluding oceanic airspace

## Slide 6
Radar separation must be applied to all aircraft that are _______.
  operating on Q routes at and below FL450
  departing a tower controlled airport
  operating in RVSM airspace below FL410

## Slide 7: ERAM Radar Separation Minima
10 Miles
FL600
5 Miles

## Slide 8: Radar Separation Minima From Adjacent Airspace
Adjacent radar controlled airspace
2 ½ miles
SWA28
140
533 510
KDAL

## Slide 9: Radar Separation Minima From Obstructions
5 miles

## Slide 10: Radar Separation Minima From Adjacent Airspace
5 miles
Aircraft at FL200 tracked off edge of Situation Display
SWA28
140
533 510
KDAL

## Slide 11
What is the approved separation minima between aircraft transitioning from approach control to center airspace, when covered by a letter of agreement?
  2 miles increasing to 3
  3 miles increasing to 5
  5 miles increasing to 7

## Slide 12: Report Passing
Vertical separation between aircraft on opposite courses may be discontinued when:
  You are in communications with both aircraft
  You tell the pilot of one aircraft about the other
  One pilot reports seeing the other aircraft and reports passing that aircraft
  Targets passing observed on radar
  Pilots advised if either aircraft is a super or heavy

## Slide 13
What is the appropriate number of miles of separation from adjacent airspace below FL600?
  2 ½
  3 ¼
  5 ¾

## Slide 14: Safety Alerts
Issue a safety alert to an aircraft if you are aware the aircraft is in a position or altitude that, in your judgment, places it in unsafe proximity to terrain, obstructions, or other aircraft
Duty Priority
  Give first priority to separating aircraft and issuing safety alerts

## Slide 15: Conflict Alert
Aircraft in close proximity or predicted to be in close proximity

## Slide 16: Group Suppression
Group ID
Subscribed Sectors
Flights of Group 03
GROUP SUP View
Sector 21

## Slide 17: En-Route Minimum Safe Altitude Warning (E-MSAW)

## Slide 18: Traffic Alert and Collision Avoidance System (TCAS)
Airborne collision avoidance system based on radar beacon signals, which operates independent of ground based equipment
  TCAS-I generates traffic advisories only
  TCAS-II generates traffic advisories and resolution advisories, but only in the vertical plane

## Slide 19
When must E-MSAW processing be enabled for Mode C equipped VFR aircraft?
  At all times regardless of aircraft altitude
  When the aircraft is experiencing an emergency
  Only when instructed by the supervisor/CIC

## Slide 20: Part-Task Exercise
Purpose:
  The student will perform tasks related to radar separation and safety alerts
Materials:
  TTL part-task exercise: Radar Separation and Safety Alerts
Directions
  This exercise takes approximately 30 minutes to complete. Each student must complete the checklist tasks. No headsets are required.

## Slide 21: Lesson Summary
This lesson covered:
Requirements for radar separation
Radar separation minima
Requirements for safety alerts

## Slide 22: The End