## Slide 2
Vectoring
Speed adjustment
Scanning

## Slide 3: Vectoring

## Slide 4: Methods of Vectoring
110
…TURN RIGHT, HEADING ONE ONE ZERO…
20º
…TURN TWENTY DEGREES RIGHT…

## Slide 5: Knowledge Check
What is a standard rate turn?
  2 degrees per second
  3 degrees per second
  5 degrees per second

## Slide 6: Knowledge Check
What information should be included when issuing a vector?
  Purpose
  Duration of the vector
  Altimeter

## Slide 7: Knowledge Check
Can you vector for noise abatement?
  Yes
  No

## Slide 8: Excessive Speed Adjustments
“AMERICAN SIXTY-ONE, REDUCE SPEED TO THREE ZERO ZERO”
“AMERICAN SIXTY-ONE, INCREASE SPEED TO THREE TWO ZERO”
“AMERICAN SIXTY-ONE, REDUCE SPEED TO TWO EIGHT ZERO”
“I wish Center would make up its mind”

## Slide 9: Techniques
“FEDEX FIFTY, INCREASE SPEED TO THREE ZERO ZERO”
“AMERICAN TWELVE, MAINTAIN THREE ZERO ZERO KNOTS”
“DELTA TEN, DO NOT EXCEED THREE ZERO ZERO KNOTS”

## Slide 10: Assignment Restrictions
ARTCC
“FEDEX SEVEN-TWELVE, REDUCE SPEED TO MACH POINT SEVEN NINER, IF UNABLE ADVISE”
FL390

## Slide 11: Issuing Speed Adjustments - Terms
Knots
  Based on indicated airspeed (IAS)
  Expressed in increments of 5
Mach numbers
  May be be used at or above FL240
  For turbojet aircraft with Mach meters
  Expressed in increments of .01

## Slide 12: Knowledge Check
Speed adjustments are based on what value?
  True airspeed
  Ground speed
  Indicated airspeed

## Slide 13: Knowledge Check
What increments, in knots, are speed adjustments expressed?
  5
  10
  15

## Slide 14: Knowledge Check
What is the range in knots (+/-) that pilots must maintain when complying with speed adjustments?
  5
  10
  25

## Slide 15: Airspeed and Mach

## Slide 16: Definitions
Airspeed
Indicated Airspeed (IAS)
True Airspeed (TAS)
Mach Number
Ground Speed (GS)

## Slide 17: Mach 1.0 = Speed of Sound
Mach is the speed an aircraft moves in relation to the speed of sound
  The speed of sound is M1.0
    Aircraft traveling at 80% of the speed of sound are maintaining M.80
    Aircraft traveling at 75% of the speed of sound are maintaining M.75

## Slide 18: Using Mach “Higher” is “Slower”
M.84 @ FL390 = 483 TAS
M.84 @ FL290 = 500 TAS
M.84 @ FL370 = 483 TAS

## Slide 19: Mach Speeds at Same Altitude
FL340
M.76
FL340
M.78
2 (.01 Mach) x 6 TAS = 12 TAS
12 TAS
6 TAS is equivalent to .01 of Mach

## Slide 20: Mach Speeds at Different Altitudes
FL290
M.82
FL330
M.82
12 TAS
2 x 6 TAS = 12 TAS
ACFT at FL290 is 12 TAS Faster
4,000’
4,000’ = 2 (2,000’ units)
6 TAS Difference per 2,000'

## Slide 21: At or Above FL240
Indicated Airspeed
Mach Number
Mach Limit
“Barber Pole”

## Slide 22: Knowledge Check
What does M.80 mean?
  Minimum speed of 80 knots
  Aircraft speed is 8 times the speed of sound
  Aircraft speed is 80% the speed of sound

## Slide 23: Knowledge Check
At or above FL360 at a given Mach number, what happens to TAS?
  Remains the same
  Increases
  Decreases

## Slide 24: Knowledge Check
Mach numbers are adjusted in increments of ___.
  M.01
  M.10
  M1.0

## Slide 25: Knowledge Check
Given a no wind situation, if an aircraft at FL350 is maintaining M.79, what Mach number would be assigned to an aircraft at FL330 to maintain the same TAS?
  M.78
  M.79
  M.81

## Slide 26: What is Indicated Airspeed?
Indicated Airspeed

## Slide 27: Relationship of IAS to TAS
Altitude | Knots IAS | Approximate Knots TAS
FL300 | 10 | 16
FL250 | 10 | 15
FL200 | 10 | 14
15,000’ | 10 | 13
10,000’ | 10 | 12
5,000’ | 10 | 11
1,000’ | 10 | 10
0’ | 10 | 10
With constant indicated airspeed, true airspeed increases about 2% per 1,000' of increase in altitude

## Slide 28: 5 - 7 Knots TAS for Every 1,000'
If both aircraft are assigned 250 IAS, the aircraft at FL240 will be 24 TAS faster.
FL240
FL200
24,000’ - 20,000’ = 4,000'
6 TAS for Every 1,000'
6 KTS x 4 = 24 TAS

## Slide 29: Knowledge Check
If aircraft at FL190 and 15,000’ are assigned 250 IAS, which will have a faster TAS?
  Both aircraft will have similar TAS
  Aircraft at 15,000’
  Aircraft at FL190

## Slide 30: Knowledge Check
What happens to the TAS of an aircraft that descends at a constant IAS?
  Increases
  Decreases
  Remains the same

## Slide 31: Minima Below 10,000'

## Slide 32: Speed Adjustment Minima
FL280
10,000’
Not Less Than
250 Knots
Turbojets
Reciprocating
Turboprops
20 Flying Miles
FL280
10,000’
Not Less Than 210 Knots
Not Less Than 200 Knots
Not Less Than 170 Knots
Not Less Than 150 Knots
20 Flying Miles

## Slide 33: Speed Minima, Departures
Departing: | Not Less Than:
Turbojet aircraft | 230 Knots
Reciprocating and turboprop aircraft | 150 Knots
Helicopter | 60 Knots
Not Less Than
230 Knots
Not Less Than
150 Knots
Not Less Than
60 Knots

## Slide 34: Knowledge Check
What is the minimum speed, in knots, that may be assigned to a departing turbojet aircraft?
  210
  230
  250

## Slide 35: Knowledge Check
What is the minimum speed, in knots, that may be assigned to an aircraft between 10,000' and FL280?
  200
  230
  250

## Slide 36: Knowledge Check
Can you assign an aircraft 270 knots below 10,000’?
  Yes
  No

## Slide 37: Speed Phraseology
Speed | Phraseology Example
250 Knots | “TWO FIVE ZERO KNOTS”
180 Knots | “ONE EIGHT ZERO KNOTS”
150 Knots | “ONE FIVE ZERO KNOTS”
Mach | Phraseology Example
1.5 | “MACH ONE POINT FIVE”
0.64 | “MACH POINT SIX FOUR”
0.82 | “MACH POINT EIGHT TWO”

## Slide 38: Maintain a Specified Speed
UAL45
110C
313OTUL
KTUL
R
AAL326
110C
321HTUL
KTUL
AAL12
110 130
324 390
KTUL
N626GA
110 130
421 390
KTUL
N626GA
110 130
421 390
S250
“NOVEMBER SIX GOLF ALPHA, MAINTAIN TWO FIVE ZERO KNOTS”

## Slide 39: Increase/Reduce Speed
“AMERICAN THIRTY-SIX, INCREASE SPEED TO THREE ONE ZERO”
“DELTA TWO SIXTY-THREE, REDUCE SPEED TO TWO SIX ZERO”
DAL263
230C
007 426
KMSP
87.6
UAL437
230T230
003 426
KORD
129.4
AAL36
210 102
009 390
KMSP
A 79.8

## Slide 40: Published Speed Restrictions
Example 1: Aircraft is inbound to MOXEE and has been cleared to descend pilot’s discretion to FL240. Because there are underlying speed restrictions on the route, the aircraft must comply with the published speed restrictions.
Example 2: Aircraft is inbound to MOXEE and has been cleared to descend via the TMBRS STAR. Aircraft must comply with published speed and altitude restrictions.

## Slide 41: 4th Line Data

## Slide 42: 4th Line Speed Value Formats
Formats | 
ddd | Mdd
ddd+ | Mdd+
ddd- | Mdd-
+d(d) | M.dd
-d(d) | .dd
dd | .dd+
dd+ | .dd-
dd- | Sddd
+ | -
PS | 
GIM-S accepted speed formats: | 
⎳(d)dd | ⎳Mdd

## Slide 43: Knowledge Check
What is the phraseology to reduce the speed of an aircraft to 250 knots?
  REDUCE SPEED TO TWO FIVE ZERO
  REDUCE TO TWO FIVE ZERO KNOTS
  SLOW TO TWO FIVE ZERO KNOTS

## Slide 44: Knowledge Check
What is the phraseology to instruct an aircraft to increase speed from 200 knots to 230 knots?
  ADJUST INDICATED AIRSPEED TO TWO THREE ZERO KNOTS
  INCREASE TO TWO THREE ZERO KNOTS
  INCREASE SPEED TO TWO THREE ZERO

## Slide 45: Activity: Airspeed Flowchart Review
Purpose
  Review Airspeed Flowchart
Materials
  Airspeed Flowchart
Directions
  Steps to use the flowchart on the next page:
    Begin at the top START oval, follow the paths
    Answer questions in decision boxes (diamonds)
    Note the answer in the last step of the chart (oval)

## Slide 46: Activity: Airspeed Flowchart Review (Cont’d)
Answer:
  True airspeed and ground speed will decrease
Situation #4
  A flight at FL220 is descending with an assigned IAS restriction
Answer:
  True airspeed and ground speed will increase
Situation #3
  A flight at 15,000’ is climbing with an assigned IAS restriction
Answer:
  No change in true airspeed and ground speed
Situation #2
  A flight at FL370 is climbing with an assigned Mach number speed restriction
Answer:
  True airspeed and ground speed will increase
Situation #1
  A flight at FL290 is descending with an assigned Mach number speed restriction
  Helps you understand the relationship between true airspeed, IAS and Mach speed, as aircraft change altitude

## Slide 47: Scanning

## Slide 48: Sector Team Responsibilities

## Slide 49: RA Position Responsibilities
Monitor and operate radios
Ensure
Separation
Monitor Radios
Ensure Situation Display accurately reflects the SAAs
Initiate Control Instructions and Clearances
Ensure Computer Entries and Strip Marking are Complete
Coordinate Other Sectors
Process Flight
Strips
Manage Flows
Initiate Direct Control Actions
Accept and Initiate
Automated H/Os
Use EDST
Nonautomated H/Os
R Position
RA Position
Operate Interphones
Scan flight progress strips

## Slide 50: Scanning
Color coding gets your attention

## Slide 51: Scanning Data Blocks
Actively scan the Situation Display
  Ensure all FDBs can be seen
    Avoid data block overlap
  Potential conflicts
    Aircraft-to-aircraft
    Aircraft-to-airspace
  Unusual situations
  Weather
  Sector boundaries

## Slide 52
Vectoring
Speed adjustment
Scanning

## Slide 53: The Decision Process
Observe
Project
Act
Start Here
Decide

## Slide 54: Observing Alerts

## Slide 55: Project and Analyze

## Slide 56: Decide if Action is Necessary
EDST alerts are projections
Display the data block on the situation display

## Slide 57: Act - Intervene
Coordinate a new or amended clearance to:
  Eliminate conflicts
  Meet objectives
  Avoid weather

## Slide 58: Necessity of Constant Scanning
Continuous scanning and attention to detail is necessary to prevent:
  Complacency
  Laxness
Do not allow your attention to be diverted by:
  Conversations not related to the job,
  Distractions from facility tours, or
  Other personnel in the area

## Slide 59: Scanning Activity
Purpose
  Scan scenarios of EDST and data blocks to observe various system notifications
Materials
  Practice exercise from Lesson 14 handout
Directions
  Change your position in class as necessary to read the screen
  Exercise will depict five EDST and five situation display examples
    Scan for alerts and any other indications
    Write down what you see

## Slide 60: Scanning
Color coding gets your attention

## Slide 61: Scenario 1
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Time
Scenario 1
Ready?

## Slide 62: Scenario 2
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Time
Scenario 2
Ready?

## Slide 63: Scenario 3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Time
Scenario 3
Ready?

## Slide 64: Scenario 4
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Time
Scenario 4
Ready?

## Slide 65: Scenario 5
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Time
Scenario 5
Ready?

## Slide 66: Scenario 6 Ready?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Scenario 6
UAL624
300C
236 422
KORD
DAL374
190+194
533 510
KEWR
R
N235SL
70C
539K-49
KAVQ
SWA296
330C
045SIDE
KMDW
N1762T
90N
204 CST
KAVP
Time

## Slide 67: Scenario 7 Ready?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Scenario 7
DAL28
240F315
798 445
N198M
30C
130MIFF
N156SB
200C
876O-47
R
SLAM21
350 221X
533 510
MARS71
170N
263FRZN
AAL31
290C
830RDOF
Time

## Slide 68: Scenario 8 Ready?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Scenario 8
N292ED
90-86
045 139
N12605
80A
454 111
AAL45
200 337
821 410
UAL425
290C
8063402
N24350
90 75#
492 111
N1172W
70C
292FAIL
Time

## Slide 69: Scenario 9 Ready?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Scenario 9
N468MT
150C
533 320
N4577
50C
143 105
A
UAL169
280C
376EMRG
SWA1198
170C
165 EFC
JAWS11
310XXXX
533 510
JBU400
350 390
005 550
Time

## Slide 70: Scenario 10 Ready?
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Scenario 10
N7188Q
50C
510DATA
JBU441
260N
031 452
UAL31
260C
806HIJK
NOMAD4380C
251 142
N6040C
30 42
109MSAW
38
N5299D
30C
365MOFF
Time

## Slide 71: The End