## Slide 2
Duty priorities
Procedures and phraseology for implementing air traffic services

## Slide 3: Duty Priorities
Give first priority to:
  Separating aircraft
  Issuing safety alerts
Use good judgement to prioritize other duties and additional services

## Slide 4: Additional Services

## Slide 5: Azimuth in Terms of 12-Hour Clock

## Slide 6: Not Radar Identified, No Mode C
5
“SOUTHWEST FOUR TWENTY-EIGHT, TRAFFIC EIGHT MILES SOUTHWEST OF LEESBURG, WESTBOUND, ALTITUDE UNKNOWN”
“SOUTHWEST FOUR TWENTY-EIGHT, TRAFFIC, NUMEROUS AIRCRAFT VICINITY LEESBURG”
SWA428
90 108
348 221
SWA428
70 102
348 221

## Slide 7: Issuing Vectors
“SOUTHWEST FOUR TWENTY-EIGHT,
TURN LEFT HEADING ONE TWO ZERO,
VECTOR FOR TRAFFIC”
“SOUTHWEST FOUR TWENTY-EIGHT, REQUEST A VECTOR TO CLEAR THE TRAFFIC”
SWA428
90 102
348 221

## Slide 8: Traffic No Longer in Sight
N21X has been issued traffic information on both targets.
1
2
3
“CESSNA TWO ONE X-RAY, TRAFFIC NO FACTOR”
“CESSNA TWO ONE X-RAY, TWELVE O’CLOCK TRAFFIC NO LONGER OBSERVED”
N21X
50C 221 150
N21X
50C 221 150
N21X
50C 221 150
7

## Slide 9: Knowledge Check
Which air traffic duties are given first priority?
  Issuing vectors requested by pilot
  Traffic advisories
  Separating aircraft and issuing safety alerts
8

## Slide 10: Knowledge Check
When issuing traffic to radar identified aircraft, give the position of the traffic in terms of the 12-hour clock or the________.
  major magnetic heading points
  eight cardinal compass points
  relative bearings from the aircraft
9

## Slide 11: Merging Target Procedures
Apply Procedures?
Yes
No
Apply Procedures?
AAL52 @ 9,000’
AAL72 @ 11,000’
UAL71 @ 8,000’
UAL65 @ 10,000’
10

## Slide 12: Merging Target Application
AAL52 @ 9,000
UAL65 @ 10,000
In RVSM airspace with two aircraft vertically separated by 1,000’:
  If either unable to maintain RVSM, vector either aircraft to avoid merging with the target of the other aircraft
If pilot requests, vector aircraft to avoid merging with a target of previously issued traffic
11
UAL72 310C 127 420
AAL12 320C 113 410

## Slide 13: Radar Monitor Holding Aircraft
AAL52 @ 9,000
UAL65 @ 10,000
Provide radar surveillance of holding airspace areas whenever aircraft are holding there
If deviation from protected airspace of the holding pattern is detected, assist pilot in returning to the assigned airspace
An adapted holding pattern airspace may be displayed on the Situation Display
12

## Slide 14: Deviation Advisories
13
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
AAL12 120C 113 250
AAL12

## Slide 15: Knowledge Check
At what altitudes should you apply merging target procedures to all radar identified aircraft?
  At and above 10,000’
  At and below 9,000’
  At and above 19,000’
14

## Slide 16: Hazardous Inflight Weather Advisory
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
“ATTENTION ALL AIRCRAFT. HAZARDOUS WEATHER INFORMATION CONVECTIVE SIGMET 7 CENTRAL FOR THUNDERSTORMS WITHIN SOUTHEAST KANSAS, THE EASTERN HALF OF OKLAHOMA, SOUTHWEST MISSOURI, AND NORTHWEST ARKANSAS AVAILABLE ON FLIGHT SERVICE FREQUENCIES.”
15

## Slide 17: Weather Observations
METAR KOKC 011955Z AUTO 22015G25KT 180V250 3/4SM R17L/2600FT +TSRA BR OVC010CB 18/16 A2992 RMK AO2 TSB25 TS OHD MOV E SLP132
16

## Slide 18: METAR Report Fields
METAR KOKC 011955Z AUTO 22015G25KT 180V250
3/4SM R17L/2600FT +TSRA BR OVC010 18/16
A2992 RMK AO2 TSB25 TS OHD MOV E SLP132
Type of Report
Station
Identifier
Date and Time of Report
Report
Modifier
Wind
Visibility
Runway Visual Range
Present
Weather
Sky
Condition
Temperature
and Dew
Point
Altimeter
Remarks
17

## Slide 19: Soliciting Pilot Reports (PIREPs)
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
18

## Slide 20: Soliciting PIREPs - Phraseology
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
“DENVER CENTER, AMERICAN TWENTY-TWO REPORTING ON TOP AT FL280 CLEAR ABOVE”
“AMERICAN TWENTY-TWO, REQUEST FLIGHT CONDITIONS”
19

## Slide 21: PIREP Fields
UA /OV APE230010/TM 1516/FL085/TP BE20
/SK BKN040-TOP065/WX FV03SM BR/TA M02
/WV 23008KT/TB LGT/IC TRACE RIME/RM TCU W
Message Type
Air Temperature
Time
Flight Level
(Altitude)
Aircraft
Type
Sky Condition
Flight Visibility and Weather
Location
Wind
Turbulence
Icing
Remarks
20

## Slide 22: Knowledge Check
Which METAR entry indicates 15 knot winds from the direction of 220 degrees gusting to 35 knots?
  22015G35KT
  04015G35KT
  15G35KT220
21

## Slide 23: Knowledge Check
What items would require PIREP solicitation?
Ceilings at or below 5,000’ (include cloud base/tops reports)
Visibility (surface and aloft) at or less than 5 miles
Thunderstorms and related phenomena
Turbulence (moderate or greater)
Icing (light or greater)
Wind shear
Braking action reports
Volcanic ash clouds
Detection of sulfur gases in the cabin, associated with volcanic activity
22

## Slide 24: Knowledge Check
Which PIREPs are forwarded for dissemination?
  Mountain wave
  Negative icing
  All
23

## Slide 25: Knowledge Check
What is the phraseology to obtain a PIREP?
  “SAY FLIGHT CONDITIONS”
  “REQUEST PIREPS”
  “PROVIDE FLIGHT CONDITIONS”
24

## Slide 26: Weather and Chaff Services
25
NEXRAD
Air Route Surveillance Radar (ARSR)
DAL552
370C
221K448
AAL543
370C
334K442
MODERATE
HEAVY
EXTREME

## Slide 27: Precipitation
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
“MOONEY FOUR NINER TANGO, ROGER, REQUEST TO DEVIATE SOUTH AROUND THE WEATHER”
“MOONEY FOUR NINER TANGO, THREE ZERO MILE AREA OF MODERATE PRECIPITATION FROM ONE ZERO MILES SOUTHWEST OF TULSA TO TWO ZERO MILES NORTHEAST OF TULSA”
26

## Slide 28: Weather Deviations
UAL71 @ 6,000
UAL65 @ 10,000
“SOUTHWEST FIVE TWELVE, DEVIATION THIRTY DEGREES LEFT APPROVED, WHEN ABLE FLY HEADING ZERO NINER ZERO, VECTOR TO JOIN JAY TWO THIRTY-FOUR AND ADVISE”
SWA512
310C 426 450
27

## Slide 29: Forwarding Weather Information
28
“DENVER CENTER, SOUTHWEST FIVE TWELVE, DEVIATING NORTH, PILOT REQUESTED”

## Slide 30: Fourth Line Data Transfer
29
UAL45
310C
024 470
D20R/F
SWA427
330C
425 400
D20R

## Slide 31: Bird Activity Information
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
“DELTA TWENTY-THREE, FLOCK OF GEESE, ONE O’CLOCK, SEVEN MILES, NORTHBOUND, LAST REPORTED AT FOUR THOUSAND”
30

## Slide 32: Fuel Dumping Separation
AAL52 @ 9,000
AAL72 @ 11,000
UAL71 @ 6,000
UAL65 @ 10,000
Vertical
Lateral
2000’
5 Miles
5 Miles
1000’
31

## Slide 33: Fuel Dumping Advisories
AAL52 @ 9,000
UAL65 @ 10,000
32

## Slide 34: Minimum Fuel
AAL52 @ 9,000
UAL71 @ 6,000
UAL65 @ 10,000
Fuel supply has reached a state where undue delays cannot be accepted
This is not an emergency situation, but an advisory that an emergency is possible
Inform any facility to whom control of the aircraft is transferred
Be alert for en route delays
33

## Slide 35: Inflight Equipment Malfunction
AAL52 @ 9,000
UAL71 @ 6,000
UAL65 @ 10,000
Determine the nature and extent of any special handling desired by the pilot
Provide the maximum assistance possible
Relay details to subsequent controllers or facilities as necessary
34

## Slide 36: Knowledge Check
When should you approve weather deviations?
  When requested by the pilot
  When there is thunderstorm activity forecast along an aircraft’s route
  When your facility authorizes it
35

## Slide 37: Knowledge Check
Issue information on bird activity that has been observed on radar, provided that the_______.
  direction and altitude are known
  activity has been pilot verified
  bird movement has been followed on radar for at least 15 minutes
36

## Slide 38: Lesson Summary
This lesson covered:
Duty priorities
Procedures and phraseology for implementing air traffic services
37

## Slide 39: The End