## Slide 2: Lesson Objectives
At the end of this lesson, you will be able to identify characteristics of:
Advanced Session Management
Session Start and Termination
Advanced Eligibility Management
Manual Frequency Uplink
Confirm Assigned Altitude (CAA) Uplink
1

## Slide 3: Session Initiation
Session initiation requires three steps:
  Pilot Logon
  Logon to flight plan correlation
  Session initiation (Connection request and acceptance)
2

## Slide 4: Aircraft Logon
Pilot must logon to the ground system
ATC LOGON/STATUS
LOGON TO
SEND>
--------------------
K
<ATC INDEX
LOGON STATUS
ACTIVE CTR
NEXT CTR
DATA LINK
U
S
A
FLIGHT NUMBER
D
A
L
4
3
2
TAIL NUMBER
2
N
2
3
7
ACCEPTED
3

## Slide 5: Logon / Flight Plan Correlation
Logon Information
Flight Plan Information
Aircraft ID (call sign)
Aircraft Registration (Tail Number)
Departure Airport
Aircraft ID (call sign)
Aircraft Registration (Tail Number)
Departure Airport
Equipment code is J4
ICAO Field 18 /DAT Code includes FANSE or FANSER
4

## Slide 6: Automatic Session Initiation
CPDLC NAP
Connection Request
Connection Accept
5

## Slide 7: Logical Data Authority (LDA)
CPDLC NAP
6

## Slide 8: CPDLC Flight Plan Readout
FR DAL123 D
QF D DAL123
1423 DAL123
1344 CORRELATION FAILED
1344 NO MATCHING LOGON
NO SESSION
1423 DAL123
NOT CORRELATED
VDL MODE2/DAT MISSING
NO SESSION
1423 DAL123
NOT CORRELATED
NO MATCHING LOGON
NO SESSION
7
FP Readout Commands
Readouts

## Slide 9: CPDLC Flight Plan Readout (Cont’d)
1423 DAL123
1344 CORRELATED
1401 ZKC(21) SESSION
1423 DAL123
1344 CORRELATED
1401 KUSA SESSION
1423 DAL123
1344 CORRELATED
NO SESSION
1423 DAL123
1344 CORRELATED
TDLS SESSION
1423 DAL123
1344 CORRELATED
NDA SESSION
1423 DAL123
1344 CORRELATED
1401 ZID SESSION
1423 DAL123
1344 CORRELATED
SESSION TERMINATED: PILOT TERMINATED
8

## Slide 10
Knowledge Check
What is the purpose of correlating logon to flight plan information?
  Ensure the aircraft is logged on to the correct system
  Ensure the correct aircraft is associated with the correct flight plan
  Ensure that the aircraft is evaluated for correct preferential routes
9

## Slide 11
Knowledge Check
What is the keyboard input for requesting a CPDLC flight plan readout?
  <FLID> FR D
  FR D <FLID>
  FR <FLID> D
10

## Slide 12
Knowledge Check
What does the third line of this readout mean?
  NDA session established, ZDC is the NDA, and sector 37 assigned eligibility at 1401
  CDA session established, ZDC is the LDA, and sector 37 assigned eligibility at 1401
  NDA session established at 1401, ZDC is the next LDA, and sector 37 planned eligible sector
1423 DAL343
1344 CORRELATED
1401 ZDC(37) SESSION
11

## Slide 13: Manually Start a Session
SD N140VT
Syntax: SD <FLID>
12

## Slide 14: Session Termination - Normal
No CDA Session Indicator
SWA427
170C 225 400
225 SWA427 B738/L 170 6545
13

## Slide 15: Session Termination - Failed
332 UAL612 A320/L 310 5223
UAL612
310C
332 400
Failed Session Indicator
14

## Slide 16: Acknowledge Failed Session
N234RA
X
ACK FAILED SESS
DRCT RDU FAIL
SESSION TERM:
PILOT TERMINATED
Required actions:
  Establish voice communications with the aircraft and resolve any open uplinks
  Acknowledge the failed session
1. TBP or TBE
2. TBP or TBE
332 N234RA BE40/L 310 5223
15

## Slide 17: Manually Terminate a Session
ED DAL334
Syntax: ED <FLID>
16

## Slide 18
Knowledge Check
What is the command to manually start a session?
  SD <FLID>
  ST <FLID>
  SC <FLID>
17

## Slide 19: Knowledge Check
What is not a reason for the red X (session failed)?
  Session has been terminated by a pilot
  Session has been manually terminated at an ATSW
  Session has terminated by entry into TRACON airspace
SWA748
310C
246 482
18

## Slide 20: Knowledge Check
Which is not a controller entered amendment that will result in an automatic failed session?
  Amend assigned altitude to VFR
  Amend remarks to contain Emergency
  Amend the Field 18 DAT/ <code>
19

## Slide 21: Knowledge Check
What is the command to manually end a session?
  ED <FLID>
  EN <FLID>
  ES <FLID>
20

## Slide 22: Advanced Eligibility Management
Eligibility is typically assigned automatically
NOTE: The system ensures that only one sector at a time can communicate with a given aircraft via CPDLC. That sector is said to have eligibility.
Two manual eligibility management options
  Release eligibility
  Steal eligibility
21

## Slide 23: Eligibility Assignment Concepts
CPDLC NAP
Track Control
Logical Data Authority (LDA)
Eligibility
ARTCC
Sector
22

## Slide 24: Eligibility Release Processing
Eligibility Reassignment to:
  Sector with track control, if there is one
  Active NAP, if no sector has track control
  Active NAP, if the only sector with track control is the sector that released eligibility
23

## Slide 25: Eligibility Release Acceptance
Eligibility release will be accepted if all the following conditions are met:
  Session exists for the flight
  Requesting sector has eligibility
  No unacknowledged abnormal uplinks for the flight
  No controller initiated open CPDLC uplink messages for the flight
  Session termination is not in progress for the current session
  No unacknowledged emergency PIDs
24

## Slide 26: Release Eligibility
Manual Options
Release Eligibility command: RE <FLID>
Mark aircraft off-frequency
Drop FDB (QN)
Drop Track (QX)
Automatic Conditions
FDB Drop Interval expires
WILCO to a TOC to approach control when flight will re-enter en route airspace
Only sector with eligibility
Only sector with eligibility but not track control
Only sector with eligibility but not track control
Any sector
25

## Slide 27: Steal Eligibility
Options:
Steal Eligibility command
Syntax: SX <FLID>
Steal Eligibility menu
16 UAL612
X
STEAL ELIGIBILITY
332 UAL612(16) A320/L 310 2702
26

## Slide 28: Knowledge Check
Which command will release eligibility?
  Track (QT)
  Suppress Group (SG)
  Drop Track (QX)
27

## Slide 29: Knowledge Check
In addition to Drop Track (QX), what other keyboard input can a controller at a sector with eligibility and track control use to release eligibility?
  RE <FLID>
  DE <FLID>
  QT //<FIX> <FLID>
28

## Slide 30: Knowledge Check
Which is not a method for a controller at a sector with eligibility but not track control to release eligibility?
  Mark the aircraft off-frequency
  Handoff the FDB
  Drop the FDB
29

## Slide 31: Knowledge Check
Does an aircraft have to be marked on frequency to steal eligibility?
  Yes
  No
30

## Slide 32: Manual Frequency Uplink
ATC UPLINK
1923Z
1/1
STATUS
OPEN
CONTACT WASHINGTON CTR AT 122.500
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOG>
Manual frequency uplink message is independent of track control change
31

## Slide 33: UF Keyboard Commands
Syntax | Contact Facility | Example(s)
UF <FLID>
Local facility sector entering command
UF 225
UF N123
UF <FacilityPosition> <FLID>
Center identifier and sector number
UF T14 985
UF N1A 674
UF PCT N123
UF ZAK07 565
UF <Facility> <Frequency> <FLID>
Facility specified, if frequency is adapted for it
UF T 126.75 798
UF PCT 131.25 357
UF <Sector> <FLID>
Local sector number
UF 21 346
UF 21 N123
UF <Frequency> <FLID>
Adapted local VHF frequency, if adapted
UF 123.5 532
UF 130.75 212
32

## Slide 34: UF FDB and ACL CHI
Generic Uplink Indicator
SWA427
170C 225 400
225 SWA427 B738/L 170 6545
33

## Slide 35: UF - Radar Services Terminated
UF RT 225
UF RT FLID | 
UF RT <Sector> FLID | UF <Sector> RT FLID
UF RT <FacilityPosition> FLID | UF <FacilityPosition> RT FLID
UF RT <Frequency> FLID | UF <Frequency> RT FLID
UF RT <Facility> <Frequency> FLID | UF <Facility> <Frequency> RT FLID
Syntax:
34

## Slide 36: UF - End Session Command
UF LJA23 ED 225
Syntax:
  UF ED <FacilityPosition> <FLID>
  UF ED <FacilityPosition> <Frequency> <FLID>
  UF <FacilityPosition> ED <FLID>
  UF <FacilityPosition> <Frequency> ED <FLID>
35

## Slide 37: UF - Both Options
UF LJA23 ED RT 225
Syntax:
  UF ED RT <FacilityPosition> FLID
  UF RT ED <FacilityPosition> <Frequency> FLID
  UF <FacilityPosition> ED RT FLID
  UF <FacilityPosition> <Frequency> RT ED FLID
36

## Slide 38: UF with End Session - FDB and ACL
TOC In Progress
225 SWA427 B738/L 170 6545
37

## Slide 39: Knowledge Check
What is the command to uplink the adapted frequency for your facility’s sector 34 to CID 225 independent of a track control change?
  UF 34 225
  UF 225 34
  UF 34/225
38

## Slide 40: Knowledge Check
What is a command to end the CPDLC session, and inform the pilot that radar service is being terminated?
  UF 225 ED RT ZAK07
  UF ZAK07 ED RT 225
  UF ED RT 225 ZAK07
39

## Slide 41: Knowledge Check
Which of these ACL entries would you see after entering the command UF ZAK07 ED RT 225?
225 DAL427 B752/L 330 4371
C.
225 DAL427 B752/L 330 4371
B.
225 DAL427 B752/L 330 4371
A.
40

## Slide 42: Confirm Assigned Altitude (CAA)
ATC UPLINK
1923Z
1/1
STATUS
OPEN
CONFIRM ASSIGNED ALTITUDE
<STANDBY
<UNABLE
WILCO>
-------------------------------
<PRINT
LOG>
41

## Slide 43: Manual CAA Keyboard Command
Syntax: UG /CAA <FLID>
CAA In Progress Indicator
AAL234
350C
123 400
225 AAL234
AAL234
350C
123 400
225 AAL234
CAA In Progress and Generic Uplink Indicators
42

## Slide 44: Knowledge Check
What is the command to manually uplink a CAA message to CID 343?
  UG /CAA 343
  /CAA 343 UG
  UG 344 /CAA
43

## Slide 45: Part-Task Exercise
Purpose
  Perform CPDLC tasks as follows:
    Advanced session and eligibility management
    Uplink a frequency and a Confirm Assigned Altitude (CAA)
Materials
  TTL part-task exercise: CPDLC Operations
Directions
  This exercise takes approximately 45 minutes to complete. Each student must complete the checklist tasks. No headsets are required.
44

## Slide 46: Lesson Summary
This lesson covered:
Advanced Session Management
Session Start and Termination
Advanced Eligibility Management
Manual Frequency Uplink
Confirm Assigned Altitude (CAA) Uplink
45

## Slide 47: The End